## Slide 1
University of Salahaddin College of Science Department of Earth sciences and Petroleum Industrial Geology
Lecture Two
Lecturer: Dr. Ahmed Aqrawi

## Slide 2
Building and Construction Materials:
They are any materials that are used for construction purposes. For example, the naturally occurring substances such as clay, rocks and sand and many industrial substances such as cement, plaster and glass. It comprises a great group of nonmetallic materials for social and industrial developments (building schools, hospitals, health centers, road pavement, residential complexes, dams, and airports etc.). They need finding and locating raw material resources such as those listed in the following table:

## Slide 3
Product | Sources | Desirable properties
Dimension stone and Ornamental stone | limestone, sandstone (hard), granite, marble, tufa (travertine), gypsum | regular bedding and joints, high compressive strength, resistance to weathering, especially in industrial regions
Slate | strongly cleaved fine-grained metamorphic rock | Regular closely-spaced cleavage, resistance to weathering
Road stone | crushed basalt, fine granite, quartzite, flint, industrial waste in combination with bitumen | Resistance to abrasion, fine-to-medium grain size, low porosity, binds well with bitumen
Aggregate: for concrete (cement + sand + gravel), for mortar (cement + sand), for asphaltic concrete or asphalt pavements (sand + gravel + cement or filler + bitumen), for roads (sub-base layer), for building foundations and dams, for water purification filters | sand and gravel (fluvial, glacial, marine), crushed sand and gravel, crushed rock, industrial waste (slag) | Range of particle sizes (grading), low impurities (such as sulphate, sulphide, organic matter, chlorides, mica, fine clay materials)

## Slide 4
Product | Sources | Desirable properties
Bricks and tiles | clays (marine, alluvial, glacial) fired at high temperatures | no excess water (plasticity index), low iron and sulphide, sulphate CaSO4 < 5%, carbonate CaCO3 < 20%), assists firing
Cement | limestone mixed with clay converted to clinker in kiln, and the product is ground to powder and mixed with 4% with gypsum | constant composition (CaO, Al2O3, SiO2, Fe2O3), low Sulphur, MgO, P, alkalies (Na2O and K2O)
Glass | quartz or silica sand, quartzite | suitable grading grains, no impurities (low iron)
Juss, plaster, plaster boards | gypsum, anhydrite | no impurities (low clay and iron)
Insulating materials | fibrous and flaky metamorphic minerals (asbestos), mica, diatomite, vermiculite | not harmful to health
Bitumen | natural residues of oil, residue from distillation of oil | melting temperature for conditions of use (in roads pavement)

## Slide 5
Aggregate: is a mixture of rocks fragments and comprises 3/4 of the volume of concrete (85 - 90% aggregate and 10 - 15% cement) and has specific physical, mechanical, and chemical properties.
Aggregates are classified by their source into:
1. Natural aggregates (sand and gravel): it is extracted from quarries and is formed by disintegration of rocks (igneous, sedimentary and metamorphic) through weathering, erosion, transportation of fragments by (air, water and glacier) and deposition.

## Slide 6
2. Artificial aggregates (slag, crushed stone): it is formed by:
A - By-product (blast furnace slag, fly ash, burned rocks)
B - Thermal process (fired clay, vermiculite)
C - Recycled concrete and municipal wastes
Natural aggregates are classified by particles shape according to British Standard BS 812- 1975 into:
1. Rounded 2. Irregular 3. Flaky 4. Angular 5. Elongated

## Slide 7
They are also classified by surface texture of grains according to BS 812 - 1975 into:
1. Glassy (flint)
2. Smooth (chert)
3. Granular (sandstone)
4. Rough (basalt)
5. Crystalline (granite)
6. Honey combed or Porous (pumice)

## Slide 8
They are also classified by grain size according to Wentworth scale and British Institute of Geological Science into:
1. Grains size > 4mm: called "gravel" (pebbles, cobbles, boulders) and is composed of rock fragments.
2. Grains size 4 - 0.063 mm: called "sand" and is composed mostly of quartz.
3. Grains size < 1/16 or 0.063 mm: known as "fines" consist of silt and clay fractions.

## Slide 9
Composition | IGS (British) | US Industry | Wentworth Scale | Size (mm)
Limestone, Chert | Gravel | Gravel | Cobble | 64
 |  |  | Pebble | 4
Quartz | Sand |  | Gravel | 2
Clay minerals | Silt | Sand | Sand | 0.06 or 1/16
 |  | Silt | Silt, Clay | 

## Slide 10
Geological Forms (Occurrence) of Sand and Gravel Deposits:
1. River deposits (main source in Iraq)
2. Glacial deposits
3. Terrace deposits unconsolidated deposits
4. Continental shelf deposits
5. Aeolian deposits (sand dunes)
6. Beach deposits
7. Lithified (solid deposits) beds or lenses, like that present in Injana Formation (Miocene age).
Pliocene and Pleistocene (Quaternary) deposits cover vast areas of Iraq, underlying Mukdadiya and Bai Hassan Formations (Pliocene).

## Slide 11
Uses of Sand and Gravel:
1. Concrete and mortar
2. Filling and grouting
3. Road pavement and railway road ballast
4. Concrete products (pipes, blocks, tiles, thermostone, kerbstone, and lime-sand brick)
5. Water purification filters and filter aid (sand)
6. Glass, refractory, foundry and ceramic
7. Manufacture of Portland cement

## Slide 12
Evaluation for Concrete:
Using Iraqi standard specifications No.45 for 1984:
1. Sieving and grading
2. Surface texture and shape
3. Deleterious materials and its effects (clays, platy particles, organic materials, salts, pyrite and sulphides, alkali- silica reaction (concrete cancer), opal (finely crystalline), chalcedony (weakly crystalline), volcanic glass (amorphous silica) react with alkalies from cement. Quartz is inert because it is coarse grained.
- Use low alkali cement (<0.6% alkalies), normal ordinary portland cement (O.P.C.) contains <1.5% alkalies.

## Slide 13: Aggregate must be strong and of low water absorption and porosity and resist frost action. - For road pavement, aggregate should be of rough surface and with sharp ends and free from fines (clay) so as to make a good bond with asphalt. Aggregate must also be tested for: Aggregate Impact value (AIV) Aggregate Abrasion value (AAV) Aggregate Crushing value (ACV) Polished stone value (PSV) Soundness Test: immersion in a saturated solution of Na2SO4 and MgSO4 (ASTM 088-99)
Physical and Mechanical properties of Aggregate:

## Slide 14: Lightweight Aggregates LWA
Density <1-1.6 gm/cm3 while normal aggregates are 1.8-2.7 gm/cm3, thermal and sound insulation, resist fire, light weight and easy to move, transport and cut, need less iron for reinforcement (lightweight concrete).
- Used in cooling stores, suspension bridges, multistory buildings .
Classification of Lightweight Aggregates (LWA):
a. Natural LWA( Diatomite, pumice, scoria and tuff, all are of volcanic origin except diatomite).
b. By-product LWA (foamed slag and fly ash, waste product from coal mines and slate quarries).
c. Manufactured LWA: Firing clays, slate and shale ---- bloating and expansion then rapid cooling.

## Slide 15: Lightweight Aggregates LWA:
Density <1-1.6 gm/cm3 while normal aggregates are 1.8-2.7 gm/cm3, thermal and sound insulation, resist fire, light weight and easy to move, transport and cut, need less iron for reinforcement (lightweight concrete).
- Used in cooling stores, suspension bridges, multistory buildings .
Classification of Lightweight Aggregates (LWA):
a. Natural LWA( Diatomite, pumice, scoria and tuff, all are of volcanic origin except diatomite).
b. By-product LWA (foamed slag and fly ash, waste product from coal mines and slate quarries).
c. Manufactured LWA: Firing clays, slate and shale ---- bloating and expansion then rapid cooling

## Slide 16
Building Stones:
Comprise different types of rocks. During history, use of local stones. Pyramids 2800 B.C. built from limestone blocks. Also used in defense sites (castles) and religious buildings (mosques, churches).
- Winged Bull in Nineveh, Nineveh Walls 5000 years B.C. are composed of weathering-resistant rocks.
Trade in ornamental stones.
- Facing with a veneer of natural stone 2 inches (granite, marble, sandstone, limestone, slate).

## Slide 17
Features of building stone:
- Strength: Resistance of rock to compression.
- Durability: Resistance of rock to climate changes (temperature, frost, …etc.)
- Spacing of joints
- Appearance after polish

## Slide 18
Economic features in consideration:
1. Ease of quarrying
2. Thickness of overburden and beds
3. Distance to the quarry
4. Drainage of the quarry
5. Compressive strength∞ ∞
- Igneous rocks, quartzite, some sandstones have high values. Porous sandstone, mudstone, chalk, tuff and shales are weak.

## Slide 19
HIT stone with a steel bar.
- Strength is influenced by texture, interlocking text is stronger with sedimentary rocks the type of cement control the strength, the strongest is siliceous, strength is also influenced by the direction of bedding.
Stone Decay:
- Causes of stone damage: Physical (frost action), chemical (acid rain).
- An increaser in CO2 and SO3 levels in the atmosphere as a result of industrial processes (H2CO3,H2SO4 emission) have serious effects specially on limestone buildings.

## Slide 20
Durability of stone:
Durable stone means long lasting
Soundness test (freezing and thawing)
Temp. variation (day and night, summer and winter), freezing, surface expands more than inner part (differential stresses).
- Cleopatra Needle persisted 3000 years in Egypt but start decaying after 25 years in New York (spalling and exfoliation) as a result of climatic change and industrial pollution.
Pore size distribution:
- movement of water by capillarity through pores, in small pores (fine) water rise rapidly in comparison with large ones.

## Slide 21
Mainly limestone, gypsum and marble.
- Impurities in marble like quartz, chlorite, tremolite, diopside and other silicates plus graphite, hematite and limonite are the causes of various colors in marbles. Pure marble > 99% CaCO3 is white.
- Grey marble contains homogeneously distributed graphite, while red and pink colors are due to hematite distribution. Traces of limonite give yellow and creamy colors. Many marbles contains veins or bands of graphite or silicates giving nice and beautiful textures.
- Marble quarries are present in Erbil and Sulaimaniya in Gallala, Rayat, kalaa Dizah, Chwarta and Khan Khosh.
Building Stones in Iraq:

## Slide 22
Slate (Roofing stone)
High ability to split into thin and parallel planes
Strong and durable .
Resist firing and non combustible .
Various colors (grey, black, red, green, spotted).
Geological and Physical features of rocks to be used as building stones :
Ease of processing and quarrying
Strength
Durability
Environmental effects of quarrying

## Slide 23
Processing:
Used as quarried
After cutting into sizes
After dressing
By calcinig
Crushing and sieving and washing

## Slide 24
Roofing Stone (Slate):
It is chosen for its following properties:
1- High ability to in parallel levels
2- Durability and toughness
3- Fire-resistant and nonflammable
4- Occur in various colors
Q: What processing are carried out on rock before using it as construction material?
A: Cutting, dressing, polishing, and thermal processing. Also it can be used unprocessed.