## Slide 1
Reinforced concrete bridges

## Slide 2
Reinforced concrete Bridges
Bridges shall be designed for specified limit states to achieve the objectives of constructability, safety and serviceability and also taking into account the economy and aesthetics.
The design of reinforced concrete bridges is based on the AASHTO specifications (American Association of State Highway and Transportation Officials). The bridges in general can be classified as follows:
According to the materials of the construction of the super structure: reinforced concrete, steel, pre-stressed concrete, composite, etc.
According to the functions: road over a river, Road or railway over a valley, highway and pipe line bridge.
According to the form of super structure:
Permanent Loads
  DC – Structural Components and Attachments
  DW - Wearing Surfaces and Utilities
  EH - Horizontal Earth Pressure
  EL - Locked-In Force Effects Including Pretension
  ES - Earth Surcharge Load
  EV - Vertical Pressure of Earth Fill
  Transient Loads
  BR – Veh. Braking Force
  CE – Veh. Centrifugal Force
  CR – Creep
  CT - Veh. Collision Force
  CV - Vessel Collision Force
  EQ – Earthquake
  FR - Friction

## Slide 3
  IC - Ice Load
  LL - Veh. Live Load
  IM - Dynamic Load Allowance
  LS - Live Load Surcharge
  PL - Pedestrian Live Load
  SE – Settlement
  SH – Shrinkage
  TG - Temperature Gradient
  TU - Uniform Temperature
  WA - Water Load
  WL - Wind on Live Load
  WS - Wind Load on Structure
Load Factors and Load Combinations (AASHTO 2012, Section 3.4)
3.4.1: Load Factors and Load Combinations
  Strength I: Basic load combination relating to the normal vehicular use of the bridge without wind.
  Strength II: Load combination relating to the use of the bridge by Owner-specified special design vehicles, evaluation permit vehicles, or both, without wind.
  Strength III: Load combination relating to the bridge exposed to wind in excess of 55 mph.
  Strength IV: Load combination relating to very high dead load to live load force effect ratios. (Note: In commentary it indicates that this will govern where the DL/LL >7, spans over 600’, and during construction checks.)
  Strength V: Load combination relating to normal vehicular use with a wind of 55 mph.
  Extreme Event I: Load combination including earthquakes.

## Slide 4
  Extreme Event II: Load combination relating to ice load, collision by vessels and vehicles, and certain hydraulic events with a reduced live load.
  Fatigue: Fatigue and fracture load combination relating to repetitive gravitational vehicular live load and dynamic responses under a single design truck.
  Service I: Load combination relating to normal operational use of the bridge with a 55 mph wind and all loads at nominal values. Compression in precast concrete components.
  Service II: Load combination intended to control yielding of steel structures and slip of slip-critical connections due to vehicular load.
  Service III: Load combination relating only to tension in prestressed concrete superstructures with the objective of crack control.
  Service IV: Load combination relating only to tension in prestressed concrete columns with the objective of crack control.
  An important note about γp: The purpose of γp is to account for the fact that sometimes certain loads work opposite to other loads.
  If the load being considered works in a direction to increase the critical response, the maximum γp is used.
  If the load being considered would decrease the maximum response, the minimum γp is used.
  the minimum value of γp is used when the permanent load would increase stability or load carrying capacity
  sometimes, a permanent load both contributes to and mitigates a critical load effect.
  For example, in the three span continuous bridge shown, DC in the first and third spans would mitigate the positive moment in the middle span. However, it would be incorrect to use a different γp for the two end spans. In this case, γp would be 1.25 for DC for all three spans (Commentary C3.4.1 – paragraph 20).
  Table 3.4.1-1 “Load Combinations and Load Factors” gives two separate values for the load factor for TU (uniform temperature), CR (creep), and SH (shrinkage). The larger value is used for deformations.The smaller value is used for all other effects.

## Slide 5
  TG (temperature gradient), γTG should be determined on a projectspecificbasis. In lieu of project-specific information to the contrary, the following values may be used:
  0.0 for strength and extreme event limit states,
  1.0 for service limit state where live load is NOT considered,
  0.5 for service limit state where live load is considered.
  For SE (settlement), γSE should be based on project specific
  information. In lieu of project specific information, γSE may be taken as 1.0.
  Load combinations which include settlement shall also be applied without settlement.
  The load factor for live load in Extreme Event I, γEQ, shall be determined on a project specific basis. Assume that the Extreme Event I Load Factor for Live Load is Equal to 0.0. (γEQ = 0.0)
  When prestressed components are used in conjunction with steel girders, the following effects shall be considered as construction loads (EL):
  If a deck is prestressed BEFORE being made composite, the friction between the deck and the girders.
  If the deck is prestressed AFTER being made composite, the additional forces induced in the girders and shear connectors.
  Effects of differential creep and shrinkage.
  Poisson effect.
3.4.2: Load Factors for Construction Loads
At the Strength Limit State Under Construction Loads:
  For Strength Load Combinations I, III and V, the factors for DC and DW shall not be less than 1.25.
  For Strength Load Combination I, the load factor for construction loads and any associated dynamic effects shall not be less than 1.5.
  For Strength Load Combination III, the load factor for wind shall not be less than 1.25.

## Slide 6
3.4.3: Load Factors for Jacking and Post-Tensioning Forces
  Jacking Forces
  The design forces for in-service jacking shall be not less than 1.3 times the permanent load reaction at the bearing adjacent to the point of jacking (unless otherwise specified by the Owner).
  The live load reaction must also consider maintenance of traffic if the bridge is not closed during the jacking operation.
  PT Anchorage Zones
  The design force for PT anchorage zones shall be 1.2 times the maximum jacking force.
  Strength I: 1.25DC+ 1.50DW + 1.75(LL+IM)
  Service II: 1.00DC + 1.00DW + 1.30(LL+IM)
  Fatigue: 0.75(LL+IM)
Common Load Combinations for Steel Design
  Strength I: 1.25DC+ 1.50DW + 1.75(LL+IM)
  Strength IV: 1.50DC + 1.50DW
  Service I: 1.00DC+ 1.00DW + 1.00(LL+IM)
  Service III: 1.00DC+ 1.00DW + 0.80(LL+IM)
  Service IV: 1.00DC+ 1.00DW + 1.00WA + 0.70WS + 1.00FR
  Fatigue: 0.75(LL+IM)
Note: Fatigue rarely controls for prestressed concrete
Common Load Combinations for Prestressed Concrete
  Strength I: 1.25DC+ 1.50DW + 1.75(LL+IM)
  Strength IV: 1.50DC+ 1.50DW
  Fatigue: 0.75(LL+IM)
  § 3.4 - Loads and Load Factors

## Slide 7
Common Load Combinations for Reinforced Concrete
  Strength I: 1.25DC+ 1.50DW + 1.75(LL+IM)
  Strength IV: 1.50DC+ 1.50DW
  Fatigue: 0.75(LL+IM)
3.5 – Permanent Loads
3.5.1 Dead Loads: DC, DW, and EV
  DC is the dead load of the structure and components present at construction. These have a lower load factor because they are kNown with more certainty.
  DW are future dead loads, such as future wearing surfaces. These have a higher load factor because they are kNown with less certainty.
  EV is the vertical component of earth fill.
  Table 3.5.1-1 gives unit weight of typical components which may be used to calculate DC, DW and EV.
If a beam slab bridge meets the requirements of Article 4.6.2.2.1, then the permanent loads of and on the deck may be distributed uniformly among the beams and/or stringers.
Article 4.6.2.2.1 basically lays out the conditions under which approximate distribution factors for live load can be used.
3.6 - Live Loads
3.6.1 Gravity loads
3.6.1.1 Vehicular Live Load
3.6.1.1.1: Number of Design Lanes
  # Design Lanes = ( w / 3.60m)
  w is the clear roadway width between barriers.
  Bridges 6.0 to 7.20m wide shall be designed for two traffic lanes, each ½ the roadway width.
  Examples:
  A 6.0m wide bridge would be required to be designed as a two lane bridge with 3.0m. lanes.
  A 11.60m wide bridge has 3 design lanes, each 3.60 wide.
  A 4.88m wide bridge has one design lane of 3.60m.

## Slide 8
3.6.1.1.2 Multiple Presence Factor
Multiple Presence Factors are NOT used with the Distribution Factors
3.6.1.2—Design Vehicular Live Load
3.6.1.2.1—General
Vehicular live loading on the roadways of bridges or incidental structures, designated HL-93, shall consist of a combination of the:
• Design truck or design tandem, and
• Design lane load.
3.6.1.2.2: Design Truck
The weights and spacing’s of axles and wheels for the design truck shall be as specified in Figure 3.6.1.2.2-1. A dynamic load allowance shall be considered as specified in Article 3.6.2. Except as specified in Articles 3.6.1.3.1 and 3.6.1.4.1, the spacing between the two 145kN axles shall be varied between 4.30m and 9.0m to produce extreme force effects. HL-93 or IL-120 Design Truck (Structure Design Manual, ILLINOIS STATE TOLL HIGHWAY, March 2013), Figures attached.
3.6.1.2.3: Design Tandem
The design tandem shall consist of a pair of 110kN axles spaced 1.20m apart. The transverse spacing of wheels shall be taken as 1.80m. A dynamic load allowance shall be considered as specified in Article 3.6.2.
3.6.1.2.4: Design Lane Load
  9.3kN/m is applied SIMULTANEOUSLY with the design truck or design tandem over a width of 3.0m within the design lane.
  NOTE: the impact factor, IM, is NOT applied to the lane load. It is only applied to the truck or tandem load.
  This is a big change from the Standard Specifications…

## Slide 9
3.6.1.2.5—Tire Contact Area
The tire contact area of a wheel consisting of one or two tires shall be assumed to be a single rectangle, whose width is 510mm. and whose length is 250mm The tire pressure shall be assumed to be uniformly distributed over the contact area.
3.6.1.3: Application of Design Vehicular Live Loads
  In cases where the transverse position of the load must be considered:
  The design lanes are positioned to produce the extreme force effect.
  The design lane load is considered to be 3.0m wide. The load is positioned to maximize the extreme force effect.
  The truck/tandem is positioned such that the center of any wheel load is not closer than:
  300mm from the face of the curb/railing for design of the deck overhang.
  600mm from the edge of the design lane for design of all other components.
Both the Design Lanes and 3.0m Loaded Width in each lane shall be positioned to produce extreme force effects.
  Center of truck wheels must be at least 600mm from the edge of a design lane
  The lane load may be at the edge of a design lane.
3.6.1.3.1: General
  The governing force effect shall be taken as the larger of the following:
  The effect of the design tandem combined with the design lane load
  The effect of one design truck (HL-93) combined with the effect of the design lane load
  For negative moment between inflection points, 90% of the effect of two design trucks (HL-93 with
  4.30m axle spacing) spaced at a minimum of 15.00m combined with 90% of the design lane load.

## Slide 10
3.6.1.3.3: Design Loads for Decks, Deck Systems, and the Top Slabs of Box Culverts
When the Approximate Strip Method is Used:
  Where the slab spans primarily in the transverse direction:
  only the axles of the design truck or design tandem of shall be applied to the deck slab or the top
  slab of box culverts.
  Where the slab spans primarily in the longitudinal direction:
  For top slabs of box culverts of all spans and for all other cases (including slab-type bridges where the
  span does not exceed 4.60m only the axle loads of the design truck or design tandem shall be applied.
  For all other cases (including slab-type bridges where the span exceeds 4.60m) the entire HL-93
  loading shall be applied.
When Refined Methods of Analysis are Used:
  Where the slab spans primarily in the transverse direction
  only the axles of the design truck or design tandem shall be applied to the deck slab.
  Where the slab spans primarily in the longitudinal direction (including slab-type bridges)
  the entire HL-93 loading shall be applied.
Centrifugal and Braking Forces need not be considered for deck design.
3.6.1.3.4: Deck Overhang Load
For design of a deck overhang with a cantilever < 1.80m measured from the centerline of the exterior girder to the face of a structurally continuous concrete railing… …the outside row of wheel loads may be replaced by a 14.6kN/m line load located 300mm from the face of the railing.

## Slide 11
New LRFD Loading:
  HL-93 Truck and Lane Load, or
  Tandem and Lane Load, or
  90% of 2 Trucks and Lane Load
  The lane load is applied, without impact, to any span, or part of a span, as needed to maximize the critical response.
  A single truck, with impact, is applied as needed to maximize the critical response (except for the case of negative moment between inflection points).
  The Specification calls for a single truck to be applied, regardless of the number of spans.
  The exception is for the case of negative moment between inflection points where 2 trucks are used.
  If an axle or axles do not contribute to the critical response, they are ignored.
  Although a truck in the third span would contribute to maximum response, by specification only one truck is used.
Live Loads for Maximum Positive Moment in Span 1
  Impact is applied only to the truck.
  In this case, the front axle is ignored as it does not contribute to the maximum
  response. Ignore this axle for this case
Live Loads for Shear at Middle of Span 1
  The distance between rear axles is fixed at 4.30m
  The distance between trucks is a minimum of 15.00m.
  This applies for negative moment between points of contra flexure and reactions at interior piers
Live Loads for Maximum Moment Over Pier 1
Use only 90% of the effects of the trucks and lane load

## Slide 12
3.6.1.4—Fatigue Load
3.6.1.4.1—Magnitude and Configuration
The fatigue load shall be one design truck or axles thereof specified in Article 3.6.1.2.2, but with a constant spacing of 9.0m between the 145kN axles. The dynamic load allowance specified in Article 3.6.2 shall be applied to the fatigue load. For the design of orthotropic decks and wearing surfaces on orthotropic decks, the loading pattern as shown in Figure 3.6.1.4.1-1 shall be used.
3.6.1.4.2—Frequency
The frequency of the fatigue load shall be taken as the single-lane average daily truck traffic (ADTTSL). This frequency shall be applied to all components of the bridge, even to those located under lanes that carry a lesser number of trucks. In the absence of better information, the single-lane average daily truck traffic shall be taken as:
ADTTSL = p× ADTT (3.6.1.4.2-1)
Where:
ADTT = the number of trucks per day in one direction averaged over the design life
ADTTSL = the number of trucks per day in a single-lane averaged over the design life
p = fraction of traffic in a single lane, taken as specified in Table 3.6.1.4.2-1
3.6.1.4.3—Load Distribution for Fatigue
3.6.1.4.3a—Refined Methods
Where the bridge is analyzed by any refined method, as specified in Article 4.6.3, a single design truck shall be positioned transversely and longitudinally to maximize stress range at the detail under consideration, regardless of the position of traffic or design lanes on the deck.
3.6.1.4.3b—Approximate Methods
Where the bridge is analyzed by approximate load distribution, as specified in Article 4.6.2, the distribution factor for one traffic lane shall be used.

## Slide 13
3.6.1.6: Pedestrian Loads
A pedestrian load of 3.60kN/m2 shall be applied to all sidewalks wider than 600mm and considered simultaneously with the vehicular design live load in the vehicle lane. Where Vehicles can mount the sidewalk, sidewalk pedestrian load shall not be considered concurrently. If a sidewalk may be removed in the future, the vehicular live loads shall be applied at 300mm from edge-of-deck for design of the overhang, and 600mm from edge-of-deck for design of all other components. The pedestrian load shall not be considered to act concurrently with vehicles. The dynamic load allowance need not be considered for vehicles. Bridges intended for only pedestrian, equestrian, light maintenance vehicle, and/or bicycle traffic should be designed in accordance with AASHTO’s LRFD Guide Specifications for the Design of Pedestrian Bridges.
3.6.2 Dynamic Load Allowance
3.6.2.1 General
Unless otherwise permitted in Articles 3.6.2.2 and 3.6.2.3, the static effects of the design truck or tandem, other than centrifugal and braking forces, shall be increased by the percentage specified in Table 3.6.2.1-1 for dynamic load allowance. The factor to be applied to the static load shall be taken as: (1 + IM/100). The dynamic load allowance shall not be applied to pedestrian loads or to the design lane load.
  The Dynamic Load Allowance is applied only to the truck load (including fatigue trucks), not to lane loads or pedestrian loads.
3.6.2.2: Buried Components
The dynamic load allowance for culverts and other buried structures covered by Section 12, in percent shall be taken as:
IM = 33(1.0 – 0.41DE) > 0%
where : DE = minimum depth of earth cover above the structure (m)

## Slide 14
3.6.3—Centrifugal Forces: CE
For the purpose of computing the radial force or the overturning effect on wheel loads, the centrifugal effect on live load shall be taken as the product of the axle weights of the design truck or tandem and the factor C, taken as:
C= f v2 / g R …….. (3.6.3-1)
v = highway design speed (km/hr) , f = 4/3 for all load combinations except fatigue and 1.0 for fatigue
g = gravitational constant = 9.807 m/sec2.
R = radius of curvature for the traffic lane (m).
  The multiple presence factors shall apply.
  Centrifugal forces shall be applied horizontally at a distance 1.80m above the roadway surface. A load path to carry the radial force to the substructure shall be provided.
  The effect of super elevation in reducing the overturning effect of centrifugal force on vertical wheel leads may be considered.
3.6.4: Braking Force - BR
The braking force shall be taken as the greater of:
  25% of the axle weights of the design truck or design tandem
  or 5% of the design truck plus lane load
  or 5% of the design tandem plus lane load
  This braking force shall be placed in all design lanes which are considered to be loaded in accordance with Article 3.6.1.1.1 (defines number of design lanes) and which are carrying traffic headed in the same direction. These forces shall be assumed to act horizontally at a distance of 1.80m above the roadway surface in either longitudinal direction to cause extreme force effects. All design lanes shall be simultaneously loaded for bridges likely to become one-directional in the future.

## Slide 15
3.6.5: Vehicular Collision Force – CT
3.6.5.1 Protection of structures
  The provisions of Article 3.6.5.2 need not be considered for structures which are protected by:
  An embankment
  A structurally independent, crash worthy ground mounted 1.37m high barrier located within 3.0m
  from the component being protected
  A 1.07m in high barrier located at more than 3.0m from the component being protected
  In order to qualify for this exemption, such barrier shall be structurally and geometrically capable of surviving the crash test for Test Level 5, as specified in Section 13.
3.6.5.2 Vehicle and Railway Collision with Structures
Abutments and piers located within a distance of 9.0mto the edge of the roadway, shall be designed for an equivalent static force of 1800kN, which is assumed to act in any direction in a horizontal plane, at distance of 1.2m above ground.
3.7—WATER LOADS: WA
3.7.1—Static Pressure
Static pressure of water shall be assumed to act perpendicular to the surface that is retaining the water. Pressure shall be calculated as the product of height of water above the point of consideration and the specific weight of water. Design water levels for various limit states shall be as specified and/or approved by the Owner.
3.7.2—Buoyancy
Buoyancy shall be considered to be an uplift force, taken as the sum of the vertical components of static pressures, as specified in Article 3.7.1, acting on all components below design water level. For substructures with cavities in which the presence or absence of water cannot be ascertained, the condition producing the least favorable force effect should be chosen.

## Slide 16
3.7.3—Stream Pressure
3.7.3.1—Longitudinal
The pressure of flowing water acting in the Longitudinal direction of substructures shall be taken as:
p = 5.14 x 10-4 CD V2
p = pressure of flowing water (MPa)
CD= drag coefficient for piers as specified in Table 3.7.3.1-1
V = design velocity of water for the design flood in strength and service limit states and for the check
flood in the extreme event limit state (m/s)
3.7.3.2—Lateral
The lateral, uniformly distributed pressure on a substructure due to water flowing at an angle, θ, to the longitudinal axis of the pier shall be taken as:
p = 5.14 x 10-4 CD V2
where:
p = lateral pressure (MPa)
CL= lateral drag coefficient specified in Table 3.7.3.2-1
3.7.4—Wave Load
Wave action on bridge structures shall be considered for exposed structures where the development of significant wave forces may occur.

## Slide 17
3.8: Wind Loads WL and WS - General
  WS is the wind load on the structure.
  WL is the wind load on the live load.
  Both horizontal and vertical wind loads must be considered.
  The pressures are assumed to be caused by a base wind velocity, VB = 160 kmph.
  The wind is assumed to be a uniformly distributed load applied to the sum area of all components of the structure, as seen in elevation taken perpendicular to the wind direction. The direction is varied to produce the extreme force effect. Areas which do not contribute to the extreme force effect may be ignored. For both WS and WL, the first step is to find the design wind velocity, VDZ, at a particular elevation, Z. For bridges more than 9.0m above low ground or water level:
VDZ = 2.5V0 (V30/ VB) ln (Z / Z0)
V30= wind velocity at 10.0m above low ground (kmph).
VB= base wind velocity = 160 kmph
Z = height of structure at which the winds are being calculated > 10.0m.above low ground or water level.
Z0= Friction length of upstream fetch (m)
V0= Friction velocity (kmph)
3.9—ICE LOADS: IC
3.9.1—General
This Article refers only to freshwater ice in rivers and lakes; ice loads in seawater should be determined by suitable specialists using site-specific information.
Ice forces on piers shall be determined with regard to site conditions and expected modes of ice action as follows:
• Dynamic pressure due to moving sheets or floes of ice being carried by stream flow, wind, or currents;
• Static pressure due to thermal movements of ice sheets;
• Pressure resulting from hanging dams or jams of ice; and
• Static uplift or vertical load resulting from adhering ice in waters of fluctuating level.
The expected thickNess of ice, the direction of its movement, and the height of its action shall be determined by field investigations, review of public records, aerial surveys, or other suitable means.

## Slide 18
3.10 Earthquake Effects: EQ
Bridges shall be designed to have a low probability of collapse but may suffer significant damage and disruption to service when subject to earthquake ground motions that have a seven percent probability of exceedance in 75 yr. Partial or complete replacement may be required. Higher levels of performance may be used with the authorization of the Bridge Owner. Earthquake loads shall be taken to be horizontal force effects determined in accordance with the response coefficient, Csm, specified in Article 3.10.4, and the equivalent weight of the superstructure, and adjusted by the response modification factor, R, specified in Article 3.10.7.1. The provisions herein shall apply to bridges of conventional construction. The Owner shall specify and/or approve appropriate provisions for nonconventional construction.
  All bridges in Erbil fall in Seismic Zone II
  Design the connection between the superstructure and substructure to resist 0.2 times the vertical reaction due to tributary permanent load.
  The Extreme Event I load factor for live load, γEQ is taken as 0.0.
  If seismic restraints are provided, EQ for substructures at Extreme Event I Limit State = 0.2 times tributary live and dead loads applied in the restrained direction resulting in maximum effect.
3.11—EARTH PRESSURE: EH, ES, LS, AND DD
3.11.1—General
Earth pressure shall be considered as a function of the:
• Type and unit weight of earth,
• Water content,
• Soil creep characteristics,
• Degree of compaction,
• Location of groundwater table,
• Earth-structure interaction,
• Amount of surcharge,
• Earthquake effects,
• Back slope angle, and
• Wall inclination.

## Slide 19
3.12—FORCE EFFECTS DUE TO SUPERIMPOSED DEFORMATIONS: TU, TG, SH, CR, SE, PS
3.12.1—General
Internal force effects in a component due to creep and shrinkage shall be considered. The effect of a temperature gradient should be included where appropriate. Force effects resulting from resisting component deformation, displacement of points of load application, and support movements shall be included in the analysis.
3.13—FRICTION FORCES: FR
Forces due to friction shall be established on the basis of extreme values of the friction coefficient between the sliding surfaces. Where appropriate, the effect of moisture and possible degradation or contamination of sliding or rotating surfaces upon the friction coefficient shall be considered. Low and high friction coefficients may be obtained from standard textbooks. If so warranted, the values may be determined by physical tests, especially if the surfaces are expected to be roughened in service.
3.14—VESSEL COLLISION: CV
3.14.1—General
The provisions of this Article apply to the accidental collision between a vessel and a bridge. These provisions may be revised as stated in Article 3.14.16 to account for intentional collisions. All bridge components in a navigable waterway crossing, located in design water depths not less than 600mm, shall be designed for vessel iMPact. The minimum design iMPact load for substructure design shall be determined using an empty hopper barge drifting at a velocity equal to the yearly mean current for the waterway location. The design barge shall be a single 10.7×60m barge, with an empty displacement of 200 ton, unless approved otherwise by the Owner. Where bridges span deep draft waterways and are not sufficiently high to preclude contact with the vessel, the minimum superstructure design iMPact may be taken to be the mast collision iMPact load specified in Article 3.14.10.3.
In navigable waterways where vessel collision is anticipated, structures shall be:
• Designed to resist vessel collision forces, and/or
• Adequately protected by fenders, dolphins, islands, or other sacrifice-able devices.
In determining vessel collision loads, consideration shall be given to the relationship of the bridge to:
• Waterway geometry,
• Size, type, loading condition, and frequency of vessels using the waterway,
• Available water depth,
• Vessel speed and direction, and • The structural response of the bridge to collision.

## Slide 20
3.15—BLAST LOADING: BL
3.15.1—Introduction
Where it has been determined that a bridge or a bridge component should be designed for intentional or unintentional blast force, the following should be considered:
• Size of explosive charge,
• Shape of explosive charge,
• Type of explosive,
• Stand-off distance,
• Location of the charge,
• Possible modes of delivery and associated capacities (e.g., maximum charge weight will depend upon
vehicle type and can include cars, trucks, ships, etc.), and
• Fragmentation associated with vehicle-delivered explosives
Section 4: Structural Analysis and Evaluation
4.6.2—Approximate Methods of Analysis
4.6.2.1—Decks
4.6.2.1.1—General
An approximate method of analysis in which the deck is subdivided into strips perpendicular to the supporting components shall be considered acceptable for decks other than:
  fully filled and partially filled grids for which the provisions of Article 4.6.2.1.8 shall apply, and
  top slabs of segmental concrete box girders for which the provisions of 4.6.2.9.4 shall apply.
Where the strip method is used, the extreme positive moment in any deck panel between girders shall be taken to apply to all positive moment regions. Similarly, the extreme negative moment over any beam or girder shall be taken to apply to all negative moment regions.
4.6.2.1.2—Applicability
The use of design aids for decks containing prefabricated elements may be permitted in lieu of analysis if the performance of the deck is documented and supported by sufficient technical evidence. The Engineer shall be responsible for the accuracy and implementation of any design aids used. For slab bridges and concrete slabs spanning more than 4600mm and which span primarily in the direction parallel to traffic, the provisions of Article 4.6.2.3 shall apply.

## Slide 22
4.6.2.1.3—Width of Equivalent Interior Strips
The width of the equivalent strip of a deck may be taken as specified in Table 4.6.2.1.3-1. Where decks span primarily in the direction parallel to traffic, strips supporting an axle load shall not be taken to be greater than 1000mm for open grids and not greater than 3600mm for all other decks where multilane loading is being investigated. For deck overhangs, where applicable, the provisions of Article 3.6.1.3.4 may be used in lieu of the strip width specified in Table 4.6.2.1.3-1 for deck overhangs. The equivalent strips for decks that span primarily in the transverse direction shall not be subject to width limits. The following notation shall apply to Table 4.6.2.1.3-1:
S = spacing of supporting components (mm)
h = depth of deck (mm)
L = span length of deck (mm)
P = axle load (N)
Sb = spacing of grid bars (mm)
+M = positive moment
−M = negative moment
X = distance from load to point of support (mm)

## Slide 23
4.6.2.1.4 Width of Equivalent Strips at Edges of Slabs
4.6.2.1.4a—General
For the purpose of design, the notional edge beam shall be taken as a reduced deck strip width specified herein. Any additional integral local thickening or similar protrusion acting as a stiffener to the deck that is located within the reduced deck strip width can be assumed to act with the reduced deck strip width as the notional edge beam.
4.6.2.1.4b—Longitudinal Edges
Edge beams shall be assumed to support one line of wheels and, where appropriate, a tributary portion of the design lane load. Where decks span primarily in the direction of traffic, the effective width of a strip, with or without an edge beam, may be taken as the sum of the distance between the edge of the deck and the inside face of the barrier, plus 300mm, plus one-quarter of the strip width, specified in either Article 4.6.2.1.3, Article 4.6.2.3, or Article 4.6.2.10, as appropriate, but not exceeding either one-half the full strip width or 1800mm.
4.6.2.1.4c—Transverse Edges
Transverse edge beams shall be assumed to support one axle of the design truck in one or more design lanes, positioned to produce maximum load effects. Multiple presence factors and the dynamic load allowance shall apply. The effective width of a strip, with or without an edge beam, may be taken as the sum of the distance between the transverse edge of the deck and the centerline of the first line of support for the deck, usually taken as a girder web, plus one-half of the width of strip as specified in Article 4.6.2.1.3. The effective width shall not exceed the full strip width specified in Article 4.6.2.1.3.
4.6.2.1.5—Distribution of Wheel Loads
If the spacing of supporting components in the secondary direction exceeds 1.5 times the spacing in the primary direction, all of the wheel loads shall be considered to be applied to the primary strip, and the provisions of Article 9.7.3.2 may be applied to the secondary direction. This Article attempts to clarify the application of the traditional AASHTO approach with respect to continuous decks. If the spacing of supporting components in the secondary direction is less than 1.5 times the spacing in the primary direction, the deck shall be modeled as a system of intersecting strips. The width of the equivalent strips in both directions may be taken as specified in Table 4.6.2.1.3-1. Each wheel load shall be distributed between two intersecting strips. The distribution shall be determined as the ratio between the stiffness of the strip and the sum of stiffness’s of the intersecting strips. In the absence of more precise calculations, the strip stiffness, ks, may be estimated as:
ks =EIs / S3
where: Is = moment of inertia of the equivalent strip (mm4)

## Slide 24
4.6.2.1.6—Calculation of Force Effects
The strips shall be treated as continuous beams or simply supported beams, as appropriate. Span length shall be taken as the center-to-center distance between the supporting components. For the purpose of determining force effects in the strip, the supporting components shall be assumed to be infinitely rigid. The wheel loads may be modeled as concentrated loads or as patch loads whose length along the span shall be the length of the tire contact area, as specified in Article 3.6.1.2.5, plus the depth of the deck. The strips should be analyzed by classical beam theory. The design section for negative moments and shear forces, where investigated, may be taken as follows:
• For monolithic construction, closed steel boxes, closed concrete boxes, open concrete boxes without top flanges, and stemmed precast beams, i.e., Cross sections(b), (c), (d), (e), (f), (g), (h), (i), and (j)from Table 4.6.2.2.1-1, at the face of the supporting component,
• For steel I-beams and steel tub girders, i.e., Cross-sections (a) and (c) from Table 4.6.2.2.1-1, one-quarter the flange width from the centerline of support,
• For precast I-shaped concrete beams and open concrete boxes with top flanges, i.e., Cross-sections(c) and (k) from Table 4.6.2.2.1-1, one-third the flange width, but not exceeding 380mm, from the centerline of support.
4.6.2.1.8—Live Load Force Effects for Fully and Partially Filled Grids and for Unfilled Grid Decks Composite with Reinforced Concrete Slabs
Moments in N.mm/mm of deck due to live load maybe determined as:
• Main bars perpendicular to traffic:
For L ≤ 3000mm, M = 1290 D0.197 L0.459 C
For L >3000mm, M = 5300 D0.887(L1.35-20 400) C / L
• Main bars parallel to traffic:
For L ≤ 3000mm, M = 408 D0.123 L0.64 C
For L >3000mm, M = 3405 D0.138 (L1.429-34 900) C / L
where: L = span length from center-to-center of supports (mm)
C = continuity factor; 1.0 for simply supported and0.8 for continuous spans

## Slide 25
D = Dx/Dy
Dx = flexural rigidity of deck in main bar direction (N.mm2/mm)
Dy = flexural rigidity of deck perpendicular to main bar direction (N.mm2/mm)
For grid decks, Dx and Dy should be calculated as EIx and EIy where E is the modulus of elasticity and Ix and Iy are the moment of inertia per unit width of deck, considering the section as cracked and using the transformed area method for the main bar direction and perpendicular to main bar direction, respectively.
Moments for fatigue assessment may be estimated for all span lengths by reducing Eq. 4.6.2.1.8-1 for main bars perpendicular to traffic or Eq. 4.6.2.1.8-3 for main bars parallel to traffic by a factor of 1.5.
Deflection in units of mm due to vehicular live load may be determined as:
• Main bars perpendicular to traffic:
Δ = 0.91D0.19L3 / Dx
• Main bars parallel to traffic:
Δ = 1.26D0.11L3 / Dx
4.6.2.1.9—Inelastic Analysis
The inelastic finite element analysis or yield line analysis may be permitted by the Owner.
4.6.2.2—Beam-Slab Bridges
4.6.2.2.1—Application
The provisions of this Article may be applied to straight girder bridges and horizontally curved concrete bridges, as well as horizontally curved steel girder bridges complying with the provisions of Article 4.6.1.2.4. The provisions of this Article may also be used to determine a starting point for some methods of analysis to determine force effects in curved girders of any degree of curvature in plan. Except as specified in Article 4.6.2.2.5, the provisions of this Article shall be taken to apply to bridges being analyzed for:
• A single lane of loading, or
• Multiple lanes of live load yielding approximately the same force effect per lane.

## Slide 26
If one lane is loaded with a special vehicle or evaluation permit vehicle, the design force effect per girder resulting from the mixed traffic may be determined as specified in Article 4.6.2.2.5.
For beam spacing exceeding the range of applicability as specified in tables in Articles 4.6.2.2.2and 4.6.2.2.3, the live load on each beam shall be there action of the loaded lanes based on the lever rule unless specified otherwise herein.
The provisions of 3.6.1.1.2 specify that multiple presence factors shall not be used with the approximate load assignment methods other than staticalmoment or lever arm methods because these factors are already incorporated in the distribution factors.
Bridges not meeting the requirements of this Article shall be analyzed as specified in Article 4.6.3.The distribution of live load, specified in Articles 4.6.2.2.2 and 4.6.2.2.3, may be used for girders, beams, and stringers, other than multiple steel box beams with concrete decks that meet the following conditions and any other conditions identified in tables of distribution factors as specified herein:
  Width of deck is constant;
  Unless otherwise specified, the number of beams is not less than four;
  Beams are parallel and have approximately the same stiffness;
  Unless otherwise specified, the roadway part of the overhang, de, does not exceed 910mm;
  Curvature in plan is less than the limit specified in Article 4.6.1.2.4, or where distribution factors are required in order to implement an acceptable approximate or refined analysis method satisfying the requirements of Article 4.4 for bridges of any degree of curvature in plan; and
  Cross-section is consistent with one of the cross sections shown in Table 4.6.2.2.1-1.
Live load distribution factors, specified herein, maybe used for permit and rating vehicles whose overall width is coMParable to the width of the design truck.

## Slide 27
4.6.2.2.2—Distribution Factor Method for Moment and Shear
4.6.2.2.2a—Interior Beams with Wood Decks
The live load flexural moment and shear for interior beams with transverse wood decks may be determined by applying the lane fraction specified in Table 4.6.2.2.2a-1 and Eq. 4.6.2.2.2a-1.When investigation of shear parallel to the grain in wood components is required, the distributed live load shear shall be determined by the following expression:
VLL= 0.50[(0.60VLU) + VLD]
where: VLL= distributed live load vertical shear (N)
VLU= maximum vertical shear at 3d or L/4 due to undistributed wheel loads (N)
VLD= maximum vertical shear at 3d or L/4 due to wheel loads distributed laterally as specified herein (N)For
undistributed wheel loads, one line of wheels is assumed to be carried by one bending member.
4.6.2.2.2b—Interior Beams with Concrete Decks
The live load flexural moment for interior beams with concrete decks may be determined by applying the lane fraction specified in Table 4.6.2.2.2b-1.For the concrete beams, other than box beams, used in multi beam decks with shear keys:
• Deep, rigid end diaphragms shall be provided to ensure proper load distribution; and
• If the stem spacing of stemmed beams is less than 1200mm or more than 3000mm, a refined analysis complying with
Article 4.6.3 shall be used.
4.6.2.2.2d—Exterior Beams
The live load flexural moment for exterior beams may be determined by applying the lane fraction, specified in Table 4.6.2.2.2d-1.The distance, de, shall be taken as positive if the exterior web is inboard of the interior face of the traffic railing and negative if it is outboard of the curb or traffic barrier.
In beam-slab bridge cross-sections with diaphragms or cross-frames, the distribution factor for the exterior beam shall not be taken to be less than that which would be obtained by assuming that the cross-section deflects and rotates as a rigid cross-section. The provisions of Article 3.6.1.1.2 shall apply
4.6.2.2.2f—Flexural Moments and Shear in Transverse Floor beams
If the deck is supported directly by transverse floor beams, the floor beams may be designed for loads determined in accordance with Table 4.6.2.2.2f-1.The fractions provided in Table 4.6.2.2.2f-1 shall be used in conjunction with the 32.0-kip design axle load alone. For spacing’s of floor beams outside the given ranges of applicability, all of the design live loads shall be considered, and the lever rule may be used.

## Slide 28
4.6.2.2.3—Distribution Factor Method for Shear
4.6.2.2.3a—Interior Beams
The live load shear for interior beams may be determined by applying the lane fractions specified in Table 4.6.2.2.3a-1. For interior beam types not listed in Table 4.6.2.2.3a-1, lateral distribution of the wheel or axle adjacent to the end of span shall be that produced by use of the lever rule. For concrete box beams used in multi beam decks, if the values of I or J do not comply with the limitations in Table 4.6.2.2.3a-1, the distribution factor for shear maybe taken as that for moment.
4.6.2.2.3b—Exterior Beams
The live load shear for exterior beams shall be determined by applying the lane fractions specified in Table 4.6.2.2.3b-1. For cases not addressed in Table 4.6.2.2.3a-1 and Table 4.6.2.2.3b-1, the live load distribution to exterior beams shall be determined by using the lever rule. The parameter de shall be taken as positive if the exterior web is inboard of the curb or traffic barrier and negative if it is out board. The additional provisions for exterior beams in beam-slab bridges with cross-frames or diaphragms, specified in Articles 4.6.2.2.2d, shall apply.
4.6.2.3—Equivalent Strip Widths for Slab-Type Bridges
This Article shall be applied to the types of cross sections shown schematically in Table 4.6.2.3-1. For the purpose of this Article, cast-in-place voided slab bridges may be considered as slab bridges. The equivalent width of longitudinal strips per lane for both shear and moment with one lane, i.e., two lines of wheels, loaded may be determined as:
E=250+0.42 √L1W1
The equivalent width of longitudinal strips per lane for both shear and moment with more than one lane loaded may be determined as:
E=2100+0.12 √L1W1 ≤ W / NL
where:
E = equivalent width (mm)
L1 = modified span length taken equal to the lesser of the actual span or 18000mm.
W1 = modified edge-to-edge width of bridge taken to be equal to the lesser of the actual width or 18000 for multilane
loading, or 9000 for single-lane loading (mm)
W = physical edge-to-edge width of bridge (mm)
NL= number of design lanes as specified in -Article 3.6.1.1.1

## Slide 29
4.6.2.9.4 Transverse Analysis The transverse design of box girder segments for flexure shall consider the segment as a rigid box frame. Flanges shall be analyzed as variable depth sections, considering the fillets between the flanges and webs. Wheel loads shall be positioned to provide maximum moments, and elastic analysis shall be used to determine the effective longitudinal distribution of wheel loads for each load location. Consideration shall be given to the increase in web shear and other effects on the cross-section resulting from eccentric loading or unsymmetrical structure geometry.

## Slide 30
Note: The roadway overhang de < 900mm does not apply to interior DFs for sections (a) and (k).
AASHTO Section 5 , concrete structures
  Concrete compressive strength ( ) , 5.4.2.1
16 MPa< < 70 MPa
≥ 28 MPa for prestressed concrete and decks
  for normal density , C.5.4.2.4
  0.2 , poison's Ratio
  Modulus of rupture ( fr ) , 5.4.2.6
fr = 0.63 Control of Cracking by Distribution of Reinforcement
fr = 0.97 for check of Minimum Reinforcement
  Steel yield stress ( fy ) 5.4.3
fy ≤ 520 MPa
for fy < 420 MPa shall be used with the approval of the owner
  Es = 200 000 Mpa
  Prestressed steel
For strand
1. Grade 250 ( 1725 MPa ) , fpu = 1725 MPa , fpy ≈ ( 0.85 – 0.9 ) fpu
2. Grade 270 ( 1860 MPa ) , fpu = 1860 MPa , fpy = ( 0.85 – 0.9 ) fpu
  Eps = 197 000 MPa

## Slide 31
Limit states, AASHTO 2012 Section 5.5
Structural components shall be proportioned to satisfy the requirements at all appropriate service, fatigue, strength, and extreme event limit states.
Service limit state: actions to be considered at the service limit state shall be cracking, deformations and concrete Stresses.
Strength limit state: the strength limit state issues to be considered shall be those of strength and stability.
Resistance factor ᵩ shall be taken as:
  Flexure and tension of R.C. ……………………… 0.9
  Flexure and tension of prestressed con. …… 1.0
  Shear and torsion (normal structural concrete ) ……… 0.9
  Axial comp. ………………………….. 0.75
  Bearing on concrete ……………… 0.7
  Comp. in Anchorage zone ( N. St. Con ) ….......... 0.8
  Tension in steel in Anchorage ……………1.0
  Resistance during pile driving …………… 1.0
. For comp. members with flexure, ᵩ increased from 0.75  0.9
. For partially prestressed concrete ᵩ = 0.9 + 0.1 PPR
PPR =
PPR : partial prestress ratio , if PRP < 50% consider R.C.
Design for flexure and axial force effect, 5.70
Rectangular stress dist. β1 = 0.65 – 0.85 for normal con.
β1 avg. = for composite
Acc : area of concrete in comp .

## Slide 32
Flexural members
Mr = φ Mu
1. Bonded tendons of prestress of fpe ≥ 0.5 fpu
fps = fpu ( 1 – k )
k = 2 * ( 1.04 - )
- T section
c =
2. Unbounded tendons
fps = fpe + 6300 ( ) ≤ fpy
= ( )
: effective tend. Length , mm
: length of tendons between anchorages
: No. of supp. hinges or bonded points
: effective stress
: when > fy , or = fs
- Flanged section (tendons bonded & comp. flange depth < c
Mn = Aps fps( dp – a/2)+As fy (ds – a/2) – As' fy' (d' – a/2)+0.85 (b-bw) 1 hf(a/2-hf/2)
:
1

## Slide 33
- Rectangular section of flanged comp. flange depth ≥ C , b = bw
Mn = Aps fps( dp – a/2) + As fy (ds – a/2) – As' fy' (d' – a/2)
Limits of reinforcement 5.7-3.3
1. Maximum reinforcement
c/de ≤ 0.42 under reinforced, otherwise comp. reinf. required ( over reinf. )
S max ≤ 1.5 t & 450 mm ( 5.10.3.2 )
2. Minimum reinforcement
Amount of prestress & non prestress reinf. shall be adequate to develop a factored flexural resistance , Mr at least equal to the lesser of :
a. 1.2 * Mcr
Mcr = Sc ( fr + fcpe ) – Mdnc ( ) Sc fr
fr = 0.97
Sc : section modulus ( mm3 ) of composite sec. due to DL.
Snc : Section modulus for monolithic or non-comp .
fcpe : comp. stress in conc. Due to effective prestress force
Mdnc : total unfactored DL for non-composite section .
b. 1.33 * M factored reqd. strength load combinations
According to (5.10.3.1)

## Slide 34
3. Control of cracking by dist. Of reinforcement.
Spacing (S) of tens. Reinforcement shall satisfy the followings :
= 1.0 for class 1 exposure
= 0.75 for class 2 exposure
dc : cover
fs ≈ 0.6 fy or fs =
Shrinkage and temperature reinforcement:
Ash ≥ 0.11 Ag /fy , Ag = 1000 * t
The steel shall be equally distribution On both faces with spacing ≤ 3t or 450 mm
If de > 900 mm , long. skin reinforcement shall be uniformly distribution Along both sides faces of the component for a distance d/2 nearest the flexural reinforcement.
Ask ≥ 0.001 ( de – 760 ) ≤ , mm2/m
- Amount for each face ≤ ( As+ Aps )
- S ≤ de/6
≤ 300 mm

## Slide 35
The nominal shear resistance, Vn determined as lesser of :
Vn = Vc + Vs + Vp
Or
Vn = 0.25 bv dv + Vp
Where :
Vc = 0.083 β bv dv
Vs = , for 𝛼=90o sin𝛼 = 1
Vs =
𝛳 = 45o , β ≈ 2.0
Provisions for structural types AASHTO 2012 sec.5.14
1. Precast beam dimensions
Thickness of any part of precast concrete beams shall not be less than :
- Top flange 50mm
- Web non post tension 125 mm
- Web post tensioned 165mm
- Bott. Flange 125mm

## Slide 36
Shear and Torsion AASHTO 2012 sec. 5.80
Vr = φ Vn
Tr = φ Tn
Torsion design reqd when Tu ≥ 0.25 φ Tcr
Transverse reinforcement shall be provided where :
Vu > 0.5 φ ( Vc + Vp )
Or
Where consideration of torsion is required
Vp : component of prestressing force in the direction of shear force .
Minimum Transverse reinforcement
Maximum spacing of transverse reinforcement
If Vu < 0.125  Smax = 0.8 dv ≤ 600 mm
If Vu ≥ 0.125  Smax = 0.4 dv ≤ 300 mm
≥ 0.72 h