## Slide 1
Microprocessor & Microcontroller
For Second Stage Computer & IT Department
Lecturer M.Sajda Hadi
MSc. in Computer & Control Eng. Dep.
Salahaddin University
College of Science Education
Computer Science Department

## Slide 2: References
The 8086 Microprocessors Architecture,software and Interfacing techniques, By: Walter A. Triebel
The 8086/8088 MPU, Architecture,programming and interfacing, BY: Barry B. Brey
Introduction to Microcontrollers, ,G¨unther Gridling, Bettina Weiss, February 26, 2007
Microcontroller and Embedded Systems Laboratory, Authors: Kileen Cheng, Patrick Frantz, CJ Ganier, October 25, 2012
Singh ,A, The 8088 Microprocessor Programming , interfacing , software , hardware and applications, 1989

## Slide 3: Objective
Understand fundamental concepts of 8086 Microprocessor architecture.
Studying assembly language 8086 instruction set and addressing mode.
Solve common problems using assembly language.
Be familiar with different types of MC’s and how to choose best type for different applications.

## Slide 4: Forms of Teaching
The course consists of two parts; a theoretical part and practical or applied part, part I (theory) depend on lectures in the hall to explain the basic concepts associated with the course by using the Data show and white board.
Part II (practical) is associated with training on EMU8086 version4 program in assembly Lab. .

## Slide 5: The Two Terms program
Week1 Introduction, course outline and grading
Week2 CPU Architecture, System bus .
Week3 PC components, Data Transfer, Fetch and Execute Cycles.
Week4 Address , Data and Control Busses
Week5 Memory Types, operation and Read/Write cycles
Week6 I/O controllers , Execution and Bus Interface unit.
Week7 Addressing data in memory, Registers of the 8086.
Week8 Data Registers, Flags, The Status Register, and Implementing Control
Week9 No. of Operands in instructions, Addressing Modes of 8086
Week10 1st semester Exam

## Slide 6: 2nd Term Program
Week 11 8 types of addressing mode .
Week12 Stack (Concepts and Applications )
Week13 Instruction set, Data transfer instructions
Week14 Arithmetic and Logic Instructions
Week15 Logical Instructions
Week16 Advance instruction (Program and Control )
Week17 Jump Instructions
Week18 String instructions
Week19 Interrupts.
Week22 Hardware interrupts and maskable INT
Week23 Input / Output Instruction
Week24 Isolated and memory I/O
Week25 -26 Iteration Instructions, Procedure Call And Return
Week26-27 microcontroller Types based on vendor or provider ; AVR, PIC,Hitachi,Motorolla etc,-RISC Vs. CISC CPU ARCHITECTURES , HARVARD Vs. VON- NEUMANN CPU ARCHITECTURE
.Week 28-30 How Do We Right the Instructions and Tell the MPU What to Do?,Working with microcontroller, Memory selection of the microcontroller, , common communication peripherals on MC’s: UART, SPI, and I2C, Different microcontroller with applications

## Slide 7: LECTURE #1

## Slide 8: Microcomputer Architecture
A computer system has three main components: a Central Processing Unit (CPU) or processor, a Memory Unit and Input Output Units (devices). In any microcomputer system, the component which actually processes data is entirely contained on a single chip called Microprocessor (MPU). This MPU can be programmed using assembly language. Writing a program in assembly language requires a knowledge of the computer hardware (or Architecture) and the details of its instruction set.

## Slide 9: Fig(1): A computer block diagram Fig(2): CPU Components
I/P
CPU
(μp)
memory
O/P
ALU
REGISTERS
CONTROL UNIT (CU)

## Slide 10: Computer main Components
The main internal hardware features of a computer are the processor, memory and registers (registers are special processor
components for holding address and data).
The external hardware features are the computer Input/Output devices such as keyboard, monitor…
Software consists of the operating system (O.S) and various programs and data files stored on disk.

## Slide 11: Evolution of Intel Microprocessor
The principle way in which MPU & microcomputer are categorized in term of the maximum number of binary bit in the data they process that is, their word length. Processor vary in their speed, capacity of memory, register and data bus, below are a brief description of various Intel processor in Table 1.
8088 and 8086 functionally identical but 8088 lower performance, 80186 run all 8088 and 8086 software, but have 10 new instructions. 80188 in function is identical to 80186 but lower performance.
80286 run all 8086, 80186 program, but has extra instruction, more powerful than 8086. 83086 has various operation mode, which allow it to act as 80286 chip or multiple 8086 chip, as well as a set of instruction capable of 32 bit operations such as arithmetic.

## Slide 12: Table 1: Different Microprocessor features descriptions
Microprocessor Name | Features Descriptions |  | 
 | Width of (DB) | Width of (AB) | Instruction Queue length
8086 | 16 bit | 20 bit | 6 Byte
8080 | 8 bit | 20 bit | 4 Byte
80186 | 16 bit | 20 bit | 6 Byte
80188 | 8 bit | 20 bit | 4 Byte
80286 | 16 bit | 24 bit | 6 Byte
80386 | 32 bit | 32 bit | 6 Byte

## Slide 13: CPU function
The function of the ALU section of the CPU is to perform arithmetic and logical operations of the computer. The function of the control unit is to provide timing signals for synchronizing the transfer of data between the CPU and peripheral devices, including memory, through a group of wires known as the system bus.

## Slide 14: System Bus
The components of the computer system must communicate with each other and with the outside world. the processor is connected to memory and all peripherals using a bus.
A Bus is a bunch of wires, and electrical path on the printed IC to which every thing in the system is connected.

## Slide 15: Types of Busses
Address Bus (AB): for carrying the address/location of the memory where the data has to be placed.
Data Bus (DB): for carrying the data/ information between micro processor and I/O device.
Control Bus (CB): for carrying the timing and control signals, typical control signals includes memory read, memory write, I/O read, I/O write, interrupt acknowledge, bus request. These control signals indicates the type of action taking place on the system bus.

## Slide 16: General organization of microcomputer
Central processing Unit
ROM
RAM
Input port
Output port
Address bus
Data bus