## Slide 1: Practical of Network Fundamentals
Computer Dept. 3rd Stage
Prepared by: Arazu S. Omer
2023-2024

## Slide 2
Lab 1
Packet Tracer: Introduction to Packet Tracer Interfaces. Creating & Configuring a simple LAN Topology.
Configuring DHCP

## Slide 3
Lab 2
Cisco IOS: Introduction to IOS & Navigating IOS Modes
Modes | Example
User EXEC mode | Router>enable
Privileged EXEC mode | Router configure terminal
Global configuration mode | Router(config)#
Edit and Help Features: ? , Tab , Up arrow.

## Slide 4
Lab 3: VLAN & Trunking Configuration
To Show Switch VLANS:
Switch# show vlan
To Create VLAN: Switch(config)#vlan 2 Students Switch(config-vlan)#name s Switch(config-vlan)#exit
Switch(config)#interface fastEthernet 0/2 Switch(config-if)#switchport mode access
Switch(config-if)#switchport access vlan 2
Switch(config)#interface fastEthernet 0/3 Switch(config-if)#switchport mode access Switch(config-if)#switchport access vlan 2
Switch(config)#vlan 3
Switch(config-vlan)#name Teachers
Switch(config)#interface range fastEthernet 0/4-6 Switch(config-if)#switchport mode access Switch(config-if)#switchport access vlan 3 Switch(config-if)#exit
Switch#write Switch#show vlan
To Configure Trunk Interface: Switchs(config)# interface fa0/24 Switch(config-if )#Switch mode trunk
To Show Trunk Interfaces:
Switch# show interface trunk

## Slide 5
Lab 4: InterVLAN Routing Using Router Ethernet Interface Configurations: Router(Config)# Interface fa0/0
Router(Config-if)# no shutdown
Router(Config-if)# no ip address
Router(Config-if)# exit
Sub-Interface Configurations: Router(Config)# Interface fa 0/0.1 Router(Config-if)# encapsulation dot1q 2
Router(Config-if)# IP address 192.168.1.0 255.255.255.0 Router(Config-if)# exit
Router(Config)# Interface fa 0/0.2
Router(Config-if)# encapsulation dot1q 3
Router(Config-if)# IP address 192.168.10.0 255.255.255.0 Router(Config-if)# exit
DIY: InterVLAN routing using Layer 3 Switch.

## Slide 6
Lab 5: Switch Port Security
To Configure:
Switch(config)# interface fa 0/1 Switch(config-if)# switchport mode access
Switch(config-if)# switchport port-security maximum 1
Switch(config-if)# switchport port-security mac-address 0013.20b7.1235
Switch(config-if)# switchport port-security violation shutdown Switch(config-if)# switchport port-security
Switch(config)# interface range fa 0/2-3 Switch(config-if)# switchport mode access
Switch(config-if)# switchport port-security maximum 1 Switch(config-if)# switchport port-security mac-address sticky Switch(config-if)# switchport port-security violation restrict Switch(config-if)# switchport port-security
To show/ verify:
Switch# show port-security Switch# show port-security address

## Slide 7
Router’s Configuration: hostname, enable password, Save. To configure the host name and enable password: Router>enable
Router#configure terminal Router(config)#hostname KanyRouter
HawlerRouter(config)#enable password myPass2017 HawlerRouter(config)#exit
HawlerRouter#write
To Verify: HawlerRouter#show start
Lab 6
Router’s Configuration: VTY Line and LAN Interface.
To configure IP address to LAN interfaces, run the commands:
HawlerRouter >enable HawlerRouter #configure terminal
HawlerRouter (config)#interface fastethernet 0/0 HawlerRouter (config-if)#ip address 10.0.0.1 255.0.0.0
HawlerRouter (config-if)#no shutdown HawlerRouter (config-if)#exit HawlerRouter (config)#exit HawlerRouter #
To configure VTY lines with password, run the following commands: HawlerRouter >enable
HawlerRouter #configure terminal

## Slide 8
HawlerRouter (config-line)#line vty 0 4 HawlerRouter (config-line)#password @Kani#2015 HawlerRouter (config-line)#login
HawlerRouter (config-line)#exit HawlerRouter (config)#exit HawlerRouter #
To Verify:
HawlerRouter#show start HawlerRouter#show ip interface brief
Router’s Configuration: View, Change and Eraser configuration.
To show the running configuration:
Router#show run
To show the start-up configuration:
Router#show startup
To erase the configuration stored in NVRAM:
Router#erase startup
To restart the router:
Router#reload

## Slide 9
Network Topology

## Slide 10
Lab 7: Router’s Configuration: WAN Interface.
To configure WAN Serial interface on Router 1, Type the following commands:
PC>telnet 192.168.1.1 Password:
Router1>ena Password:
Router1#conf t
Router1(config)#interface serial 0/0/0 Router1(config-if)#ip add 172.16.0.1 255.255.0.0 Router1(config-if)#no sh
Router1(config-if)#clock rate 64000
Router1(config-if)#encapsulation ppp
Router1(config-if)#exit
Router1#show start Router1#show run Router1#write
DIY Task: Using same commands configure the other Serial interfaces.

## Slide 11
Lab 8
: Static Routing Configuration
The following configuration commands enable static routing in Router1 and Router2. To Enable Static Routing, add only indirectly connect networks to router.
Router1:
Router1(config)#ip route 192.168.2.0 255.255.255.0 ser 0/0/0
Router1(config)#do show ip route
….
C 172.16.0.0/16 is directly connected, Serial0/0/0
C 172.16.0.2/32 is directly connected, Serial0/0/0
C 192.168.1.0/24 is directly connected, FastEthernet0/0
S 192.168.2.0/24 is directly connected, Serial0/0/0
….
Router2:
Router2(config)#ip route 192.168.1.0 255.255.255.0 ser 0/0/0
Router2(config)#do show ip route
….
C 172.16.0.0/16 is directly connected, Serial0/0/0 C 172.16.0.1/32 is directly connected, Serial0/0/0
S 192.168.1.0/24 is directly connected, Serial0/0/0
C 192.168.2.0/24 is directly connected, FastEthernet0/0
….
To check network connectivity between PCs on Lab1 and Lab2 using ping command
ping 192.168.2.10
tracert 192.168.2.10
To remove static routing on any router use “No”, for example
Router1(config)# no ip route 192.168.1.0 255.255.255.0 ser 0/0/0
DIY Task: Enable Static Routing in all Routers.

## Slide 12
Lab 9: RIP Configuration
The following configuration commands enable dynamic routing protocol RIP version 2 in both Router1 and Router2.
To Enable RIP, advertise only directly connect networks in each router.
Router1:
Router1(config)#router rip
Router1(config-router)#version 2
Router1(config-router)#network 192.168.1.0
Router1(config-router)#network 172.16.0.0 Router1(config-router)#exit
Router1(config)#do sh run Router1(config)#do sh ip route
…
R 192.168.2.0/24 [120/1] via 172.16.0.2, 00:00:02, Serial0/0/0
…
Router2:
Router2(config)#router rip
Router2(config-router)#version 2
Router2(config-router)#network 192.168.2.0
Router2(config-router)#network 172.16.0.0 Router2(config-router)#exit
Router2(config)#do sh run Router2(config)#do sh ip route
…
R 192.168.1.0/24 [120/1] via 172.16.0.1, 00:00:02, Serial0/0/0
…
To check network connectivity between PCs on Lab1 and Lab2 using ping command
DIY Task: Enable RIP in all Routers.

## Slide 13
Lab 10: OSPF Configuration
The following configuration commands enable dynamic routing protocol OSPF in both Router1 and Router2.
To Enable OSPF, advertise only directly connect networks in each router and using
wildcard mask with area.
Router1:
Router1(config)#router ospf 1
Router1(config-router)#network 192.168.1.0 0.0.0.255 area 0
Router1(config-router)#network 172.16.0.0 Router1(config-router)#exit Router1(config)#do sh run Router1(config)#do sh ip ospf neighbor Router1(config)#do sh ip route
…
0.0.25.255 area 0
O 192.168.2.0/24 [110/65] via 172.16.0.2, 00:02:16, Serial0/0/0
…
Router2:
Router2(config)#router ospf 1
Router2(config-router)# network 192.168.2.0
Router2(config-router)# network 172.16.0.0 Router2(config-router)#exit Router2(config)#do sh run Router2(config)#do sh ip ospf neighbor Router2(config)#do sh ip route
…
0.0.0.255 area 0
0.0.25.255 area 0
O 192.168.1.0/24 [110/65] via 172.16.0.1, 00:00:02, Serial0/0/0
…
To check network connectivity between PCs on Lab1 and Lab2 using ping command
DIY Task: Enable OSPF in all Routers.

## Slide 14
Lab 11: EIGRP Configuration
The following configuration commands enable dynamic routing protocol EIGRP in both Router1 and Router2.
To Enable EIGRP, advertise only directly connect networks in each router using
autonomous system number.
Router1:
Router1(config)#router eigrp 1
Router1(config-router)#network 192.168.1.0
Router1(config-router)#network 172.16.0.0
Router1(config-router)#exit Router1(config)#do sh run Router1(config)#do sh ip eigrp neighbor Router1(config)#do sh ip route
…
D 192.168.2.0/24 [90/2172416] via 172.16.0.2, 00:00:31, Serial0/0/0
…
Router2:
Router2(config)#router eigrp 1
Router2(config-router)# network 192.168.2.0
Router2(config-router)# network 172.16.0.0 Router2(config-router)#exit Router2(config)#do sh run Router2(config)#do sh ip eigrp neighbor Router2(config)#do sh ip route
…
D 192.168.1.0/24 [90/2172416] via 172.16.0.1, 00:00:45, Serial0/0/0
…
To check network connectivity between PCs on Lab1 and Lab2 using ping command
DIY Task: Enable EIGRP in all Routers.

## Slide 15
Lab 12: ACL
Standard Access Control List
Scenario: configure an ACL on Router2 such that PC1 (192.168.1.11) should not communicate with Lab2 Network (192.168.2.0).
Before configuring ACL check network connectivity between PC1 and Lab2 network.
Router#conf t
Router(config)#access-list 1 deny 192.168.1.11 0.0.0.0
Router(config)#access-list 1 permit any
Router(config)#int fa 0/0
Router(config-if)#ip access-group 1 out
Router(config-if)#exit
Router(config)# do show ip access-list
To test ping from PC1 to any PC in Lab2.
DIY Task: Lab 1 network could not communicate with Lab 2 only.

## Slide 16
Extended Access Control List
Scenario: configure an ACL on Router2 such that PC1 (192.168.1.11) should not access only HTTP Server in Lab2 Network (192.168.2.0).
Before configuring ACL, add an HTTP server and then check HTTP access between PC1 and Lab2 HTTP server.
Router#conf t
Router(config)#access-list 100 deny tcp 192.168.1.11 0.0.0.0 192.168.2.2 0.0.0.0 eq 80
Router(config)#access-list 100 permit ip any any
Router(config)#int fa 0/0
Router(config-if)#ip access-group 100 out Router(config-if)#exit
Router(config)# do show ip access-list Router(config)# do show ip int fa 0/0
To test first ping from PC1 to HTTP server and then accessing HTTP server.
DIY Task: Only PC1 could access with Lab 2 HTTP Server.

## Slide 17
Lab 13:
Using CDP
CDP is enabled by default on all Cisco devices. It is used for troubleshooting connectivity between Cisco devices. To check output of CDP use the following commands.
To enable CDP:
Router(config)#cdp run
To show CDP setting:
Router(config)#do show cdp
To show directly connected devices:
Router(config)#do show cdp neighbor Router(config)#do show cdp neighbor detail
Backup and Restore IOS and Configuration
To backup and restore Cisco IOS and configuration (start and run) follow the procedure below:
First install and configure a TFTP server.
To backup startup configuration:
Router2#copy startup-config tftp:
Address or name of remote host []? 192.168.2.2 Destination filename [Router-confg]? kanyconfig Writing startup-config...!!
[OK - 1006 bytes]
1006 bytes copied in 0.082 secs (12268 bytes/sec)
To backup IOS configuration: Router2#show flash Router2#copy flash: tftp:

## Slide 18
Source filename []? c1841-advipservicesk9-mz.124-15.T1.bin
Address or name of remote host []? 192.168.2.2
Destination filename [c1841-advipservicesk9-mz.124-15.T1.bin]? KanyRouter2IOS
Writing c1841-advipservicesk9-mz.124- 15.T1.bin...!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!
!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!
!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!
!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!
!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!
!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!
!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!
[OK - 33591768 bytes]
33591768 bytes copied in 0.795 secs (4436474 bytes/sec)
DIY Task: Restore Startup configuration and IOS from TFTP Server to Router2.
Password Recovery/Reset
Do the following steps to reset the password of Cisco Router.
Interrupt the boot sequence by Ctrl+ Break or Ctrl + C.
type Confreg 0x2142. 3.type reset.
Press No , enable .
Copy startup-config file running-config.
Set Enable secret Kany2018.
Apply “No Shutdown” to all interfaces.
type config-register 0x2102.
type Write.
type Reload.

## Slide 19
VTP Configuration.
To share VLAN database between switches using the following commands in each switch:
To Configure:
Switch(Config)# VTP domain kany Switch(Config)# VTP mode server
Switch(Config)# VTP password k@2017
To Verify:
Switch# show vtp status
Switch# show vtp password Switch# show vlan

## Slide 20
Lab 14: IPV6
To Assign IPv6 address: Router(Config)#interface fa 0/0 Router(Config)#ipv6 2001:1::1/64
To Enable IP6 Routing:
Router(Config)#ipv6 unicast-routing
To enable IPv6 Static Routing:
Router(Config)#ipv6 route 2001:0::/64 2001:3::2
To Show IPv6 Routing Table:
Router#show ipv6 route