## Slide 1: Experiment- 2 Visible Spectrophotometric Determination of Aspirin

## Slide 2
The salicylate ions will form an intensely colored complex with the ferric ion in acidic solution.
The wavelength of maximum absorption for this complex is 530 nm

## Slide 3
Stock salicylate solution. Weigh 0.4 g of salicylic acid and place it into a beaker.
Add 10 mL of 1.0 M NaOH and heat the mixture until it dissolve. Cool and quantitatively transfer this solution to a 500-mL volumetric flask, and dilute to the mark with water.
A- Working solution ( 100ppm) in 25ml volumetric flask, and dilute to the mark with D.water

## Slide 4: C- Preparation of unknown Tablet Aspirin
Weigh an aspirin tablet on an analytical balance.
Place it in a clean 50 mL beaker and add 10 mL 0f 1.0 M NaOH.
Carefully crush the tablet with a stirring rod. Dissolve as much of the tablet as possible.
Heat the mixture to boiling.
Boil for five minutes and avoid splattering, washing down the sides of the flask with distilled water as needed.
Cool and quantitatively transfer this solution to a 500-mL volumetric flask, and dilute to the mark with D. water.

## Slide 5: B- Fe3+ (reagent): Add 6.8 g FeCl3.6H2O to 100 mL deionized water in a 250-mL beaker. Add 3.0 mL of concentrated HCl and 12.0 g of KCl. Dissolve and dilute to 1.0 L with deionized water.

## Slide 6
There is some Abs. vs. Conc. where graph is linear.
Avoid very high or low absorbencies when drawing a standard curve. The best results are obtained with 0.1 < A < 1
NEVER extrapolate beyond point known where becomes non-linear.

## Slide 7
Avoid very high or low absorbencies when drawing a standard curve.
The best results are obtained with 0.1 < A < 1

## Slide 8
What concentration do you think the unknown sample is?

## Slide 9
Calculate the weight of acetylsalicylic acid (ASA) in the aspirin tablet applying the appropriate stochiometric factors and considering the dilutions involved.
4. Calculate the percentage (w/w) of acetyl salicylic acid in aspirin tablet.