## Slide 1
Lecture 1 :
Introduction Communication System
1
by:basud mohammad rasool

## Slide 2: Communications
2
Communications
Transfer of information from one place to another. Should be efficient, reliable and secured.
“A communication system is a process of conveying information from a source to a destination”
Communication system Components/subsystems act together to accomplish information transfer/exchange
“An electronic communication system is transferring information using an electrical field as a mean of signal”

## Slide 3: Requirements
3
Rate of information transfer
  The rate of information transfer is defined as the amount of information that must be communicated from source to destination.
  It will determined the physical form and technique used to transmit and receive information and therefore determines the way system is designed and constructed
Purity of signal received
  The received signal must be the same as the transmitted signal

## Slide 4: Requirements
Simplicity of the system
  Any communication system must be convenient in order to be effective and efficient and easy to use
Reliability
  Users must be able to depend on a communication system. It must work when needed and transmit and receive information without errors or with an acceptable error.
4

## Slide 5: Elements of Communication system
Input Transducer
Transmitter
Channel
Receiver
Output Transducer
Input Message
Output Message
Transmission
medium
noise
5

## Slide 6: Elements of Communication system
6
 Input Transducer
To convert the message to a form suitable for the particular type of communication system.
Eg: Speech waves are converted to voltage variation by a microphone.
 Transmitter
Processes the input signal  to produce a transmitted signal that suited the characteristic of transmission channel.
eg: modulation, coding
Other functions performed: Amplification, filtering

## Slide 7: Elements of Communication system
 Channel (Transmission medium)
A medium that bridges the distance from source to destination.
eg: Atmosphere (free space), coaxial cable, fiber optic, waveguide
Signal undergoes degradation from noise, interference and distortion.
7

Transmission systems can be evaluated according to five (5) main criteria:
 Capacity  Performance
 Distance  Security
 Cost which include installation, operation and maintenance

## Slide 8: Elements of Communication system
The two main categories of channel commonly used are:
Line (conducted media)
  The channel is made up metallic cable (such as coaxial cable, twisted pair, parallel wires, and others) or fibre optic cable.
Free space or radiated media
  This is the medium where the transmission of signal is carried out by the propagation of electromagnet wave.
  The main applications are in radio broadcasting, microwaves and satellites transmission systems.
8

## Slide 9: Elements of Communication system
Loses in medium of transmission
  However, each medium introduces losses termed as attenuation, distortion and adds noise to some degree to the transmitted signal. The amount of attenuation, distortion and noise depends on the type of transmission medium used.
  There is normally no signal processing in the transmission medium, it is just the medium where the transmitter is connected to the receiver.
9

## Slide 10: Elements of Communication system
10
 Receiver
To extract the desired signal from the output channel and to convert it to a form suitable for the output transducer.
eg: Demodulation, decoding
Other functions performed:
Amplification, filtering.
 Output Transducer
Converts the electrical signal at its input into a form desired by the system used.
Eg: Loudspeaker, PC and tape-recorders.

## Slide 11: Losses in Communication System
Various unwanted undesirable effect crop up in transmissions
Attenuation
  Reduces signal strength at the receiver
Distortion
  Waveform perturbation caused by imperfect response of the system to the desired signal itself
  Equalizer can be used to reduced the effect
Interference
  Contamination by extraneous signals from human sources
11

## Slide 12: Losses in Communication System
Noise
  Random and unpredictable electrical signals from internal or external to the system
  The term SNR (signal to noise ratio) is used to measure performance (noise) relative to an information analog signal
  The term BER (Bit Error Rate) is used in digital system to measure the deterioration of the signal
12

## Slide 13: Analog vs. Digital
13
The signal can be analog or digital message:
Analog
  Continuous Variation
    Assumes the total range of frequencies/time
  All information is transmitted.
Digital
  Takes samples
    non-continuous stream of on/off pulses
  Translates to 1s and 0s

## Slide 14: Analog Vs Digital (Advantages and Disadvantages)
14
Digital CS Analog CS
Advantages:
Inexpensive
Privacy preserved (Data encrypt.)
Can merge different data
Error correction
Disadvantages:
Expensive
No privacy preserved
Cannot merge different data
No error correction capability
Disadvantages:
Larger bandwidth
Synchronization problem is relatively difficult.
Advantages:
Smaller bandwidth
Synchronization problem is relatively easier.

## Slide 15: Baseband vrs Modulated Signal
15
Baseband Signal
  Base band signal is the modulating signal/original information signal either in a digital or analog form (intelligent/message) in communication system
Example: voice signal (300Hz – 3400Hz)
  Transmission of original information whether analog or digital, directly into transmission medium is called baseband transmission.
Modulated Signal
  Modulated signal is baseband signal which its original frequency is shifted to higher frequency to facilitate transmission purposes

## Slide 16: Block Diagram of Modulation Process
MODULATION PROCESS
Baseband
16
signal
Modulated
signal
Carrier

## Slide 17: Baseband Transmission
17
The need of baseband transmission:
  The concepts and parameter of baseband transmission are used in modulated transmission
  Performance of baseband transmission is used as the standard for comparing modulation techniques
Baseband signal is not suitable for long distance communication because:
  Hardware limitation (eg: requires very long antenna)
  Interference with other waves

## Slide 18: Modulation
18
Modulation –
Process of changing baseband signals to facilitate
the transmission medium
Process of modulation
  Frequency translation such as AM, FM, PM etc
  Sampling and coding such as PAM, PCM etc
  Keying such as ASK, FSK etc

## Slide 19: Modulation
Types of modulation :
  Analogue modulations are frequency translation method caused by changing the appropriate quantity in a carrier signal
  Digital modulation is the result of changing analogue signal into binary ones by sampling and coding
  Keying modulations are digital signals subsequently modulated by the frequency modulation by using one or other analogue method
19

## Slide 20: Why Modulate?
20
Reduce noise and interference
  By using proper frequency where noise and interference are at minimum
  Increasing power is costly and may damage equipment
Frequency Assignment
  For TV and radio broadcasting, each station has a different assigned carrier
Multiplexing
  Combining several signals for simultaneous transmission on one channel by placing each signal on different carrier frequency

## Slide 21: Electromagnetic Frequency Spectrum
21
The electromagnetic frequency spectrum is divided into
 subsections, or bands, with each band having a different name and boundary
The International Telecommunications Union (ITU) is an international agency in control of allocating frequencies and services within the overall frequency spectrum

## Slide 22: Electromagnetic Frequency Spectrum
# Speed of electromagnetic wave = speed of light, c = 3.0x108 ms-1
f = freq
λ = wavelength
c  f
22
 In the United State, the Federal Communications Commission (FCC) assigns frequencies and communications services for free space radio propagation

## Slide 23
21/06/15
Communication System: Introduction Prof. Hendre V.S., TCOER, Pune
23

## Slide 24: Frequency allocation
If the transmission channel is the atmosphere,
interference and propagation are strongly dependent on the transmission frequency
On international basis, frequency assignment and technical standards are set by the ITU
There are three main sector that provides frequency assignment and is concerned with the efficient use of radio frequency spectrum



ITU(R)
ITU(T)
ITU(D)

## Slide 25: Frequency Bands
3 – 30 kHz 30 – 300 kHz 300 – 3000 kHz | VLF LF MF | (very low freq) (low freq) (medium freq) | Ground wave Ground wave Ground wave/sky wave | 
 |  |  | 3 – 30 MHz HF (high | 
freq) | Sky wave (Ionospheric) |  |  | 
30 – 300 MHz | VHF (very high freq) |  |  | Space wave (LOS)
300 – 3000 MHz | UHF (ultrahigh freq) |  |  | Space wave (LOS)
3 – 30 GHz | SHF (superhigh freq) |  |  | LOS/Satellite
30 – 300 GHz | EHF (Extremely high freq) |  |  | LOS/Satellite
International Telecommunications Union (ITU) Band Designation

## Slide 26: Frequency Bands
Frequency Bands
Letter Designation
1.0 – 2.0 GHz
2.0 – 4.0 GHz
4.0 – 8.0 GHz
L S C
8.0 – 12.0 GHz
12.0 – 18.0 GHz
18.0 – 27.0 GHz
27.0 – 40.0 GHz
26.5 – 40.0 GHz
X
Ku K
Ka R
Federal Communications Commission (FCC) Emission Classifications

## Slide 27: Frequency Bands
Frequency Bands
Letter Designation
Uses
33.0 – 50 GHz | Q | Radar/satellite comm
40.0 – 75.0 GHz | V | Radar/satellite comm
75.0 – 110 GHz | W | Radar/satellite comm
103 – 107GHz | Infrared, visible | Optical communication
light and ultra violet
Federal Communications Commission (FCC) Emission Classifications

## Slide 28: Radio Communication System
It is wireless communication system
The information is being carried by the electromagnetic waves, which is propagated in free space
Electromagnetic waves are waves that travel at the speed of light and made up of an electrical field and magnetic field at right angles to one another and to the direction of propagation

## Slide 29: Radio Communication System
Transmitter
Receiver
Transmitting antenna
Receiving antenna
Block diagram of a radio communication system

## Slide 30: Propagation Waves
There are three main type of propagations:
Ground wave propagation
  Dominants mode for frequencies below 2 MHz
  The movement tend to follow the contour of the earth with large antenna size
Sky-wave propagation
  Dominants mode for frequencies between 2 – 30 MHz range
  Coverage is obtained by reflection the wave at ionosphere and at the earth boundaries
  This is because the index refractions of the ionosphere
varies with the altitude as the ionization density changes

## Slide 31: Propagation Waves
There are areas of no coverage along the earth surface
between transmitting and receiving antenna
The angle of reflection and the loss of signal depend on the
frequency, time, season, activities of the sun etc
Space wave propagation (LOS)
  Dominants mode for frequencies above 30 MHz where in propagates in straight line
  No refraction and can almost propagates through ionosphere

## Slide 32: Propagation Waves
Sky-wave propagation
But the signal path has to be above horizon to avoid blocking leading antenna to be placed on tall towers
The distance to radio horizon is
d = √2h miles
Space-wave propagation
Ground-wave propagation

## Slide 33: Propagation Waves
 The three waves propagation methods:



Ground wave propagation Sky wave propagation Space wave propagation
Earth
Ionospheric layer
Sky wave propagation
Space wave propagation
Receiver
Transmitter
Fig: Radio wave propagation methods

## Slide 34: Propagation Waves
 Ground (surface) wave
 Wave that progress along the surface the earth

It follows the curvature of the earth
 Sky wave propagation
 Sky waves are those waves that radiated towards ionosphere. By a process of refraction and reflection, the receiver on the earth will receive the signal. The various layers of the ionosphere have specific effects on the propagation of radio waves

## Slide 35: Propagation Waves
 Space wave
 The wave is propagated in a straight line


space wave is limited in their propagation by the curvature of the earth
sometimes it is called direct wave or line-of-sight (LOS)
 The radio horizon of the antenna is the distance between the transmitter and receiver and is denoted by d,
where
in km
and and

## Slide 36: Propagation Waves
Receiver
Transmitter
Fig: Line of sight propagation
dt
dr
dt = radio horizon of the transmitting antenna, in km
ht = height of transmitting antenna, in m
dr = radio horizon of the receiving antenna, in km
hr = height of receiver antenna, in m
LOS propagation
d

## Slide 37: Satellite Communication
Satellite employs LOS radio transmission over very long distance
It offers brad coverage even across the ocean and can handle bulk of very long distance telecommunication
Satellite
uplink
down-link

## Slide 38: Historical Development
Year
1844
1876
1904
1923
1936
1962
1966
1972
Events Telegraph Telephone AM Radio Television FM Radio Satellite
Optical links using laser and fiber optics Cellular Telephone

## Slide 39: Historical Development
Year
1975
1975
1980
1981
1982
1985
1989
1990
1990-2000
Events
First digital telephone switch
Wideband communication system (cable TV etc) Compact disc is developed by Philip & Sony
FCC adopts rules for commercial cellular telephone Internet is used to replace ARPANET
Fax machines widely available in offices
First SONET standard optical fiber products released WWW becomes part of the internet
Digital communication system (ISDN, BISDN, HDTV, handheld computers, digital cellular etc Global
telecom system

## Slide 40: Power Measurement (dB, dBm)
The decibel (dB) is a transmission-measuring unit used to express gain and losses an electronic devices and circuits
for describing relationship between signal and noise
  dB  1W
  dBm  1mW
 example: 100W = 10 log10 100 = 2dB
= 10 log10 100 = 50 dBm
1mW

## Slide 41: Power Measurement (dB, dBm)
 If two powers are expressed in the same unit (eg: watts or microwatts), their ratio is a dimensionless quantity that can be expressed in decibel form as follows:
)
2
10
P
P1
dB  10 log (
Where P1 = power level 1 (watts) P2 = power level 2 (watts)
The dB value is the difference in dB between P1 and P2

## Slide 42: Power Measurement (dB, dBm)
 When used in electronic circuits to measure a power gain or loss, that equation can rewritten as
in
P
( Pout )
Gain (dB) 10 log10
Where
Gain (dB) = power gain (dB)
Pout Pin
= output power level (watts)
= input power level (watts)

in
P
Pout
absolute power
(+) dB - power gain
  output power is greater than input power
(-) dB power loss
  output power is less than input power

## Slide 43: Examples
Convert the absolute power ratio of 200 to a power gain in dB
Solution:
Power gain, Ap (dB) = 10 log10 [200]
= 10(2.3)
= 23 dB
Convert the power gain Ap = 23 dB to an absolute power ratio
Solution
Power gain, Ap (dB) = 10 log10 [Pout/Pin]
2.3 = log10 [Pout/Pin]
[Pout/Pin]
= antilog 2.3
= 200

## Slide 44: Examples
3. Convert a power level of 200mW to dBm
Solutuion:
dBm = 10 log10 [200mW/1mW]
= 10(200)
= 23 dBm

## Slide 45: Limitation in a Communication System
There are two categories of limitations:
 Technological constraint




Equipment ability Economy and cost factor
National and international law and agreement as well as standardization (such as ITU etc)
Interaction with existing system
 Physical constraint

Bandwidth


The difference between the upper frequency and lower frequency of the signal or the equipment operation range
Noise

Any unwanted electrical energy present in the usable passband of a communication circuit

## Slide 46: Communication System Chart
Communication System
Continuous Wave
Digital Wave
Amplitude Modulation (AM)
Pulse Modulation (PM)
Angle Modulation
Frequency Modulation (FM)
Analogue Pulse Modulation
Digital Pulse Modulation