## Slide 1: Lecture-3
Internal Loadings Developed in Structural Members
Internal Loadings at a Specified Point
Sign Convention
Shear Force and Bending Moment Functions
Shear and Moment Diagrams for a Beam
Shear and Moment Diagrams for a Frame
Moment Diagrams Constructed by the Method of Superposition
Qualitative Deflected Shapes

## Slide 2
Unlike trusses, considered in the preceding chapter, whose members are always subjected to only axial forces, the members of rigid frames and beams may be subjected to shear forces and bending moments as well as axial forces under the action of external loads. The determination of these internal forces and moments (stress resultants) is necessary for the design of such structures. The objective of this chapter is to present the analysis of internal forces and moments that may develop in beams, and the members of plane frames, under the action of coplanar systems of external forces and couples.
Internal Loadings Developed in Structural Members

## Slide 3
Before a structural member can be proportioned, it is necessary to determine the force and moment that act within it. In this chapter we will develop the methods for finding these loadings at specified points along a member's axis and for showing the variation graphically using the shear and moment diagrams. Applications are given for both beams and frames.

## Slide 4: Internal Loadings at a Specified Point
The internal load at a specified point in a member can be determined by using the method of sections. In general, this loading for a coplanar structure will consist of a normal force N, shear force V, and bending moment M. It should be realized, however, that these loadings actually represent the resultants of the stress distribution acting over the member's cross-sectional area at the cut section. Once the resultant internal loadings are known, the magnitude of the stress can be determined provided an assumed distribution of stress over the cross-sectional area is specified.

## Slide 5: Sign Convention
The positive normal force tends to elongate the segment, positive shear tends to rotate the segment clockwise, and positive bending moment tends to bend the segment concave upward, so as to "hold water."

## Slide 6: Internal loadings at a cross section
Sign
Convention
+
-
+x
+y
Coordinates
M
V
N
M
V

## Slide 7: Example
Sign
Convention
+
-

## Slide 8
The design of a beam requires a detailed knowledge of the variations of the internal shear force V and moment M acting at each point along the axis of the beam. The internal normal force is generally not considered for two reasons: (1) in most cases the loads applied to a beam act perpendicular to the beam's axis and hence produce only an internal shear force and bending moment, and (2) for design purposes the beam's resistance to shear, and particularly to bending, is more important than its ability to resist normal force.
An important exception to this occurs, however, when beams are subjected to compressive axial forces, since the buckling or instability that may occur has to be investigated.
Shear and Moment Functions

## Slide 9
The variations of V and M as a function of the position x of an arbitrary point along the beam's axis can be obtained by using the method of sections discussed in previous section. Here, however, it is necessary to locate the imaginary section or cut at an arbitrary distance x from one end of the beam rather than at a specific point.

## Slide 10: Force, Shear and Bending Moment
+
M+dM
V+dV
V
M
dx
VC
VD
C
D

## Slide 11: Force, Shear and Bending Moment
V-P
V
dx
P
Shear force moves toward
negative direction
+
M-Mo
M
dx
Mo
Moment moves toward
Negative direction
x
V
V-P
P
x
Mo
M-Mo
M

## Slide 12: Shear Force & Bending Moment Diagram
L/2
L/2
V
+P/2
-P/2
M
+PL/4
Need to know deflection shape qualitatively
curvature
+M
-M

## Slide 13: Shear Force & Bending Moment Diagram
Structure under loads
Qualitative deflection shape
Bending moment diagram
Shear force diagram
Bending moment diagram
(plotted on the compression side)
Slope of V = load
Slope of M = V

## Slide 14: Shear & Moment Diagrams for a Beam
Sign
Convention
+
-

## Slide 15: Example

## Slide 16: PROCEDURE FOR ANALYSIS
Support Reactions
Before the member is "cut" or sectioned, it may be necessary to determine the member's support reactions so that the equilibrium equations are used only to solve for the internal loadings when the member is sectioned.
If the member is part of a pin-connected structure, the pin reactions can be determined using the equations of equilibrium.

## Slide 17
Free-Body Diagram
Keep all distributed loadings, couple moments, and forces acting on the member in their exact location, then pass an imaginary section through the member, perpendicular to its axis at the point where the internal loading is to be determined.
After the section is made, draw a free-body diagram of the segment that has the least number of loads on it. At the section indicate the unknown resultants N, V, and M acting in their positive directions.

## Slide 18
Equations of Equilibrium
Moments should be summed at the section about axes that pass through the centroid of the member's cross-sectional area, in order to eliminate the unknowns N and V and thereby obtain a direct solution for M.
If the solution of the equilibrium equations yields a quantity having a negative magnitude, the assumed directional sense of the quantity is opposite to that shown on the free-body diagram.

## Slide 19
Shear and Moment Functions
The horizontal members on this power line support frame were designed once the shear and moment within the members were established.
Specify separate coordinates x and associated origins, extending into regions of the beam between concentrated forces and/or couple moments, or where there is a discontinuity of distributed loading.
Section the beam perpendicular to its axis at each distance x, and from the free-body diagram of one of the segments determine the unknowns V and M at the cut section as functions of x. On the free-body diagram, V and M should be shown acting in their positive directions, in accordance with the sign convention given in Fig. 4-1.
V is obtained from ΣFy = 0 and M is obtained by summing moments about the point S located at the cut section, ΣMS = 0.
The results can be checked by noting that dM/dx = V and dV/dx = w, where w is positive when it acts upward, away from the beam. These relationships are developed in next Sec.

## Slide 20
Since beams are used primarily to resist bending stress, it is important that the moment diagram accompany the solution for their design. In previous Sec. the moment diagram was constructed by first drawing the shear diagram. If we use the principle of superposition, however, each of the loads on the beam can be treated separately and the moment diagram can then be constructed in a series of parts rather than a single and sometimes complicated shape. It will be shown later in the text that this can be particularly advantageous when applying geometric deflection methods to determine both the deflection of a beam and the reactions on statically indeterminate beams.
Moment Diagrams Constructed by the Method of Superposition

## Slide 22
Software

## Slide 23: Example
Draw shear force and bending moment diagrams

## Slide 24: Solution
9m

## Slide 25: QUALITATIVE DEFLECTED SHAPES
A qualitative deflected shape (elastic curve) of a structure is simply a rough (usually exaggerated) sketch of the neutral surface of the structure, in the deformed position, under the action of a given loading condition.
According to the sign convention, a positive bending moment bends a beam concave upward (or toward the positive y direction), whereas a negative bending moment bends a beam concave downward (or toward the negative y direction). Thus, the sign (positive or negative) of the curvature at any point along the axis of a beam can be obtained from the bending moment diagram.

## Slide 30: Internal Hinges

## Slide 31: 2 hinges

## Slide 32: 3 hinges

## Slide 33: Closed Loop