## Slide 1
Abrasive Water Jet process
Prepared by:
Dr: Gawhar Ibraheem Khidhir
2-May-2023

## Slide 2: Content
Introduction
Working Principle
AWJ system components
Process parameters
Applications
Advantages & disadvantages
References

## Slide 3: Introduction Abrasive Water Jet machining is a non traditional machining process. abrasive particles must usually be added to the jet stream to facilitate cutting . It is based on the principle of water erosion.
uses a fine, high-pressure, high-velocity stream of water directed at the work surface to cause cutting of the work, as illustrated in Fig.1. To obtain the fine stream of water a small nozzle opening of diameter 0.1 to 0.4 mm is used. To provide the stream with sufficient energy for cutting, pressures up to 400MPa are used, and the jet reaches velocities up to 900 m/s . The fluid is pressurized to the desired level by a hydraulic pump. The nozzle unit consists of a holder made of stainless steel, and a jewel nozzle made of sapphire, ruby, or diamond. Diamond lasts the longest but costs the most.
Important process parameters include standoff distance, nozzle opening diameter, water pressure, and cutting feed rate.
Size of the nozzle orifice affects the precision of the cut; smaller openings are used for finer cuts on thinner materials. To cut thicker stock, thicker jet streams and higher pressures are required.
The cutting feed rate refers to the velocity at which the WJC nozzle is traversed along the cutting path. Typical feed rates range from 5 mm/s to more than 500 mm/s, depending on work material and its thickness.
Fig.1 Water jet cutting.