## Slide 1
ENGINEERING DRAWING & DESCRIPTIVE GEOMETRY
Syllabus
References
1- FUNDAMENTALS OF ENGINEERING DRAWING by: Warren J. Luzadder
2- TECHNICAL DRAWING by: Goetsch nelson chalk
3- الــــرســــــــــــــــــــم الهندســـــــــــــــي د. فتحي شريف
4- الــــرســــــــــــــــــــم الهندســــــــــــــي كتاب منهجـــي
5- DESCRIPTIVE GEOMETRY by: Yousif Nicola
  Chapter One : Projections
  Chapter Two : Sectional views
  Chapter Three : Pictorial Drawing
  Chapter Four : Descriptive geometry

## Slide 2
4.1 : INTRODUCTION
    Projection is a method to represent the exact shape of an
    Object on the plane.
4.2 : PROJECTION TYPE
The two main type of the projection are ( Perspective projection and
Orthographic projection )
4.2.1 : PERSPECTIVE PROJECTION
  In Perspective projection , the
  Projecting line or visual rays converge
  At a point.
O
A
B
C
D
A’
B’
C’
D’
Projection plane
Projecting line
Chapter ONE : PROJECTIONS

## Slide 3
4.2.2 : ORTHOGRAPHIC PROJECTION
  Orthographic projection or parallel
  Projection is the projection system that
  Engineers use for manufacturing and
  Construction drawings, In which the
  Projecting lines are parallel and
  perpendicular to the projection plane.
A’
B’
C’
D’
Projection plane
Projecting line
A
B
C
D
4.3 : PROJECTION PLANES
  1- Horizontal Plane (H.P):
  The projection on the Horizontal Plane called --------------- TOP VIEW (T.V)
  2- Vertical Plane (V.P):
  The projection on the Vertical Plane called --------------- FRONT VIEW (F.V)
  3- Profile Plane (P.P):
  The projection on the Profile Plane called --------------------SIDE VIEW (S.V)

## Slide 4
FV
TV
SV

## Slide 5
30
15
50
60
30
30
15
30
30
25
R20
20
20
450
FV
TV
SV