## Slide 1: Geochemistry Geochemical Exploration
*Geochemistry in Mineral Exploration, 2nd Edition, 1981, New York
By: Ross A. W., Hawkes H. E. and Webb J. S.
*Introduction to Exploration Geochemistry, 2nd Edition, 1980, USA
By: Levinson A. A.
*Essentials of Geochemistry, 2nd Edition, 2010, Jones and Bartlent
By: Walther J. V.

## Slide 2: Week (1): Geochemistry in mineral exploration - geochemical environments, dispersion and mobility. Week (2): Geochemical reactions – dispersion of elements under deep- seated conditions. Week (3): Association of elements – mobility under surficial conditions. Week (4): Epigenetic anomalies in bedrocks. Week (5): Mechanical and biological dispersion in the surficial environment. Week (6): Surficial dispersion patterns – soil formation. Week (7): First midterm exam. Week (8): Anomalies in residual and transported overburden. Week (9): Anomalies in natural waters. Week (10): Anomalies in drainage sediments – geochemical drainage surveys. Week (11): Vegetations surveys. Week (12): Volatiles and airborne particulates. Week (13): Geochemical thermodynamics: fundamental principles and phase equilibria. Week (14): Second midterm exam. ??

## Slide 3: Geochemistry is concerned with: 1. The determination of the relative and absolute abundance of the elements in the earth. 2. The study of the distribution and migration of the individual elements in the various parts of the earth with the object of discovering principles governing this distribution and migration. 3. The application of geochemical principles and information in solving human needs.

## Slide 4: The object of geochemistry is to define a geochemical anomaly which distinguishes an ore deposit from background and insignificant mineralization.

## Slide 5: Pressure, temperature, and the availability of the most abundant chemical components are the parameters of the geochemical environment that determine which mineral phases are stable.
Geological and geochemical processes fall into two groups, those that take place at or near to the Earth's surface (surface processes) and those that take place at depth within the Earth (internal processes).

## Slide 6: Geochemical Cycle Geologically and geochemically the Earth constitutes a dynamic system consisting of two major environments: Deep seated (Primary) & Surficial (Secondary) They have gross differences in pressure, temperature and chemistry, which can be represented by the: Geochemical Cycle

## Slide 7: The primary (deep-seated) environment extends downward from the lower levels of circulating meteoric water to the deepest level of the crust and may extend into the mantle. It is an environment of high T and P, restricted circulation of fluids, and relatively low free-O2 content.

## Slide 8: The secondary (surficial) environment is the environment of weathering, erosion, and sedimentation at the surface of the Earth. It is characterized by low -T, nearly constant low pressure, free movement of solutions, and abundant free oxygen, water, and carbon dioxide.

## Slide 9: Elements Associate with certain phases: Siderophile (Fe) Chalcophile (S) Lithophile (Si) Atmophile (gas) Biophile (organic) Distributions in the natural environment are influenced by an element’s fundamental chemical characteristics.

## Slide 10
Dissolved oxygen and hydrogen sulfide species are very useful because:
1. They are very strongly tied to redox reactions.
2. Their concentrations have very major effects on organisms.
3. They exert a major amount of control on the formation of
authigenic minerals.
4. They cannot coexist.
5. Bacteria divide neatly into aerobes and anaerobes.

## Slide 11: In Oxic Environment
15O2 (aq) + 4FeS2 + 8H2O »» 2Fe2O3 + 8SO42– + 16H+
O2 (aq) + 4FeCO3 »» 2Fe2O3 + 4CO2
O2 (aq) + MnS »» MnO2 + S
Oxygen + Sulfides »» CO2 + SO42– + Metal oxides

## Slide 12: For an Anoxic-sulfidic Environment
3H2S (aq) + S + Fe2O3 »» 2FeS2 + 3 H2O
H2S (aq) + S + FeCO3 »» FeS2 + CO2 + H2O
2H2S (aq) + MnO2 »» MnS + S + 2H2O
H2S (aq) + MnO2 + CO2 »» MnCO3 + S + H2O
H2S + Oxides »» Sulfides ± Carbonates

## Slide 13: Consider a water-sediment interface at pH 7. *If there is not much sulfur present, then Fe2+ predominates at -----?---- Eh. (high or low) *If there are free Fe2+ and Mn2+ in the pore water, then the system is -----?---- (anoxic or oxic).

## Slide 14: Geochemical / *Background Normal element abundance level in unmineralized earth material which usually is a range rather then an absolute value. ---------- Any departure from the normal range, positive or negative, is viewed as *anomalous. ---------- *Thresholds

## Slide 15: *Target and *Pathfinder Elements (Indicator) Use is frequently made of target elements-Indicator (i.e. Au). In some instances these elements may not be particularly effective. In these cases attention is directed to pathfinder elements (As, Hg, Sb) which may not be the target metal but have geochemically useful features (immobility, mobility, easier or cheaper analysis, better detection limits, etc).

## Slide 16: *Geochemical dispersion The process, in which atoms and particles move to new locations and geochemical environments, is called geochemical dispersion.
Mobile phase
Immobile phase
Transport
Dispersion pattern
Matrix
Environment of
mobilization
Environment of
deposition

## Slide 17: Dispersion may be the effect of exclusively mechanical agencies, such as: the injection of magma or the movement of surficial material by glacial action