## Slide 1
Experiment (3).
Gravimetric Determination of Chloride (Cl-) as Silver Chloride (AgCl) by Precipitation Method

## Slide 2
The aqueous solution of the chloride is acidified with nitric acid and a slight excess of silver nitrate solution is added, whereupon silver chloride is precipitated.
NaCl + AgNO3 AgCl + NaNO3
The precipitate, which is initially colloidal, is coagulated by heating the solution and stirring the suspension vigorously.

## Slide 3
AgNO3 + NaCl NaNO3
+ AgCl
Precipitate

## Slide 5
Silver chloride (AgCl) has solubility in water of 1.4mg/L at 20°C, and 21.7 mg/L at 100 °C. The solubility is less in the presence of very dilute nitric acid (HNO3), and is very much less in the presence of moderate concentrations of silver nitrate (AgNO3).

## Slide 6
Notes:
1- The sample solution was acidified in order to prevent the precipitation of other silver salt such as phosphate and carbonate, or formation of insoluble AgOH in alkaline medium.

## Slide 7
2- The formed ppt. is sensitive to the light.
2AgCl(s) light 2Ag(s) + Cl2(aq)
The results will be (-ve error) due to the removal of Cl- from the ppt. In the absence of excess silver nitrate (AgNO3).
But causes (+ve error) in the presence of excess silver nitrate (AgNO3), because the chlorine (Cl2) changed back to ppt. (AgCl), which cause further precipitation of silver chloride according to this reaction:
2AgCl(s) light 2Ag(s) + Cl2(aq)
3Cl2(aq) + 3H2O + 5AgNO3 5AgCl(s) + HClO3 + 5HNO3

## Slide 8
3- The precipitant agent was added slowly with constant stirring, to prevent local high concentration of the ppt.
4- 10% excess of the real volume of AgNO3 was added to decrease the solubility of silver chloride by common-ion effect.
AgCl Ag+ + Cl-
AgNO3 Ag+ + NO3-
Common ion

## Slide 9
5- When a very slight excess than 10% of silver ion was added then the solubility of silver chloride increase due to formation of the soluble complex cations:
AgCl(s) + Ag+(excess) Ag2Cl+(aq)
Ag2Cl+ + Ag+(excess) Ag3Cl++(aq)

## Slide 10
6- The ppt. was washed with 0.01M HNO3 (dilute), not higher concentration because the solubility of AgCl is greater in the stronger HNO3.
7- Solubility of AgCl is increased by increasing temperature therefore it is filtered at room temperature.
8- Precipitant agent (AgNO3) is light sensitive, therefore it must be protect from the light.
2AgNO3 light 2Ag(s) + 2NO2 + O2

## Slide 11
Procedure: