## Slide 1
Q.1// Fill the following blanks with suitable word or statements:
i) Detector convert radiant energy into an electrical signal.
ii) Example for radiation absorption is photometry.
iii)The use of a specific type of instrument for analysis is technique.
iv) The measured property proportional to concentration of analyte is called quantitative analysis.
v) Instrumental analyses are more sensitive and selective than volumetric and gravimetric methods, but they may be less accurate.

## Slide 2
Question bank (Cont.)
Q.2// Fill the following blanks with suitable word or statements:
a- The term precision is used to describe the reproducibility of the results.
b- Precision can be detected by standard deviation or relative standard deviation.
c- Accuracy is refers to the closeness of the results to true value.
d- Accuracy express in terms of relative error or recovery.

## Slide 3: Question bank
Q.3// To what region of the electromagnetic spectrum does each of the following belong?
i) 450 nm; ii) 200 nm; iii) 1000 cm; iv) 1 m; v) 10 Å; vi) 3000 nm.
Ans. 3) i) Visible region; ii) UV-region; iii) radio; iv) micro; v) x-ray; vi) I.R. (infra-red).
Q.4// What kind of electrons in the molecule directly takes part in absorbing for:
i) Visible; ii) U.V.; and iii) x-ray radiations?
Ans. 4) i) valence electron; ii) valence electron; iii) core electron (inner electron).

## Slide 4: Question bank
Q.5// Choose the correct answer from the following: (Correct answer shown in Bold)
1) Spectrofluorometer is more sensitive than spectrophotometer, because:
a) Spectrofluorometer has a filter as wavelength selector.
b) Spectrofluorometer has a tungsten lamp.
c) Spectrofluorometer can be used for determination of organic species only.
d) Non of them.
Q.6// Which one is more sensitive? Explain why?
Spectrophotometers or photometers.
Ans. Spectrophotometer is more sensitive than photometer; because the wavelength selector is very selective which is either prism or grating.
Q.7// Distinction between: photometer and pectrophotometer.
Ans. Photometer: used filter as wavelength selector.
Spectrophotometer: used monochromators instate of filters as wavelength selector.

## Slide 5
Question bank
Q.8// Fill the following blanks with suitable word or statements:
1- The most common source of U.V. radiation is either: xenon lamp or mercury lamp or hydrogen lamp.
2- Wavelength selectors will be used for improving selectivity.
3- Monochromators are either prism or grating.
4- The most common source of visible radiation is: tungsten.
5- The types of filters (as wavelength selector) are: 1- glass; 2- interference filter.
6- The sources of I.R. radiation is either glober (SiC) or nernest glower.
Q.9// Which one is more sensitive? Explain why?
i) Photo tube or photomultiplier tube as detector.
Ans. Photomultiplier tube is more sensitive than photo tube; due to have many dynodes.

## Slide 6
Question bank
Q.10// State the true or false from the following and correct the false: (Cont.)
1- U.V. and Vis-spectrophotometry have somewhat limited application for qualitative analysis because deviation occurs in Beer’s law.
Ans. False; because the number of absorption maxima and minima are relatively few.
2- If the radiation includes two wavelengths (λ1 & λ2) the Beer’s law is apply for each independently; if Є1 > Є2, the relation between A and C is normal straight relation.
Ans. False; if Є1 = Є2.
Q.11// How can you solve the following problems Use necessary diagrams, graphs and equations:
a) Un-selectivity of a spectrophotometric reagents?
Ans. solve by controlling the pH.
b) Deviation from the Beer’s law?
Ans. solve by using double beam spectrophotometric instrument.

## Slide 7: Questions?
Q. 12// Which of the following pairs of compounds is likely to absorb radiation at the longer wavelength?
1) acetone (CH3COCH3) or 2-butanone (CH3COCH2CH3)?
Ans. Give similar spectra in shape and intensity.
2) benzene (C6H6) or naphthalene (C10H8)?
Ans. Naphthalene have increased conjugation and so absorb at longer wavelengths than benzene.
3) CH3CH2COOH or CH2 = CHCOOH?
Ans. CH2 = CHOOH has absorb radiation at the longer wavelength due to the double bonds.
4) CH3CH2CNS or SNCCH2CH2CH2CNS
Ans. Absorption maximum due to the CNS group occurs at 245 nm with ɛ of 800 (1st molecule), in the 2nd molecule גmax = 247 nm with ɛ=2000

## Slide 8: Questions? Home work
Which of the following pairs of compounds is likely to absorb radiation at the longer wavelength?
1) CH2CH=CHCH=CHCH3 or CH3C≡C-C≡CCH3
2) C6H5OCH3 or C6H5CH3

## Slide 9: Question bank
Q.13// Explain why I.R. spectroscopy is mostly useful for qualitative analysis?
Ans. Because I.R. has many spectra bands, and the slit is wider.

## Slide 10: Question bank
Q.14// How can you solve the following problems Use necessary diagrams, graphs and equations:
A) Non- rigidity in fluorimetric analysis?
Ans. Non-rigidity solve by complexation with metal ions.
B) Non- fluorescent behavior of some compounds.
Ans. solve by increasing the rigidity of the compound.
Q.15// State the true or false from the following and correct the false:
1- Spectrophotometer is more sensitive than spectrofluorometer.
Ans. False; spectrofluorometer is more sensitive than Spectrophotometer;
or Spectrophotometer is less sensitive than spectrofluorometer.

## Slide 11: Question bank
Q.16// Choose the correct answer from the following: (Correct answer shown in Bold)
1) Chemiluminesence reaction between sulfur dioxide and oxygen atoms are a suitable example of:
a) Gas-phase CL. b) Liquid-phase CL.
c) Solid-phase CL. d) Non of them.
2) Chemiluminescence is:
a) the production of light due to biological reaction.
b) the production of light due to chemical reactions.
c) the production of gases from atmosphere.
d) non of them.
3) Determination of nitrogen oxides bases on the reaction with ozone is:
a) an example of liquid-phase CL. b) an example of solid-phase CL.
c) an example of gas-phase CL. d) non of them.
4) Chemiluminesence reaction between luminol and hydrogen peroxide in basic medium are a suitable example of:
a) Liquid-phase CL. b) Solid-phase CL.
c) Gas-phase CL. d) Non of them.

## Slide 12: Question bank
Q.17// State the true or false from the following and correct the false:
1- Turbidimetric or nephelometric methods are widely used in the analysis of water.
Ans. True
2- Turbidimetry is more sensitive than Nephelometry.
Ans. False, Nephelometry is more sensitive than turbidimetry.

## Slide 13: Question bank
Q.18// How can you solve the following problems Use necessary diagrams, graphs and equations:
A) Spectral interference in atomic emission spectrophotometer (AES)?
Ans. solve by using AAS because for each element use HCL.
B) Low selectivity of AES due to the chemical interferences.
Ans. solve by adding releasing agent.
C) Ionization in atomic spectroscopy?
Ans. solve by adding low ionization potential element e.g. Li.

## Slide 14: Question bank
Q.19// Fill the following blanks with suitable word or statements:
1- X-rays causes the excitation of the Core electron.
2- The major applications of X-ray spectroscopy is for qualitative analysis.
3- X-ray can be applied in the field of medical imaging, airport security, inspecting industrial welds and elemental analysis.

## Slide 15: Question bank
Q. 20// Fill the following blanks:
i) FIA is a semi-automated technique.
ii) The disadvantages of Peristaltic Pump is
the tubes elongated.
iii) Weak redactor like silver redactor.
iv) Poly Tetra Fluoro Ethylene (PTFE ) tube resists solvents and mineral acids.