## Slide 1
Ministry of Higher Education and Scientific Research Salahaddin University
College of Agricultural Engineering Sciences Soil and Water Department
Lecture-3- Third Stage
By
Kamyar M. Mohammed
2023-2024

## Slide 2: Windbreaks were first used in connection with the dust bowl.
A windbreak causes the wind to swirl and it therefore does not cause as much damage.
Wind blowing in the same direction for a long time is able to gain speed and therefore evaporate more water from the soil and move more topsoil.

## Slide 6
The energy available for erosion takes two forms:
1. Potential energy (PE)
PE = mhg
PE = potential energy in (Joule) m = mass in (kg)
h = height difference in (m)
g = acceleration due to gravity in (ms-2)

## Slide 7
2. Kinetic energy (KE)
KE = ½ mv2
KE = kinetic energy in (joule) m = mass in (kg)
v = velocity in (ms-1)

## Slide 8
Fig. Typical infiltration rates for various soils.

## Slide 9: 1. Detachment of soil particles by flow
D = Q1.12 s0.64
detachment of an individual soil particle from the soil mass occurs when the forces exerted by the flow exceed the forces keeping the particle at rest.
D = detachment rate
Q = discharge or flow rate s = land slope

## Slide 10: 2. Transport of soil particles by flow
Once sediment has been entrained within the flow, it will be transported until
such time as deposition occurs.
T = 0.0085 Q1.75 s1.625 D-1.11
T = transport of the soil particles
Q = discharge rate
s = slope of land
D = diameter of particle size of the surface material

## Slide 11: 3. Deposition of soil particles
Dp = vs * C
Dp = rate of deposition of soil particles
C = actual sediment concentration
Vs = settling velocity of the particles

## Slide 12: Now lets talk about wind

## Slide 13: WIND EROSION
CREEP
SUSPENSION
SALTATION
SALTATION DETACHES PARTICLES
SMALLER PARTICLES SUSPENDED
LARGER PARTICLES CREEP
SANDY AND SILTY SOILS MOST SUSCEPTIBLE
SOIL ACCUMULATION IN DITCHES AND FENCE ROWS

## Slide 14: WIND EROSION CAN BE SIGNIFICANT
Near Mitchell, SD

## Slide 15: Severe dust storm. An example erosion by wind.

## Slide 17: Dust storms can carry loose unprotected soil into cities, too.

## Slide 19: What about animals?

## Slide 20: Many animals graze….is this good or bad for the soil??

## Slide 21
Overgrazing leads to the extinction of indigenous plant and animal species, soil erosion, and eventual desertification that renders once- fertile land barren.

## Slide 22: How do people effect soil erosion?

## Slide 24: Residential construction effects on soil

## Slide 25: Commercial construction

## Slide 26: Traditional Plowing

## Slide 28: Deforestation