## Slide 1: Methods and Estimation of Excess Runoff
Soil and Water Conservation
Lecture -6-
2023-2024

## Slide 2: 2. Curve number method
Where,
F =Actual retention, mm;
S =Potential maximum retention, mm;
Q =accumulated runoff depth, mm;
P =accumulated rainfall depth, mm Ia =Initial abstraction, mm

## Slide 3: Factors determining curve number values
Indicate runoff response characteristics of the drainage basin.
condition in the to curve number
Parameters like
1. Land use
2. Land treatment
3.Hydrological condition
4. Hydrological soil group
5. Antecedent soil moisture drainage basin are related
values.

## Slide 4: 3. Estimation of Runoff by Using Remote Sensing and GIS

## Slide 5: 3. Estimation of runoff by using remote sensing and GIS
Processes
Preparation of Land use/Land cover map by using the remote sensing and GIS.
Preparation of hydrologic soil group map for making appropriate hydrological soil classification A, B, C & D
Decide the curve number (CN) values based on field condition.
Calculate S value and then estimate runoff Q

## Slide 6: Estimation of runoff depth -Example
Preparation of Various Thematic Maps:
Contour map
Drainage map
DEM
Slope map
Land land use/ land cover map.
Kanhaiya nala watershed
In Tons River catchment
Elevation - 480 to 620 m aboveMSL
Satna District (M.P.)

## Slide 7: Soil and Land use land cover

## Slide 8: Generating CN and runoff depth map

## Slide 9: Runoff measuring devices
Direct Discharge Methods
Weirs
Orifices
Flumes
Velocity - Area Methods
Float method
Current meter
Tracer method

## Slide 10: Weir
Rectangular weir with no end contraction
Q = C L Hm
Where,
Q = discharge;
C = coefficient dependent
on the nature of weir
crest and approach conditions;
L = length of crest;
H = head on the crest
m = exponent depending on weir opening.
Weirs should
determine
be calibrated to these
parameters
before use.
Rectangular weir with two end contraction

## Slide 11: Orifice
Where,
Q = discharge rate, l/sec;
C = coefficient of discharge (0.6 - 0.8);
a = area of the orifice opening, cm2;
g = acceleration due to gravity, cm/s2
h = head of water causing the flow, cm

## Slide 12: Orifice

## Slide 13: Flumes Parshal Flumes
Used under free flow and submerged flow condition.
The single, primary point of measurement, denoted as Ha, which determine the flow rate through the flume.
In short throated flume, the Ha is
upstream of the
throat at a specific location - 2/3 of the sidewall length as measurement back from where the converging section meets the throat
For large Parshall flumes the point of measurement is closer to the throat

## Slide 14: Flumes

## Slide 15: Standard design dimensions (from USDA-SCS 1965)
Throat width | A (feet, inches) | B | C | D
W |  |  |  | 
(feet) 1 | 3-0 | 4-4 7/8 | 2-0 | 2-9 1/4
1½ | 3-2 | 4-7 7/8 | 2-6 | 3-4 3/8
2 | 3-4 | 4-10 7/8 | 3-0 | 3-11½
3 | 3-8 | 5-4 3/4 | 4-0 | 5-1 7/8
4 | 4-0 | 5-10 5/8 | 5-0 | 6-4 1/4
5 | 4-4 | 6-4½ | 6-0 | 7-6 5/8
6 | 4-8 | 6-10 3/8 | 7-0 | 8-9
7 | 5-0 | 7-4½ | 8-0 | 9-11 3/8
8 | 5-4 | 7-10 1/8 | 9-0 | 11-1 3/4
Dimension A = 2/3 (w/2+ 4)

## Slide 16: Cut Throat Flume
Improved version of Parshal
flume.
It is having flat bottom, vertical wall and no throat section.
For free flow critical depth is measured at throat.
Free flow depends on flume size and submergence ratio.

## Slide 17: Stream flow monitoring methods
The
volume of water that
Step 1:
moves through the channel is then calculated by dividing the channel into smaller units of known or approximated areas (width
× depth)
Measuring the flow within each area (velocity - distance over time).
By multiplying area and velocity, flow is calculated from the location
Selecting the channel location
Step 2: Developing a cross- section of the site and establishing a reference or staff gauge
Step 3: Measuring interval and depth

## Slide 18: Measurement of stream flow discharge
Mid sectionmethod

## Slide 19: Velocity-area method

## Slide 20: Velocity-area method

## Slide 21: Float Method
A floating object is put in water and time is recorded to cover a known distance.
Assuming the float travels ‘D’ meters in ‘t’ seconds
Velocity of water at surface =
(D/t) m/s,
Average velocity of flow = 0.8 (D/t),
= Cross
velocity of
Flow rate, Q sectional area × flow

## Slide 22: Current meter
Current meter is a small instrument containing a revolving wheel or vane that is turned by the movement of water.
Current meter is inserted to the depth = 0.6 d (d = depth of flow).
Number of rotations (rpm) was recorded and then velocity of flow is calculated from calibrated chart.
A current meter is used to measure velocity at 0.2 and 0.8 depth or at only 0.6 depth.

## Slide 23: Stage level recorder
Non recording stream gage
  Staff
  Wire(String)
  Crest staff
Recording stream gage
  Float type
  Digital gage

## Slide 25
Measurement of discharge in Sunity Creek
Sl. No | Distance from mouth, | Av. Count/ minute | Measured Velocity, | Top width, | Bottom width, | Water depth, | Area, (A) | Discharge, Q
 | m |  | m sec-1 | m | m | m | m2 | m3 sec-1
1 | 60 | 80 | 0.40 | 40.00 | 38.80 | 0.40 | 15.76 | 6.33
2 | 120 | 80 | 0.40 | 60.00 | 59.10 | 0.30 | 17.87 | 7.12
3 | 180 | 71 | 0.36 | 50.00 | 49.10 | 0.30 | 14.87 | 5.28
4 | 240 | 78 | 0.39 | 50.00 | 49.04 | 0.32 | 15.85 | 6.21
5 | 300 | 80 | 0.40 | 51.00 | 50.10 | 0.30 | 15.17 | 6.09
6 | 360 | 80 | 0.40 | 42.00 | 41.04 | 0.32 | 13.29 | 5.34
7 | 420 | 82 | 0.41 | 46.00 | 45.07 | 0.31 | 14.12 | 5.79
8 | 480 | 80 | 0.40 | 49.00 | 48.10 | 0.30 | 14.57 | 5.80
9 | 540 | 82 | 0.41 | 40.00 | 38.92 | 0.36 | 14.21 | 5.83
10 | 600 | 76 | 0.38 | 53.00 | 52.04 | 0.32 | 16.81 | 6.36
11 | 660 | 77 | 0.39 | 38.00 | 36.86 | 0.38 | 14.22 | 5.48
12 | 720 | 67 | 0.34 | 55.00 | 54.10 | 0.30 | 16.37 | 5.51
13 | 780 | 63 | 0.32 | 71.00 | 70.28 | 0.24 | 16.95 | 5.29
14 | 840 | 65 | 0.33 | 63.00 | 62.25 | 0.25 | 15.66 | 5.09
15 | 900 | 56 | 0.28 | 61.00 | 60.13 | 0.29 | 17.56 | 4.89
16 | 960 | 44 | 0.22 | 52.00 | 51.16 | 0.28 | 14.44 | 3.20
17 | 1020 | 36 | 0.18 | 63.00 | 62.16 | 0.28 | 17.52 | 3.18
18 | 1080 | 44 | 0.22 | 92.00 | 91.40 | 0.20 | 18.34 | 2.63
19 | 1140 | 40 | 0.20 | 40.00 | 39.16 | 0.28 | 11.08 | 2.22
20 | 1200 | 39 | 0.20 | 52.00 | 51.10 | 0.30 | 15.47 | 3.04
21 | 1260 | 34 | 0.17 | 49.00 | 48.22 | 0.26 | 12.64 | 2.17
22 | 1320 | 35 | 0.17 | 47.00 | 46.10 | 0.30 | 13.97 | 2.42
23 | 1380 | 73 | 0.37 | 47.00 | 46.04 | 0.32 | 14.89 | 5.46
24 | 1440 | 65 | 0.33 | 49.00 | 48.10 | 0.30 | 14.57 | 4.73
25 | 1500 | 57 | 0.29 | 58.00 | 57.25 | 0.25 | 14.41 | 4.11
26 | 1560 | 57 | 0.28 | 44.00 | 43.16 | 0.28 | 12.20 | 3.46
27 | 1620 | 48 | 0.24 | 42.00 | 41.13 | 0.29 | 12.05 | 2.89
28 | 1680 | 62 | 0.31 | 37.00 | 36.10 | 0.30 | 10.97 | 3.38
29 | 1740 | 65 | 0.32 | 41.00 | 40.04 | 0.32 | 12.97 | 4.19
30 | 1800 | 77 | 0.38 | 31.00 | 29.92 | 0.36 | 10.97 | 4.20
31 | 1860 | 66 | 0.33 | 32.00 | 30.86 | 0.38 | 11.94 | 3.96
32 | 1920 | 62 | 0.31 | 30.00 | 28.80 | 0.40 | 11.76 | 3.65
33 | 1980 | 74 | 0.37 | 34.00 | 32.80 | 0.40 | 13.36 | 4.97
34 | 2040 | 63 | 0.32 | 30.00 | 28.80 | 0.40 | 11.76 | 3.70

## Slide 26
Water availability in creeks and water quality
Creek | Discharge at creek cross section ( m3/sec) | Volume of Water available (November - January), m3
Creek Q1 | 11.03 | 
Creek Q2 | 9.35 | 
Creek Q3 | 7.84 | 
Creek Q4 | 7.04 | 
Average (Creeks) | 8.81 | 31474958
Sub Creek Q1 | 10.5 | 
Sub Creek Q2 | 5.87 | 
Sub Creek Q3 | 4.73 | 
Sub Creek Q4 | 4.42 | 
Average (Sub creeks) | 6.38 | 22324896
Total |  | 53799854