## Slide 1
Salahaddin University-Erbil
College of Agricultural Engineering Sciences
Soil and Water Department
Lecture – 4 -
Watershed Management
By
Kamyar M. Mohammed
2023-2024

## Slide 2: B. Areal Morphometric Parameters
Areal aspects deal with two-dimensional parameters like basin shape and area, drainage density, drainage texture, stream frequency, elongation ratio, circularity ratio, and form factor. The area of the basin is defined as the total area flowing to a given outlet, or pour point upon a horizontal plane contributing to cumulate of all orders of a basin which are delineated by ridgelines which are called water divides. Perimeter is the length of the outline of a basin that can be plot and calculate in the GIS software

## Slide 4: 1. Drainage density (Dd) = ƩL/A
It is the ratio of total channel segment length cumulated for all orders within a basin to the basin area. It is expressed in terms of Km/Km². The drainage density is an expression of the closeness of spacing of channels. Dd is suggested that the low drainage density indicates the basin is a highly permeable subsoil and thick vegetative cover. High drainage density is the result of weak or impermeable subsurface material, sparse vegetation, and mountainous relief. Low drainage density leads to coarse drainage texture while high drainage density leads to fine drainage texture.

## Slide 5: 2. Stream frequency (Fs) = (ΣNu)/A
The stream frequency (Fs) of a basin may be defined as the total number of stream segments within the basin per unit area. Stream frequency exhibits a positive correlation with drainage density in the watershed indicating an increment in stream population with respect to increase in drainage density. Climatic character, vegetation coverage, rock and soil types, rainfall intensity, infiltration capacity, relief, run-off intensity, permeability terrain, slope has played vital role in controlling the drainage frequency and density. Greater the drainage density and stream frequency in a basin, the runoff is faster, and therefore, flooding is more likely in basins with a high drainage and stream frequency

## Slide 6: 3. Form factor (Rf)= A/Lb2
Form factor (Rf) is defined as the dimensionless ratio of the basin area to the square of the basin length. This factor indicates the flow intensity of a basin of a defined area. The value of form factor would always be less than 0.754 (the value indicating to a perfectly circular watershed). The smaller the value of the form factor, the more elongated will be the basin whereas the higher values corresponding to the circular basin. Basins with high form factors experience larger peak flows of shorter duration, whereas elongated watersheds with low form factors experience flatter peak flows of longer duration. For the purpose of reducing the impact of peak runoff rate, there are two methods to be used: mechanical measures and agronomic measures. The agronomic measures include contour farming, strip cropping, and crop rotation

## Slide 7: 4. Elongation ratio (Re) = (2 √A/π)/Lb
Elongation ratio (Re) is defined as the ratio of the diameter of a circle of the same area as the drainage basin and the maximum length of the basin. The maximum length of the basin is plotted in GIS. Schumm’s ratio shows values between 0.6 and 1.0 over a wide variety of climatic and geologic types. The varying index of elongation ratio can be classified as; i) circular (more than 0.9), ii) oval (0.9 to 0.8), and iii) elongated (less than 0.7). A circular basin is more efficient in the discharge of runoff than an elongated basin. The value ranges from 0.6 to 0.8 for regions of high relief and the values close to 1.0 have very low relief with circular shape

## Slide 8: 5. Circulatory ratio (Rc) = 4πA/P2
Circulatory ratio is defined as the ratio of the area of a basin to the area of the circle having the same circumference as the perimeter of the basin. The value of the ratio is equal to unity when the basin shape is a perfect circle and is range 0.4 – 0.5 when the basin shape is strongly elongated and highly permeable homogeneous geologic materials. Rc is influenced by the frequency of stream, slope, relief geologic structure, climate and land use/landcover of the basin. Rc is a dimensionless number. Its low, medium, and high values are indicative of the youth, mature, and old stages of the life cycle of the tributary basins.

## Slide 9: 6. Length of overland flow (Lg)
The Length of Overland Flow (Lg) is defined as the length of water over the ground before it gets concentrated into mainstream which affect hydrologic and physiographic development of the drainage basin. Lg is significantly affected by infiltration (exfiltration) and percolation through the soil, both varying in time and space. The high Lg value indicates that the rainwater had to travel a relatively longer distance before getting concentrated into stream channels.

## Slide 10
When
Lg = length of overland flow (slope length) in km
P = perimeter in km
Lb = basin length in km
S = average slope basin in percent (%)
Rb = mean bifurcation ratio (unitless).

## Slide 11: 7. Drainage Texture (Dt) = (ΣNu)/P
The drainage texture, which is expressed in (km-1), is the ratio of the sum of stream portions belonging to all of the orders to the region's perimeter. The Dt is determined by the terrain's lithology, infiltration capability, and relief parameters. Dt further explained that unconsolidated rocks with no vegetation cover cause fine texture, while huge and consolidated rocks lead to coarse texture. Finer drainage textures form on dry environment rocks than on humid environment rocks due to the sparse flora. Divided drainage texture into five types: i) extremely coarse (less than 2), ii) coarse (2 to 4 ), iii) moderate (4 to 6), iv) fine (6 to 8), and v) very fine (more than 8).

## Slide 12: 8. Basin length (Lb)
The basin length (Lb) of a drainage basin, which is expressed in km, is a geometric measurement of its shape and extent. It is a basin's largest length within the greatest circle encircling the basin's boundaries and along the major river length. Using the ArcGIS program, the maximum basin length.

## Slide 13: 9. Infiltration number (If) = Fs × Dd
Infiltration number (If), expressed in (km-3), is defined as the value obtained by multiplying Dd and Fs. If values specify a basin’s infiltration potential. Values equal to or less than 6 indicate lower infiltration numbers, values greater than 10 indicate higher infiltration numbers, and those lying between 7 and 10 are moderate. A lower infiltration number means the basin has a high infiltration rate and a low runoff rate

## Slide 14: 10. Constant of channel maintenance (Ccm) = 1/ Dd
The inverse of drainage density is the constant of channel maintenance. Ccm is expressed in kilometers. It is determined not only by the permeability of the rock, the climatic regime, the flora, and the relief but also by the soil erosion duration and the climatic profile.

## Slide 15: 11. Compactness coefficient (Cc) = 0.2821 P/A0.5
The compactness coefficient (Cc) of a catchment is the ratio of the catchment's diameter to the radius of the circle, which is relative to the basin's area. The shortest period of concentration prior to the occurrence of peak flow is caused in a circular basin. When the Cc value is equal to one, it is an indication that the watershed under study behaves completely as a circular basin. If the Cc is above one, some deviation away from the circular nature is noticed in the basin. However, if the Cc exceeds three, the basin can have a very elongated shape