## Slide 1: Determination of Nitrogen and Crude Protein
Lecture 7

## Slide 2: Principle
The kjeldahl method is the standard method of nitrogen determination.
This method is applicable for the determination of nitrogen (N) in all types of forages and feeds.

## Slide 3: kjeldahl method consists of three basic steps:
Digestion of the sample in concentrated sulfuric acid with a catalyst which results in removes all OM and conversion of nitrogen to ammonia sulfate.
NaOH is then added to convert the NH4SO4 to ammonia NH3 which is distillates into a trapping solution (weak acid , boric acid H3Bo3.
Quantification of the ammonia in boric acid by titration with a standard acid solution HCl. the amount of acid neutralized by the ammonia is an estimate of the amount of nitrogen in the sample. Crude protein is estimated by multiply the nitrogen with a constant factor.

## Slide 4: Crude protein estimation steps

## Slide 5: Materials and equipment used:
Kjeldahl devices.(Digestion and distillation)
Sulfuric acid.
Catalyst.
Glass granules.
Boric acid.
Sulfuric acid 0.1 normality.
Sodium Hydroxide.
Indicator.
Distilled water.
Sensitive balance.

## Slide 6: Procedure: Digestion
Add 0.5g of the sample to Kjeldahl apparatus tube.
Add 25ml of sulfuric acid and 5gm catalyst for each sample.
Place tubes set on bock digester preheated to 420C (Digester must be equipped with an exhaust and /or placed in a fume hood), digest about 45min.
Remove tube and let cool about 10 min in a fume hood (time will depend upon airflow around tubes), then add directly about 25-30ml of distilled water to the bottom of each tube to dissolve acid digest completely).

## Slide 7: Procedure: Distillation / titration
Place NaOH in alkali of steam distillation unit. Make sure that sufficient NaOH is dispensed from unit to neutralize all acid in tube and excess (about 50- 55ml) before conducting distillation.
Place 250ml titration flask containing trapping solution (about 25ml 4% boric acid containing indicator) on the receiving platform with tube the condenser extending below the surface of the trapping solution.
Attach digestion tube containing diluted, cooled digest to distillation unit.
Dispense appropriate volume of distilled water (50ml) and the base (NaOH) solution (50ml).
Steam distillation until 100- 125ml distillate collects in titration flask.
Remove titrating flask from unit, rinsing condenser tip with water.
Titrate trapping solution containing ammonia (N) with 0.1 or 0.2 HCl to neutral gray endpoint, record volume of acid VA required to nearest 0.01ml , and then titrate reagent blank (VB) similarly. Colour change is from pink to green to gray to purple.

## Slide 8: Calculation
N% (as fed basis) = (VA-VB1)* NHCl * 0.014/W *100
N% (as DM basis) = N % (as fed basis)* 100/DM%
VA= volume, in ml, of standard HCl required for sample
VB1=volume in ml of standard HCl required for blank
NHCl= normality of acid standard
0.014= milliequivalent weight of N, in grams
W= weight of sample in grams
CP% (DM basis)= N%(DM basis)*F