## Slide 1: CHAPTER TWO Cathode Ray Oscilloscope

## Slide 2: Cathode Ray Oscilloscope
The Cathode Ray Oscilloscope (CRO) is a very useful and versatile laboratory instrument used for display, measurement and analysis of waveform of electrical and electronic circuits.

## Slide 3: CRO Construction
The heart of the Oscilloscope is the Cathode Ray Tube which it consists of four main parts:
Electron Gun
Deflection part
Post deflection Acceleration
Screen

## Slide 5: Electron Gun
This section is responsible for generating the electrons and directed them toward the next section (Deflecting), the electron gun composed of two main parts:
Triode section
Filament
Cathode
Grid
First Anode (A1)
2. Focusing
Second Anode (A2)
Third Anode (A3)

## Slide 6: Triode section
Filament : It is a heater to Heat the Cathode
Cathode :Made of Nickel and it is a cylinder shaped with a flat, oxide-coated electron emitting surface directed toward the hole in the Grid.

## Slide 7: Triode section
Grid: It is a nickel cup with a hole in it, almost completely encloses the cathode, and connected to a potential with a cathode and they control the number of electrons directed to the screen (Brightness control).
First Anode (A1): It is a cylinder shaped, open at one end and closed at the other end with a hole at the center of the closed end, it accelerates the electron to the focusing section

## Slide 9: Focusing
Second Anode (A2) : It is connected to a high negative voltage to produce equipotential lines to focus the electrons to a fine point on the screen.
Third Anode (A3) : It accelerates the electron after they focused .