Salahaddin University                                                                                         Stage: 2

College of Science- Geology		        Date:23 / 11 /2022

Subject: Hydrology		        Time: 60 minutes

Examination, (2022-2023) (First) Attempt

Q1/ Fill in the blanks.                  (20 Mark)

- Water as a solid (ice) is ………………………dense than it is as a liquid

- The ratio of surface water in the world is equal to  ………..%

- In semi-arid climate, the Evaporation > ………………………> Groundwater recharge.

- Evaporation + Transpiration =…………………………………

- Volume of ice increase with increasing …………to up to zero.

- N = (Cv /є)2 Where:   N: Optimal number of stations, є: ………………, and Cv: coefficient of variation of the rainfall values at the existing m stations (in percent)

- Water availability Elements include Precipitation and …………………..

- ………........: is the real quantity of water vapor in each cubic meter of air. It’s measured in gm/m3.

- The rate of evaporation is controlled by three things, the amount of energy, the difference in concentration and of water molecules, and…………………….

- The pan coefficient, K pan, depends on: The type of pan used, the pan environment, and the……………...

- PE = KP (0.46t + 8.13) Where: K: Correction factor which is equal to (0.0311t+0.24), P: ……….. and  t: Mean monthly temperature (°C)

- Infiltration is important for soil water recharge, groundwater recharge, ………………………, flooding, and contaminant movement.

- In ……………mineralized water, the Ec ranged between 0.6 – 1.0 ds/m

- If Infiltration rate ranged between (20-60)mm/h is called …………...

- If we have two stations (points) to measure water velocity in the rivers, the expressed equation will be V=…………………

- ……………….= Atomic weight of ion / Valance of ion

- ………..stream: water table lower than bottom of stream channel and it loss as you go down stream

- The dilution method is a suitable for rivers of shallow depths and ………..flow.

- In ……………weir, Q = 3.37 LH3/2

- ………….aquifer is an aquifer that is bounded above and below by confining beds.

Q 2/ Answer by True or False (10 Mark)

- Groundwater is the variety of ways water moves across the land.

- Intensity ratio of low rain is between 2.5 t0 7.5 mm/hour

- Hydrology is a basic branch of Earth Science.

- In humid arid climate, groundwater recharge is less than groundwater recharge, and surface water is less than evaporation.

- The variation of rainfall with respect to time may be shown graphically by hydrograph and mass curve of rainfall.

- In Kharufa  Pav= {(P1xA1) + (P2xA2) +……....+ (PnxAn)} / A1 + A2 + …….…+An

- In arithmetic method        PE / ρ = atm

- If WD = P – PE ; P > PE

- A non-flowing artesian well: the water is under enough pressure to rise all the way to the surface without being pumped and must be capped to control the flow.

- Infiltration rate decreasing in non compacted soil comparing with compact soil.

- Methods for measuring the river discharge are: Velocity-Area method, Weirs and flumes, Dilution methods, Float-Area method and Direct Volumetric methods.

- The mean velocity of water in river is measured in 0.4 of the depth.

- In the small basins the flow is as high flow , while in large area basins the flow is in stream courses.

- In Chezy equation, Q = (1/n) AR2/3 S1/2

- Hyetograph: is the graph that represents the variation of stream discharge with time.

- The TDS in salty water is more than the TDS in saline water.

- Turbulent flow is the portion of stream flow that comes from subsurface flow, water infiltrated but returned to the surface in a stream channel.

- Convective precipitation: This is the precipitation that is caused by the expansion of air on uplift along or near a frontal surface. Kurdistan region rainfall is mostly of this type.

- The K pan is high if: the pan is placed in a fallow area, the humidity is high, the wind speed is low

- Slope of the basin: large slopes of land surface produces high and sharp peak hydrographs

Q3/ A catchment has six raingauge stations. In a year, the annual rainfalls recorded by the gauges are as follows: (6 Mark)

| Stations | A | B | C | D | E | F |
| --- | --- | --- | --- | --- | --- | --- |
| Rainfall(mm) | 929 | 1011 | 1766 | 1205 | 889 | 1362 |

For a 8% error in the estimation of the mean rainfall, calculate the optimum number of stations in the catchment.

Q4/ Table below show the chemical analysis of deep well. Calculate the total hardness (by using Faure method) of this analysis.  (8 Mark)

| Ca++ ppm | Mg++ ppm | Na+ ppm | K+ ppm | Cl- epm | HCO3- epm | SO4—2 epm | NO3- epm |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 171 | 69 | 70 | 6.9 | 2.65 | 8.3 | 6.11 | 2.60 |

Atomic eight of ions:        Ca = 40                  Mg = 24                  Na = 23                      K = 39

Cl =35.5                HCO3 = 61              SO4 = 96                   NO3 = 63

Q5/ Define the following (6 Mark)

- The catchment or river basin(watershed)

- ponding time

Good luck

Q 1/

|  | Answers |  | Answers |
| --- | --- | --- | --- |
| 1 | less | 11 | Percentage of sun shine hours in each month to sun shine |
| 2 | %1 | 12 | river base flow |
| 3 | Surface runoff | 13 | Highly |
| 4 | Evapotranspiration | 14 | moderate |
| 5 | Temperature | 15 | 1/2(V0.2+V0.8) |
| 6 | allowable degree of error in the estimate of the mean rainfall | 16 | Equivalent weight of ion |
| 7 | Relative humidity | 17 | Losing (influent) |
| 8 | Absolute humidity (Ah) | 18 | turbulent |
| 9 | The pressure differential | 19 | trapezoidal |
| 10 | climate | 20 | Unconfined |

Q2/

|  | Answers |  | Answers |
| --- | --- | --- | --- |
| 1 | Runoff | 11 | T |
| 2 | moderate | 12 | 0.6 |
| 3 | Applied | 13 | sheet |
| 4 | Arid | 14 | manning |
| 5 | Hyetograph | 15 | Hydrograph |
| 6 | Thiessen polygon | 16 | less |
| 7 | kharufa | 17 | Base flow |
| 8 | WS | 18 | Frontal |
| 9 | flowing artesian | 19 | T |
| 10 | Increasing | 20 | T |

Q3/ A catchment has six raingauge stations. In a year, the annual rainfalls recorded by the gauges are as follows: (7 Mark)

| Stations | A | B | C | D | E | F |
| --- | --- | --- | --- | --- | --- | --- |
| Rainfall(mm) | 929 | 1011 | 1766 | 1205 | 889 | 1362 |

For a 8% error in the estimation of the mean rainfall, calculate the optimum number of stations in the catchment.

For data above:

M = 6

P = 1193.6667                       	σm – 1 =332.345

є = 8            	    Cv = [(100 x 359.815) / 1306.66] = 27.84

N = (27.84 / 8)2 = 12 stations

Q4/ Table below show the chemical analysis of deep well. Calculate the total hardness (by using Faure method) of this analysis. The data measured in ppm

| Ca++ ppm | Mg++ Ppm | Na+ ppm | K+ ppm | Cl- epm | HCO3- epm | SO4—2 epm | NO3- epm |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 171 | 69 | 70 | 6.9 | 2.65 | 8.3 | 6.11 | 2.60 |

Atomic weight of ions:    Ca = 40                  Mg = 24                  Na = 23                      K = 39

Cl =35.5                HCO3 = 61              SO4 = 96                   NO3 = 63

Ca = 171/20 = 8.55                        Na = 70  /23 = 3.04

Mg = 69 / 12 = 5.75                       K = 6.9 / 39 = 0.77

Sam of cat.= 18.06

Sum of anion = 19.66

U% = {(1.6 /37.72)} / 100

= 4.24

certain

TH = (2.497 x 171) + (4.115 x 69 )

=426.99 + 283.94 = 710.93

Q5/ Define the following (6 Mark)

- The catchment or river basin(watershed)

This can be defined as the area of land from which water flows towards a river and then in that river to the sea.

A river basin can be defined in terms of its topography through the assumption that all water falling on the surface flows downhill. In this way a catchment boundary can be drawn (as in Figures below) which defines the actual catchment area for a river basin

- ponding time

It is the time needed to reach saturation at the top of the soil column