## Slide 1
Computing Temperature by speed of Sound
By : Belan Araz Hasan

## Slide 2: Abstract:
Environmental effects change the velocity and the absorption of sound in air. Even small percentage changes may cause serious listening problems in enclosed acoustic spaces. A detailed analysis of the environmental effects of temperature on the speed of sound is presented. An overview of the available literature reveals serious shortcomings for practical applications. New graphs, tables, and equations present the findings in a more useful manner for sound reinforcement. The results show that tight control of temperature must accompany the popular trend of splitting microseconds when time correcting sound systems. Results exploits the high sensitivity of the speed of sound in air to the air temperature. The comparison with the traditional temperature sensors highlighted the limit of the latter in case of fast temperature variations
Keywords: Temperature, Speed of sound

## Slide 3
WHAT IS SOUND?
A form of energy that travels through the air.

## Slide 4
WHAT IS SOUND?
Sound is made when something vibrates.
Sound needs a medium to travel.

## Slide 5
Louder sound waves carry more energy
Intensity decreases as distance increases.
Intensity: The amount of energy that flows through a certain area in a specific amount of time

## Slide 6
HOW IS SOUND TRANSMITTED?
Transmission of sound requires matter (air, liquids, solids) as transmitting medium, unlike light which can travel through matter and space.
Notes: Sound travels through solids and liquids
  Example- knocking on a door
    When you knock, the particles of the door vibrate
    The vibration creates sound waves that travel through the door
    When the sound waves reach the other side, the same vibrations make sounds waves in the air.

## Slide 7
Speed of Sound: Elasticity
The more elastic the medium, the faster sound travels
  Sound travels well in solids because they are usually more elastic
    Particles of solids do not move very far , so they bounce back and forth very quickly as the compressions and rarefaction of the sound waves pass
  Most liquids are not very elastic and sound does not travel well
  Sound travels very slowly in gases because gases are not very elastic

## Slide 8: Chapter Two: Theory
The theoretical expression for the speed of sound c in an ideal gas is
(1)
where P is the ambient pressure, the gas density, and the ratio of the specific heat of gas at constant pressure to that at constant volume.
The term is dependent upon the number of degrees of freedom of the gaseous molecule. The number of degrees of freedom depends upon the complexity of the molecule, = 1.67 for monatomic molecules = 1.40 for diatomic molecules = 1.33 for triatomic molecules.
Since air is composed primarily of diatomic molecules, the speed of sound in air is
(2)

## Slide 9: 2.1-Temperature Dependence
Substituting the equation of state of air of an ideal gas (PV = RT) and the definition of density p (mass per unit volume), Eq. (2) may be written as
(5)
where R is the universal gas constant, T the absolute temperature, and M the mean molecular weight of the gas at sea level.

## Slide 10: Effect of temperature on speed of sound
C= 330+0.58 t
  then at 20ᵒC  343 m/s
  But at 0ᵒC  330 m/s
Above equation show that the speed of sound increase with increasing temperature.

## Slide 11: Effect of temperature on speed of sound
The speed of sound is seen to increase as the square root of the absolute temperature. Substituting centigrade conversion factors and the reference speed of sound gives

## Slide 12: Chapter Three: Methods/Materials
In present work the following instruments used for calculating the temperature from the measuring the speed of sound: Microphone, speaker, oscilloscope, audio generator, thermometer, hairdryer, and a 1.1m pipe.

## Slide 13: Computing speed of sound at different temperatures
By using an application on a smartphone we try to measure the speed of sound in different temperatures, then we draw the relation of temperature on the speed of sound.

## Slide 14: an acoustic stopwatch

## Slide 15: Chapter Four: Results and Discussion
Results:
Theoretically relation of temperature and speed of sound can be obtain from equation (7)
(7)
where t is the temperature in degrees Celsius.
Graphs of Eq. (7) are shown in Fig.(1) , respectively. Table(1) tabulates results for Eq. (7).

## Slide 16
Temperature(Co) | Speed of sound(m/s)
10 | 337.4659
11 | 338.0616
12 | 338.6563
13 | 339.2499
14 | 339.8425
15 | 340.434
16 | 341.0245
17 | 341.614
18 | 342.2025
19 | 342.79
20 | 343.3765
21 | 343.9619
22 | 344.5464
23 | 345.1299
24 | 345.7124
25 | 346.2939
26 | 346.8744
27 | 347.454
Table(1): Theoretically calculated the relation between the temperature and the speed of sound

## Slide 17
Chart: speed of sound versus temperture
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33
 | 332.0565 | 332.6619 | 333.2662 | 333.8694 | 334.4715 | 335.0725 | 335.6725 | 336.2713 | 336.8692 | 337.4659 | 338.0616 | 338.6563 | 339.2499 | 339.8425 | 340.434 | 341.0245 | 341.614 | 342.2025 | 342.79 | 343.3765 | 343.9619 | 344.5464 | 345.1299 | 345.7124 | 346.2939 | 346.8744 | 347.454 | 348.0326 | 348.6103 | 349.187 | 349.7627 | 350.3375 | 350.9113
Figure(2): Theoretically calculated speed of sound versus temperature

## Slide 18: Table (2): The calculated speed of sound from experimentally measured the distance between two smart phones and then determining the temperature of the air in Co with the value of temperature measured by thermometer
t/sec | V m/sec | T/oC(calculated) | T/oC(measured)
0.01483 | 337.46 | 10 | 11
0.01473 | 339.24 | 13 | 13
0.01470 | 340.43 | 15 | 14
0.01467 | 341.02 | 16 | 15
0.01461 | 342.20 | 18 | 18
0.01457 | 343.37 | 20 | 21
0.01451 | 344.54 | 22 | 22
0.01448 | 345.12 | 23 | 24
0.01444 | 346.29 | 25 | 25
0.01439 | 347.45 | 27 | 26
0.01435 | 348.03 | 28 | 28
0.01431 | 349.18 | 30 | 29
0.01427 | 350.33 | 32 | 32
0.01422 | 351.48 | 34 | 33

## Slide 19
Chart: speed of sound
| 337.46 | 339.24 | 340.43 | 341.02 | 342.2 | 343.37 | 344.54 | 345.12 | 346.29 | 347.45 | 348.03 | 349.18 | 350.33 | 351.48
T/oC | 10 | 13 | 15 | 16 | 18 | 20 | 22 | 23 | 25 | 27 | 28 | 30 | 32 | 34
Figure (3): relation between the speed of sound in air and the temperature

## Slide 20
By comparing the calculated values of temperature from the experimentally values of speed of sound with the theoretically calculated values of and measured values by thermometer it show a good agreement and this is a criteria that the present work is a good method for calculation the temperature of air.
By analyzing the data, you can determine the empirical relationship between the speed of sound and temperature for the specific gas you used. This relationship can be compared to theoretical models like the ideal gas law to validate the experimental results.

## Slide 21: Conclusions
I concluded that I was able to accurately predict the temperature by the velocity of the sound that passed through it. Whenever the temperature was increased, the speed increased; conversely, as the air slowly cooled, the speed decreased. I think this is due to the fact that with a higher temperature, more energy is in the air. With more energy, particles are able to vibrate faster, thus increasing the speed of sound.

## Slide 22: References
HARDY, H. C., TELFAIR, D. & PIELEMEIER, W. H. 2005. The Velocity of Sound in Air. The Journal of the Acoustical Society of America, 13, 226-233.
KAZYS, R. & VASKELIENE, V. 2021. High Temperature Ultrasonic Transducers: A Review. Sensors (Basel), 21.
KERKER, M. 1986. Classics and classicists of colloid and interface science: 2. John William Strutt, Lord Rayleigh. Journal of Colloid and Interface Science, 113, 589-593.
KROUT, K. & SOHRAB, S. 2016. On the Speed of Sound. International Journal of Thermodynamics, 19, 29.
LI, J., MA, Y., ZHANG, T., SHUNG, K. & ZHU, B. 2022. Recent Advancements in Ultrasound Transducer: From Material Strategies to Biomedical Applications. BME Frontiers, 2022, 1-19.
WEAST, R. C. 1986. CRC handbook of chemistry and physics Sixty-seventh edition, United States, CRC Press Inc.

## Slide 23
Thank you for your attention