## Slide 1
General Introduction
Design means presentation of the client’s demand in an engineering manner, ready to be executed by specialized company according to specifications and engineering laws.
Design must satisfy:
Essential requirements
- structural safety
- durability
2. Relative properties
- early completion
- low maintenance
- light of the structure
- likely change of use
Design must combine:
- overall economy
- safety
- aesthetics of the structure
Design stages:
1. design of appropriate form or type of structure.
2. detailed design of various parts.

## Slide 2
Design must sure that an acceptable probability is achieved that the
structure does not fail during the specified life.
Acceptable condition or failure limit-state:
Very safe design high cost
Absolute safety impossible because of;
1. Variation in strength of material
2. Variation in actual loading
3. Deterioration in strength of material
Cost of any structure is made of:
1. design
2. construction
3. running expenses ( heating , lighting , …)
4. insurance premium against acceptable risks ( fire, flood, …)
5. insurance premium against losses due to structural failure
6. demolition

## Slide 3
The design of a structure may be regarded as the process of selecting the proper materials and proportioning the different elements of the structure according to state-of-the-art engineering science and technology. In order to fulfill its purpose, the structure must meet the conditions of safety, serviceability, economy, and functionality. This can be achieved using design approach-based strain limits in concrete and steel reinforcement.
Limit state design is a further step in the strength design method. It indicates the state of the member in which it ceases to meet the service requirements such as losing its ability to withstand external loads or suffering excessive deformation, cracking, or local damage. According to the limit state design, reinforced concrete members have to be analyzed with regard to three limiting states:
1. Load-carrying capacity (safety, stability, and durability)
2. Deformation (deflections, vibrations, and impact)
3. Formation of cracks.
The aim of this analysis is to ensure that no limiting state will appear in the structural member during its service life.

## Slide 4
Reinforced concrete building elements

## Slide 5
Reinforced concrete building elements

## Slide 6
Reinforcement position

## Slide 7
Strain and stress distributions in a singly reinforced rectangular section
For singly reinforced section:
; ; ;
Where ФMn=ultimate moment capacity of the section, kN.m,
b, d ; are section properties, mm,
ρ ; reinforcement ratio, ρ = As/ bd
fc` ; concrete compressive strength based on standard 150x300 mm cylinders, MPa
fy ; yield strength of reinforcing bars, MPa.