## Slide 1
University of Salahaddin – College of Engineering Software & Informatics Dep. Computer Architecture II 2022-2023 Lecture 4 Lecturer Nyan D. Sallman

## Slide 2: OUTLINE
Statement in assembly language
Arithmetic Instruction
Special Assembler Directive
Basic logical Instructions

## Slide 3: Statement in assembly language
Any statement consist of four part:
Label OP code Operand(s) Comment
Label :- symbolic name for memory location (begin with any letter or symbol :- a, b, A, B, …. @, $, -, ?,…….)
Op code:- code of the instruction
Operand:- data used by the instruction
Comment :- contains comments on instr., Previously begin with (;)

## Slide 4: Data definition in data segment
DATA1 DB 23H ;label DATA1 defined as byte contain 23h
DATA2 DW 1000H ; label DATA2 defined as word contain 1000h
Dir DD F100 F342h ; label Dir defined as double word contain ; F100 F342h (hold 4 byte in memory)

## Slide 5: Example
START: MOV AL,44H ;copy 44 to AL
MOV CX, 200 ;copy 200 to CX
MOV Dt1, AL ;copy AL into byte memory
location Dt1
MOV BX, Dt2 ; copy word begin from memory
location named Dt2 to BX
MOV ES:[2000h], BH
Dt1 DB 23H ;data1 defined as byte contain 23h
Dt2 DW 1000H ;data2 defined as word contain 1000h

## Slide 6: Example
.DATA
DATA1 DB 10H
DATA2 DB 20H
DATA3 DW 1000h
DATA4 DW AABBH
.CODE
.STARTUP
MOV AL,DATA1
MOV AH,DATA2
MOV DATA3,AX
MOV AX,DATA4
.EXIT

## Slide 7
Some of illegal instruction :
MOV ES, DS ; segment to segment
MOV BL,DX ;mixed sizes
MOV CS,AX ;CS must not to be destination register
MOV DATA1, DATA2 ;memory to memory directly
MOV ES:[DI],DS:[SI] ; = = =

## Slide 8
Arithmetic Instruction
Addition
Subtraction
Multiplication and Division
Basic logic instruction
AND
OR
Exclusive-OR
NOT
SHIFT and ROTATE

## Slide 9
Addition operation
ADD AL,BL ; AL=AL+BL
ADD CX,DI ;CX=CX+DI
ADD CL,[BP] ;CL=CL+[BP]
ADD BH,33H ;BH=BH +33H
ADC BX,CX ;BX=BX + CX+ carry
ADC DX,[BP+2] ;DX=DX+[BP+2]+ carry
stack
INC BL ; BL= BL+1
INC SP ; SP=SP+1
INC DATA ; DATA=DATA+1

## Slide 10
Subtraction operation
SUB CL,BH ; CL=CL-BH
SUB AX,SP ; AX=AX-SP
SUB [BX],DX ; [BX]=[BX]-DX
SUB AH,TEMP ;AH=AH- TEMP
SBB AH,AL ; AH=AH-AL-carry
SBB DX,2 ;DX=DX-2-carry
DEC BL ;BL=BL-1
DEC CX ;CX=CX-1
DEC NUMB1 ;NUMB1=NUMB1-1

## Slide 11
BX
AX
BX
DX
CX
AX
+
CF
(ADC)
(ADD)
Write a program to adds BX-AX with DX-CX and the sum appearing in BX-AX

## Slide 12
Write a program to subtract DX-CX from BX-AX with the result appearing in BX-AX
BX
AX
BX
DX
CX
AX
-
CF
(SBB)
(SUB)

## Slide 13
AA00 1122
- 1000 2442
Final result of (BX AX)-(DX CX)=(99FF ECE0)H
And the state of FLAGES : Z=0, S=1, AC=0, C=0, P=1 , and O=0
MOV BX, AA00H
MOV AX, 1122H
MOV DX,1000H
MOV CX,2442H
SUB AX,CX
SBB BX,DX
Subtraction of 32 bit from 32 bit in 8086 microprocessor

## Slide 14
Special Assembler Directive
(PTR operator , OFFSET directive )

## Slide 15
Improper instr. without operand size boundaries
Solution by PTR operator
Notes: PTR :- pointer directive to translate Reference of operand (special Assembler directive )

## Slide 16
Q: Check on these instructions if there would use Pointer operator {PTR} or not
.data
LAB1 DB 10h
LAB2 DW 1000 H
.code
MOV AL, LAB1
MOV DL, [BX]
SUB [BX],2
MOV CL,LAB2
ADD AL, LAB1+1
.data
LAB1 DB 10h
LAB2 DW 1000 H
.code
MOV AL, LAB1
MOV DL, [BX]
SUB BYTE PTR [BX], 2
MOV CL, BYTE PTR LAB2
ADD AL, LAB1 +1

## Slide 17
OFFSET directive
0000 DATA DW 1234H
MOV BX, DATA ;copy content of memory
location DATA to BX
BX=1234h
MOV BX, OFFSET DATA ;copy the offset address of
DATA to BX
BX=0000h

## Slide 18: Multiplication
8- bit multiplication
MUL CL ; AX=AL * CL (unsigned result )
IMUL DH ; AX=AL*DH (signed result)
IMUL BYTE PTR[BX] ; AX=AL*BYTE PTR[BX]
(signed result)
MUL TEMP ; AX=AL*TEMP (unsigned result)
Note: multiplicand always in AL
C, O flag are predictable and used

## Slide 19
Example: multiply content of BL=5, and CL =10 and save the product in DX, suppose all the data unsigned:
Sol//
MOV BL,5
MOV CL,10
MOV AL,CL
MUL BL
MOV DX,AX
Carry | Overflow | Result
0 | 0 | Most significant byte (8 bit multiplication), or most significant word (16 bit multiplication), is zeros
1 | 0 | 16 bit wide (8 bit multiplication), 32 bit wide (16 bit multiplication),

## Slide 20: 16- bit multiplication
MUL CX ; DX_AX= AX *CX unsigned product
IMUL DI ;DX_AX=AX *DI signed product
MUL WORD PTR [SI]
;DX_AX=AX*WORD PTR [SI] unsigned product
Note : AX contain multiplicand

## Slide 21: 32- bit multiplication
MUL ECX
IMUL EDI
MUL DWORD PTR[ESI]
;same operation as above, but multiplicand in EAX and the product to be save in EDX-EAX

## Slide 22: (8 bit Division)
Dividend AX
Divisor 8-bit reg. or memory location
Result : AL= quotient
AH= Remainder

## Slide 23: (8 bit Division)
DIV CL
IDIV BL
DIV BYTE PTR [BP]
Example : if AX=0010h(+16), BL=FDh(-3)
After IDIV BL making AX=01FBh
Quotient AL= FB(-5) ; truth sign
Remainder AH =1 ; dividend sign
Note if the dividend (-16) and divisor(+3)
AL=(-5) and AH=(-1)

## Slide 24: (16 bit Division)
Dividend DX_AX
Divisor 16-bit reg. or memory location
Result : AX= quotient
DX= Remainder

## Slide 25: (16 bit Division)
DIV CX ; (DX_AX) / CX , DX=Rem. , AX=Quo.
IDIV SI
DIV NUMB
Note: some Division need to extend AX
By:
CBW :- convert byte to word
CWD:- convert word to double

## Slide 26: Example : Write Ass. Por. to Divide (AX=-100) on (CX=9)
MOV AX,-100
MOV CX , 9
CWD ; convert word in (AX) to double word saved in DX-AX
IDIV CX

## Slide 27: (32 bit Division)
Dividend EDX-EAX
Divisor 32-bit reg. or memory location
Result : EAX= quotient
EDX= Remainder
DIV ECX
IDIV DATA
DIV DWORD PTR[EDI]

## Slide 28
Example : (program to save quotient and Remainder as a fraction value )
MOV AX,13
MOV BL,2
DIV BL
MOV ANSQ, AL ; SAVE QUOTIENT
MOV AL,0
DIV BL ;GENERATE REMAINDER
MOV ANSF,AL ;SAVE Fraction