## Slide 1
    University of Salahaddin – Hawler
            College of Engineering
        Civil Engineering Department
HYDRAULIC STRUCTURES
Lecturer: Othman K. Mohammed

## Slide 2
Contents | 
Chapter 1 | Canal Design and Lining
Chapter 2 | Hydraulic Structures on Pervious Foundations
Chapter 3 | Hydraulic Jump and Energy Dissipation
Chapter 4 | Design of Main Canal Head Works
Chapter 5 | Drop or Fall Structures
Chapter 6 | Design of Dams and Reservoirs
Chapter 7 | Spillways
1

## Slide 3
Set by: Othman K. Mohammed
Types of Hydraulic Structures
According to the purpose of its function
Storage Structures: to store water such as Dams & Tanks.
Conveyance Structures: to convey water from place to another such as pipelines, Siphons, Culverts, Tunnels, aqueducts and open channels.
A hydraulic structure is a structure submerged or partially submerged in any body of water, which disrupts the natural flow of water.
Introduction
CHAPTER ONE
CANAL DESIGN AND LINING

## Slide 4
Flow Diversion Structures: to regulate and divert the quantities of flow to another structures or canals such as barrages and regulators.
Flow measurement structures: to measure the flow passing through it such as Weirs, Orifices, nozzles, Venturi and Parshall flume.
Energy dissipation structures: to protect the floor of hydraulic structure from erosion and damage due to severe waves which impact with the body of structure such as Stilling basins, Surge tanks, Check dams and vertical drop.
Sediment and Chemical Control Structures: to control or remove sediments and other pollutants such as Sedimentation tanks, Screens, Traps, Filters & mixing basins.
2

## Slide 5
Open Channel
Set by: Othman K. Mohammed
An open channel is the one in which stream is not complete enclosed by solid boundaries and therefore has a free surface subjected only to atmosphere pressure. The flow in such channels is caused only by gravitational component along the slope of channel. Examples of open channel are Rivers, canals, streams, & sewerage system etc.
Types of channels
based on material
Lined channels
(Rigid boundary channels)
Minimum velocity
to prevent sedimentation
Unlined channels
(erodible or earthen channels)
Maximum velocity
to prevent erosion

## Slide 6
Trapezoidal channel
Shapes of channels
Circular channel
Triangular channel
Rectangular channel
Set by: Othman K. Mohammed
Open Channel Design
It is the process to obtain a shape, slope and geometry of channel/canal which should not have objectionable silting and scouring.

## Slide 7
For example for a trapezoidal channel, it consists of determining;
depth,
bed width,
side slope and
longitudinal slope of the channel so as to produce a non-silting and non-scouring velocity for the given discharge and sediment load.
4
where: Q : discharge in m3/sec,
  A : wetted cross-sectional area in m2
  R : hydraulic radius in m, R = A / P
Manning formula
P
A
1
m
1
m

## Slide 8
Hydraulic structures such as dams, weirs, barrages, head regulators, cross-drainage works, etc. may either be founded on an impervious solid rock foundation or on a pervious foundation.
Whenever, such a structure is founded on a pervious foundation, it is subjected to seepage of water beneath the structure, in addition to all other forces to which it will be subjected when founded on an impervious rock foundation.
Introduction
Set by: Othman K. Mohammed
CHAPTER TWO
HYDRAULIC STRUCTURES ON PERVIOUS FOUNDATIONS

## Slide 9
Causes of Failure of Hydraulic Structures on Pervious Foundations
Failure by Subsurface Flow
By Piping or undermining
Controlled by Floor Length (b)
By Direct uplift
Controlled by Floor Thickness (t)
Failure by Surface Flow
By Hydraulic Jump
By Scouring
Controlled by Protection Works
Set by: Othman K. Mohammed

## Slide 10
The water from the upstream side continuously percolates through the bottom of the foundation and emerges at the downstream end of the weir or barrage floor. The force of percolating water removes the soil particles by scouring at the point of emergence.
(a) Failure by Piping or undermining
The percolating water exerts an upward pressure on the foundation of the weir or barrage. If this uplift pressure is not counterbalanced by the self weight of the structure, it may fail by rapture.
(b) Failure by Direct uplift
The water seeping below the body of the hydraulic structure, endanger the stability of the structure and may cause its failure, either by
Failure by Subsurface Flow
9

## Slide 11
Gradient at the exit end is called exit gradient (GE) which is determined from the equation below:
Exit gradient (GE)
3. Khosla’s theory of seepage flow
b
ΔH
In this method. a composite weir or barrage section is split up into a number of simple standard forms where analytical solutions are known
10

## Slide 12
Set by: Othman K. Mohammed
No | Type of Soil | Gs
1 | Shingle | 
2 | Coarse Sand | 
3 | Fine Sand | 
No | Type of Soil | Gs
1 | Shingle | 
2 | Coarse Sand | 
3 | Fine Sand | 
Values of Khosla’s Safe Exit Gradient for different types of Soils
In order to keep the structure safe against piping.

## Slide 13
b
ΔH
Straight horizontal floor of negligible thickness with Pile at downstream end.
Uplift Coefficients at Key Points in Standard forms
11

## Slide 14
b
ΔH
Straight horizontal floor of negligible thickness with Pile at upstream end.
Set by: Othman K. Mohammed

## Slide 15
b1
b2
ΔH
Straight horizontal floor of negligible thickness with Pile at intermediate points.
12

## Slide 16
b
Straight horizontal floor of Depressed thickness below the bed (with no cutoff)
Set by: Othman K. Mohammed
do

## Slide 17
US
sheet pile
DS
sheet pile
Intermediate
sheet pile
Uplift Pressure Coefficients at Key Points
13

## Slide 18
Correction for floor thickness
The correction to the evaluated values at key points E and C that is applied considering a floor thickness t
Set by: Othman K. Mohammed
t
Corrections in Khosla’s theory
The pressures obtained at the key points by considering simple profile are then corrected for the following:

## Slide 19
Correction for mutual interference of sheet piles
The correction C for interference of one sheet pile on the other.
Where,
D = vertical distance measured from the key point to the bottom of the interfering sheet pile.
b′ = The horizontal distance between two pile lines
d = The depth of the pile on which the effect is considered
b = Total floor length
Note: Mutual Interference corrections are:
    (+) for points (C)
    () for points (E)
14

## Slide 20
b
Set by: Othman K. Mohammed

## Slide 21
b
15

## Slide 22
b
Set by: Othman K. Mohammed

## Slide 23
b
16

## Slide 24
Correction for slope of the floor
bs is the horizontal length of the slope
b’ is the distance between the two pile lines between which the sloping floor is located.
Set by: Othman K. Mohammed
Notes: This correction is This correction is taken as
  (+) for the downward slope
  () for the upward slope
+
This correction is applicable only to the key points of the pile line fixed at the Start or the End of the slope.

## Slide 25
Slope H : V | 1 : 1 | 2 : 1 | 3 : 1 | 4 : 1 | 5 : 1 | 6 : 1 | 7 : 1 | 8 : 1
 | 0.112 | 0.065 | 0.045 | 0.033 | 0.028 | 0.025 | 0.023 | 0.02
Slope H : V | 1 : 1 | 2 : 1 | 3 : 1 | 4 : 1 | 5 : 1 | 6 : 1 | 7 : 1 | 8 : 1
 | 0.112 | 0.065 | 0.045 | 0.033 | 0.028 | 0.025 | 0.023 | 0.02
H
V
17

## Slide 26
Uplift Pressure Coefficients at Intermediate Points
Set by: Othman K. Mohammed

## Slide 27
In the glacis type of weirs, a hydraulic jump is formed on the d/s glacis. In this case, the water surface profile in the hydraulic jump trough is much lower than the subsoil H.G.L. Therefore uplift pressure occurs on the glacis. This uplift pressure is known as the suction pressure. If the thickness of floor is not adequate, the rupture of floor may occur.
Set by: Othman K. Mohammed
(c) Failure by Hydraulic Jump
CHAPTER THREE
HYDRAULIC JUMP AND ENERGY DISSIPATION DEVICES

## Slide 28
Hydraulic jump
When the water flows with a very high velocity over the crest of a weir or under the gates of a barrage, the hydraulic jump develops.
Glacis
Crest level
US Floor level
DS Floor level
DS Water level
US Water level
Point of Jump formation (O)
19
Hydraulic Jump

## Slide 29
HL
DS TEL
US TEL
HL
DS TEL
D1
D2
Ef1
Ef2
O
Pre-Jump profile
Post-Jump profile
Va
Level of Jump formation
Set by: Othman K. Mohammed

## Slide 30
The location of hydraulic jump and the profile of water surface on the u/s and d/s of the point at which the jump is formed are required. The basic relations for a hydraulic jump are
Hydraulic Jump Expressions
20

## Slide 31
For known discharge intensity q, and the difference in the levels of the upstream and downstream levels of total energy line, HL determine the downstream specific energy, Ef2, Using Blench’s curves.
The location of the jump on a glacis can then be obtained by finding the intersection of the glacis with the horizontal plane Ef2 below the downstream level of the total energy line.
Location of Hydraulic Jump Formation on Glacis
Set by: Othman K. Mohammed

## Slide 32
Plotting water surface profile before the jump
Divide the glacis up to point (O) into several intervals and determine elevation of that point on the glacis.
Determine the value of specific energy Ef at these points from the relation
Form Montague curve for q and Ef read (D) on the supercritical side.
Determine the water surface level from:
21

## Slide 33
HL
DS TEL
US TEL
HL
DS TEL
O
D2
D1
Join the water levels determined in step 4 by smooth carve to obtain the prejump water surface profile
Set by: Othman K. Mohammed

## Slide 34
Determine the square of Froude number () of the incoming flow from the relation
Divide the D/S from point (O) into several intervals into a distance 5 to 6 (D2 – D1).
Determine the horizontal distances (x) of these points from the point (O) . Determine the values of () for each point.
Determine the values of () for each point for the given values of () and (x/D1) from the curve.
Determine the depth D for that points from () values and obtain the water surface levels.
Join the water surface levels to obtain the post-jump profile .
Plotting water surface profile after the jump
22

## Slide 35
HL
DS TEL
US TEL
HL
DS TEL
D1
D2
O
Set by: Othman K. Mohammed

## Slide 36
Chart: 
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 8 | 10 | 12 | 14 | 15 | 16 | 18 | 20 | 22 | 25 | 28 | 30
2 | 1 | 1.2 | 1.35 | 1.45 | 1.5 | 1.5
3 | 1 | 1.22 | 1.48 | 1.63 | 1.74 | 1.8 | 1.85 | 1.93 | 1.98 | 2 | 2
4 | 1 | 1.25 | 1.6 | 1.8 | 1.97 | 2.1 | 2.2 | 2.4 | 2.48 | 2.49 | 2.5 | 2.5
6 | 1 | 1.28 | 1.65 | 1.9 | 2.11 | 2.3 | 2.48 | 2.7 | 2.84 | 2.92 | 2.95 | 2.99 | 3 | 3.01 | 3.05 | 3.09 | 3.1 | 3.11 | 3.11
8 | 1 | 1.3 | 1.7 | 2 | 2.25 | 2.5 | 2.75 | 3 | 3.2 | 3.35 | 3.4 | 3.48 | 3.5 | 3.52 | 3.6 | 3.67 | 3.7 | 3.72 | 3.72
10 | 1 | 1.3 | 1.7 | 2 | 2.26 | 2.53 | 2.78 | 3.07 | 3.34 | 3.56 | 3.66 | 3.74 | 3.79 | 3.84 | 3.94 | 4.02 | 4.07 | 4.11 | 4.14
15 | 1 | 1.3 | 1.7 | 2 | 2.3 | 2.6 | 2.85 | 3.25 | 3.7 | 4.1 | 4.3 | 4.4 | 4.5 | 4.65 | 4.8 | 4.9 | 5 | 5.1 | 5.18
20 | 1 | 1.3 | 1.7 | 2 | 2.3 | 2.6 | 2.85 | 3.25 | 3.7 | 4.1 | 4.35 | 4.47 | 4.58 | 4.83 | 5.03 | 5.2 | 5.42 | 5.6 | 5.7
30 | 1 | 1.3 | 1.7 | 2 | 2.3 | 2.6 | 2.85 | 3.25 | 3.7 | 4.1 | 4.45 | 4.6 | 4.75 | 5.2 | 5.5 | 5.8 | 6.25 | 6.6 | 6.75
60 | 1 | 1.4 | 1.8 | 2.05 | 2.4 | 2.7 | 2.95 | 3.35 | 3.8 | 4.2 | 4.55 | 4.75 | 4.95 | 5.3 | 5.7 | 6.1 | 6.7 | 7.2 | 7.5
23

## Slide 37
Set by: Othman K. Mohammed

## Slide 38
24

## Slide 39
Uplift Pressure Under The Hydraulic Structure
Plotting the Subsoil Hydraulic Gradient Line
The elevation of the subsoil hydraulic gradient line above the bottom of the floor at any point measures the uplift pressure at that point
Set by: Othman K. Mohammed

## Slide 40
Subsoil Hydraulic Grade Line at Static Condition
HGL
26

## Slide 41
Subsoil Hydraulic Grade Line at Dynamic Condition
HGL
Set by: Othman K. Mohammed

## Slide 42
Unbalanced Static Head
or
or
Unbalanced Region
Balanced Region
27

## Slide 43
Unbalanced Dynamic Head
Unbalanced Region
Set by: Othman K. Mohammed
Balanced Region

## Slide 44
The floor should have appropriate thickness to counteract the uplift pressure acting on it.
At selected point let the uplift pressure is U which is the subsoil H.G.L. measured from the top surface of the floor.
Floor Thickness
T
A
F2
F1
h
28