## Slide 1: Erythrocyte Sedimentation Rate

## Slide 2
The erythrocyte sedimentation rate (ESR), also called a sedimentation rate, it measures the rate of erythrocytes settling in diluted human plasma over a specified time period (1 hour).
It is a relatively simple, inexpensive, non-specific test that has been used for many years to help detect inflammation associated with conditions such as infections, cancers, and autoimmune diseases.

## Slide 3
Principle
When anticoagulated blood is allowed to stand in a narrow vertical glass tube, undisturbed for a period of time, the RBCs – under the influence of gravity- settle out from the plasma. The rate at which they settle is measured as the number of millimeters of clear plasma present at the top of the column after one hour (mm/hr)

## Slide 4
This mechanism involves three stages:
Stage of aggregation: The RBC aggregate to Rouleaux formation. It occurs in the first 10-15 minutes.
Stage of sedimentation: It is the stage of actual falling of RBCs in which sedimentation occurs at constant rate. This occurs in 30-40 minutes out of 1 hour
Stage of packing: This is the final stage and is also known as stationary phase. In this stage, there is a slower rate of falling because of packing and accumulation(packing) of RBCs in bottom of the tube. It occurs in final 10 minutes

## Slide 5
The ESR is directly proportional to the RBC mass and inversely proportional to plasma viscosity
In normal whole blood, RBCs do not form rouleaux; the RBC mass is small and therefore the ESR is decreased (cells settle out slowly), while in abnormal conditions when RBCs can form rouleaux, the RBC mass is greater, thus increasing the ESR (cells settle out faster).

## Slide 6
The aggregated RBCs in the rouleaux formation have a higher ratio of 'mass to surface area' as compared to single RBCs and hence sink faster in plasma.

## Slide 7
Adults Normal values
Children: 0-10 mm\hr
Women: 0-20 mm\hr
Men: 0-15 mm\hr Above 50 years 0-30 mm/h
Above 50 years 0-20 mm/h

## Slide 8
Factors affecting on the rate of RBC settling
Biological factors
  Hematologic factor
  Proteins factors (Rate of rouleaux formation)
  Miscellaneous factors
Physical factor: room temperature, tilted ESR tube, vibration, bubbles in ESR column.

## Slide 9
Hematologic factors | Increases ESR | Decreases ESR
RBC count | anemia | polycythemia
RBC shape | Microcytosis | Macrocytosis, spherocytosis
WBC count |  | Extremely high WBC
Protein factors |  | 
fibrinogen | hyperfibrinogenemia | Hyporfibrinogenemia, dysfibrinogenemia
Other serum proteins | Increased alpha-globulins , beta-globulins and gamma- globulins | hypogammaglobulinemia
Miscellaneous factors |  | 
temperature | fever | hypothemia
Serum cholesterol | High serum cholesterol | 
Gender of patient | Females specially during prignancy | 
Age of patient | Advanced age | 

## Slide 10
Methods
1- Westergren’s method
2- Wintrobe’s method
3- Automated method

## Slide 11
Westegren’s method
The Westergren’s method is preferred by National Committee for Clinical Standards (NCCLS) because of its simplicity and greater distance of sedimentation measured in the longer Westergren tube. The straight tube is 30 cm long, 2.5 mm in internal diameter, and calibrated in millimeters from 0-200. Approximately 1 mL of blood is required.

## Slide 12
Glass tubes can be re-used provided that they are adequately cleaned by washing through with water, followed by alcohol, and then allowed to dry overnight. Specially made racks with a scale graduated in mm from 0 to 140 are available and these have adjustable leveling screws for holding the tubes in an exactly vertical position. It is conventional to set up sedimentation rates at room temperature (18 - 25oC).

## Slide 13
The test is performed on venous blood diluted accurately with 3.8 % trisodium citrate in the proportion of one volume of citrate to four parts of blood. It should be carried out within two hours of collecting the blood.

## Slide 14
Under aseptic conditions withdraw (1.6 ml) of blood from a vein and mix with (0.4 ml) of 3.8% sodium citrate (anticoagulant) (4:1) in test tube.
Mix the contents of test tube gently.
Fill the Westergren’s tube to 0 mark.
Set up the Westergren’s tube right in a stand with a spring clip on top and rubber at bottom.
Leave undisturbed for 60 min.
At the end of the hour read the height of clear plasma above the upper margin of the column of sedimenting cells to the nearest millimeter?
Report this measurement as the ESR (Westergren) in units of mm in 1 hour
Procedure

## Slide 16
Sources of error
Specimen older than specified time after collection and before testing
Incorrect proportion of anticoagulant
Incorrect type of anticoagulant
Haemolysed sample
Contaminated sedimentation tubes
Tubes tilted during sedimentation
Test set up near central heating or direct sunshine
Test set up adjacent to centrifuge or other instrument causing vibration Failure to read at exactly one hour.

## Slide 17
Causes of a significantly raised ESR :
  All types of anemias except sickle cell anemia
  Acute and chronic inflammatory conditions and infections including: – HIV disease – Tuberculosis – Acute viral hepatitis – Arthritis – Bacterial endocarditis – Pelvic inflammatory disease – systemic infection
  Pregnancy
Myocardial infarction
  Systeic lupus erythematosus
Myelomatosis, lymphoma, multiple myeloma
  Hodgkins disease, some tumours

## Slide 18
Causes of Reduced ESR
Polycythaemia
Poikilocytosis
Congestive heart failure
Newborn infants
Dehydration
Sickle cell anemia

## Slide 19: Important
Erythrocyte sedimentation rate is a non-specific test and is not diagnostic of any particular disease. It has a high sensitivity but low specificity. Never base a diagnosis solely on an ESR value, either normal or high.
Interpretation of the result should always be along with the patient's clinical history, examination findings and results of other tests done.
If high ESR is encountered without any obvious reasons, patient should be reassured and the test repeated after a reasonable amount of time (a couple of months).

## Slide 20
ESR and C-reactive protein (CRP) are both markers of inflammation.
Generally, ESR does not change as rapidly as does CRP, either at the start of inflammation or as it goes away.
CRP is not affected by as many other factors as is ESR, making it a better marker of inflammation.
However, because ESR is an easily performed test, many doctors still use ESR as an initial test when they think a patient has inflammation.