## Slide 1: Practical Ppllution
COD
Lab .8

## Slide 2
Determination of Chemical Oxygen demand(COD) in water
Chemical oxygen demand (COD) is a measure of the quantity of oxygen consumed in the oxidation of a sample chemically under defined condition or required to oxidize all organic materials. The high level of the COD documented or indicates that the water is polluted.

## Slide 3
The contamination may be due to domestic materials or substances that are released into the water body either directly or indirectly, the extent of oxidation depended on the nature of the oxidable substance, the pH, the temperature, reaction time.

## Slide 4
COD is an important and rapidly measured variable for characterizing water bodies, sewage, industrial wastes and treatment plant effluents. Generally, COD is higher than BOD values because more compounds can be chemically oxidizing than can be biologically oxidizing.

## Slide 5
Principle
Potassium permanganate has been used for long time as oxidizing agent for the determination of organic compounds in water and waste water, this method is only used for slightly contaminated surface water or preliminary testing of drinking water because it has low organic compounds and used only particularly oxidizing process.

## Slide 6
Reagents:
-Potassium permanganate solution
-oxalic acid
-sulfuric acid (H2SO4 %36)
β(KMnO4)= (a-b) × t × 316 ̸ v
a: ml of KMnO4 consumed by sample.
b: ml ofKMnO4 consumed by blank.
t: titration factor =1
V: volume of sample by ml.