## Slide 1
Bearing Capacity of
Shallow Foundation

## Slide 2
Ultimate Bearing Capacity of Shallow Foundation:
To perform satisfactorily, shallow foundations must have two main characteristics:
1. They have to be safe against overall shear failure in the soil that supports them.
2. They cannot undergo excessive or settlement. (The term excessive I relative, because the degree of settlement allowed for a structure depends on several considerations.)
The load per unit area of the foundation at which shear failure in soil occurs is called the ultimate bearing capacity
Mode of Bearing Capacity Failures:
Bearing capacity failures of foundations can be grouped into three categories
1- General shear failure.
2- Local shear failure
3- punching shear failure

## Slide 3
A strip foundation with a width of B resting on the surface of a dense sand or stiff cohesive soil, At a certain point when a sudden failure in the soil supporting the foundation will take place, and the failure surface in the soil will extend to the ground surface 3.1a. This load per unit area, is usually referred to as the ultimate bearing capacity qu of the foundation. When such sudden failure in soil takes place, it is called general shear failure.
If the foundation under consideration rests on sand or clayey soil of medium compaction. A considerable movement of the foundation is required for the failure surface in soil to extend to the ground surface 3.1b. The load per unit area at which this happens is the ultimate bearing capacity, qu. Beyond that point, an increase in load will be accompanied by a large increase in foundation settlement. The load per unit area of the foundation, is referred to as the first failure load. Note that a peak value of q is not realized in this type of failure, which is called the local shear failure in soil.
If the foundation is supported by a fairly loose soil, the load–settlement plot will be like the one in Figure 3.1c. In this case, the failure surface in soil will not extend the ground surface. Beyond the ultimate failure load, the load–settlement plot will be steep and practically linear. This type of failure in soil is called the punching shear failure.

## Slide 4
The Terzaghi Bearing-Capacity Equation
Terzaghi suggested that for a continuous, or strip, foundation (i.e., one whose width to-length ratio approaches zero), the failure surface in soil at ultimate load may be assumed to be similar to that shown in the Figure. The failure zone under the foundation can be separated into three parts :
1. The triangular zone ACD immediately under the foundation
2. The radial shear zones ADF and CDE, with the curves DE and DF being arcs of a logarithmic spiral
3. Two triangular passive zones AFH and CEG.
Figure 3.3 Bearing capacity failure in soil under a rough rigid
continuous (strip) foundation
qult = cNc+ qNq+ 0.5gBNg ….. 3.1
(For strip footings, such as wall foundations)
For (vertical load- no eccentricity – horizontal ground – horizontal base)
Where, Nc , Nq and Ng are the soil-bearing capacity factors, dimensionless terms, whose values relate to the angle of internal friction .

## Slide 5
The bearing capacity factors are defined by
………. 3.2
……….. 3.3
………. 3.4
Where the Kpg values and variation of the bearing capacity factors which defined by equations (3.2), (3.3) and (3.4) are given in table (3.1)
qult = 1.3cNc+ qNq+ 0.4gBNg ……. 3.5
(For square footings, typical of interior columns)
qult = 1.3cNc+ qNq+ 0.3gBNg ……. 3.6
(For circular footings, such as towers, chimneys)
In equation (3.5), B equals to dimension of each side of the foundation in equation (3.6), B equals the diameter of the foundation.

## Slide 6
,, and the modified bearing capacity factors, can be calculated by using the bearing capacity factor equations (for , , and , respectively) by replacing
For foundations that exhibit the local shear failure mode in soils, Terzaghi suggested that the following modifications to equations (3.1), (3.5) and (3.6)

## Slide 7
Example 1
A square foundation is 1.5 m x 1.5 m in plan. The soil supporting the foundation has a friction angle of = 20° and c = 15.2 kN/m². The unit weight of the soil, = 17.8 kN/m3. Assume that the depth of the foundation is (1 m) and that general shear failure occurs in the soil. Compute the ultimate bearing capacity of the soil. Use Terzaghi’ Method.
Solution:
For square footing use
qult = 1.3cNc+ qNq+ 0.4gBNg
For Ø=20° from table 3-1
Nc =17.7 Nq =7.40 Ng =5
qu=(1.3)(15.2)(17.69)+(1x17.8)(7.4)+(0.4)(17.8)(1.5)(5)
=349.55+131.72+53.4= 534.67kN/m2
Example 2
A circular foundation with 2m diameter. The soil supporting the foundation has Ø = 20° and c = 25 kN/m². The unit weight of the soil, . Assume that the depth of the foundation is (1 m) and that local shear failure occurs in the soil. Compute the ultimate bearing capacity of the soil. Use Terzaghi’ Method.
Solution:
For circular footing (local shear failure)
qult = 0.867cNc+ qNq+ 0.3g BNg
For Ø = 20°
Nc=11.85 Nq=3.88 N=2.13
qu= 0.867(25)(11.85)+(1x18)(3.88)+0.3(18)(2)(2.13)
= 256.8+69.8+23
=349.6 kPa

## Slide 8
Allowable Bearing Capacity qall :
qall is the permissible soil pressure which keeps the footing safe against shear failure
where F.S is factor of safety against bearing capacity ranges between(2 – 4 )average of (3) is commonly used in most designs.
There are more uncertainties in determining the allowable strength of the soil than in the superstructure elements. A number of these uncertainties may be summarized as follows:
1- Complexity of soil behavior
2- Lack of control over environmental changes after construction
3- Incomplete knowledge of subsurface conditions
4-Inability to develop a good mathematical model for the foundation
5- Inability to determine the soil parameters accurately

## Slide 9
Effect of Water Table on Bearing Capacity
If the water table is close to the foundation, some modifications of the bearing capacity equations will be necessary. (See the Figure 3.4)
Figure 3.4 Modification of bearing capacity equations for water table

## Slide 10
Meyerhof Equation
(vertical or inclined load- eccentricity – horizontal ground – horizontal base)
qult= cNc sc dc+ q Nq sq dq+ 0.5  B N s d for vertical load
qult= cNc dc ic+ q Nq dq iq+ 0.5  B N d i for inclined load

## Slide 11
Table 3.2
Bearing-capacity factors for the Meyerhof, Hansen, and Vesic bearing capacity equations

## Slide 12
Table 3.3
Shape, depth, and inclination factors for the Meyerhof bearing-capacity equations of Table 3.2

## Slide 13
Hansen Equation
(vertical or inclined load- eccentricity – horizontal. or slope ground – horizontal or slope base)
qult= cNc sc dc ic gc bc+ q Nq sq dq iq gq bq + 0.5  BNsdig b
for general
When
;
qult= 5.14cu (1+sc +dc -ic - bc-gc )+ q
Nc, N , Nq = bearing capacity factors see Tables 3.2 or by the following equations
c= cohesion of the soil ,q or q= overburden pressure at footing base,
 or  = density of foundation soil
B = least dimension of the footing (width)
sc, dc, ic ,gc ,bc ,sq, dq, iq ,gq, bq, ,s ,d, i ,g, b : are shape, depth, inclination, ground , and foot base factors from table 3.4 & 3.5.

## Slide 14
The ultimate bearing capacity for footings with eccentricity, using either the Meyerhof or Hansen equations, is found in either of two ways:
Method 1.
Use either the Hansen bearing-capacity equation with the following adjustments:
a. Use B' in the BN term.
b. Use B' and L' in computing the shape factors
c. Use actual B and L for all depth factors. The computed ultimate bearing capacity qult is then reduced to an allowable value qall with an appropriate safety factor SF as qall = qult/SF
Method 2.
Use the Meyerhof general bearing-capacity equation and a reduction factor Re used as quIt, = quIt, comp * Re
it should be used only with the Meyerhof equation to compute the bearing capacity. The original Meyerhof method gave reduction curves; however, the following equations are suitable for obtaining the reduction factor:
Re = 1 - 2e/B (cohesive soil)
Re = 1 – (e/B)1/2 (cohesionless soil and for 0 < e/B < 0.3)
Alternatively, one may directly use the Meyerhof equation with B' and L' used to compute the shape and depth factors and B' used in the 0.5gB'Ng term.

## Slide 15
Example 3
A footing load test made by a designer produced the following data:
D = 0.5 m B = 0.5 m L = 2.0 m
g' = 9.31 kN/m3 Ø triaxial= 42.5° Cohesion c = 0
Pult = 1863 kN (measured) , qult = 1863/(0.5x2)=1863 kPa (computed)
Required
Compute the ultimate bearing capacity by both Hansen and Meyerhof equations and compare these values with the measured value.
Use Hanson equation
Since c = 0, any factors with subscript c do not need computing. All g,i and b factors are 1.00; with these factors identified, the Hansen equation simplifies to
qult= q Nq sq dq iq gq bq + 0.5  B N s d i g b
LIB = 2/0.5 = 4
Øps = 1.5(42.5) - 17 = 46.75°
Use Ø = 47°
From Hanson equations table 3-5 for Ø=47 obtain
Nq=187 N=299
Calculate s factor
sq = 1 + B’/L’ sin Ø eqn. from table 3-6
=1+ (0.5/2) sin47 = 1.18
sg = 1 - 0.4 (B’/L’) eqn. from table 3-6
= 1- 0.4 (0.5/2) = 0.9 ≥ 0.6
Calculate d factor
k=(D/B) for (D/B)≤1 0.5/0.5=1
dq= 1+2tan Ø(1-sinØ)2 (D/B)
= 1+0.155 (D/B)
= 1+0.155 (0.5/0.5) =1.155
d=1 for all Ø
qult=9.31(0.5)(187)(1.18)(1.155)+0.5(9.31)(0.5)(299)(0.9)(1)=1812kPa

## Slide 16
Using Meyerhof equation
By the Meyerhof equations of Table 3-5 , and Øps= 47°,
we can proceed as follows Nq=187
N=(Nq-1)tan(1.4 Ø)
N=(187-1)tan(1.4 x47)
=413.8=414
Kp=tan2(45+ Ø/2)=6.44
calculate s factors
sq= s= 1+ 0.1Kp(B/L) = 1+0.1( 6.44)(0.5/2)=1.16
calculate d factors
dq= d = 1+ 0.1(Kp)1/2(D/B) = 1+0.1( 2.54)(0.5/0.5)= 1.25
Substitute into the Meyerhof equation (ignoring any c subscripts):
qult= q Nq sq dq+ 0.5  B N s d
qult= 9.31(0.5)(187)(l.16)(1.25) + 0.5(9.31)(0.5)(414)(1.16)(1.25)
=2659kPa
Example 4
A square footing 1.8mx1.8m is loaded with an axial total column load of 1820kN at center and Mx=275kN.m,My=165kN.m. The column size is 0.4mx0.4m. Undrained triaxial test give Ø= 36o and c=9kPa. The foundation base is at 1.8m depth the soil has g= 15.6kN/m3 and the water table is at 6m depth. What is the allowable gross qall if factor of safety =3 is required against shear failure use:
1- Hanson B.C equation and the effective area method.
2- Meyerhof B.C equation and the eccentricity reduction factor.

## Slide 17
Solution:
1-Using Hanson BC equation
qult= cNc sc dc ic gc bc+ q Nq sq dq iq gq bq + 0.5  B N s d i g b
From table 3-3 for Ø= 36o Nc=50.55 Nq= 37.7 N= 40
Bʹ= B- 2e L= L- 2e eB= 275/1820=0.15m
eL= 165/1820=0.09m
L = 1.8 - 2x.09 = 1.62m Bʹ = 1.8 -2x0.15 = 1.5m
For h=0 all b factors will equal to 1
For b=0 all g factors will equal to 1
The resultant of all load is vertical so HB and HL =0 all (i) factors are 1
The overburden soil is above W.T  eff. = tot. = 15.6kN/m3
Determine S factors
sc= 1+(Nq/Nc). (B’/L’)
sc= 1+(37.7/50.5)(1.5/1.62)=1.69
sq = 1 + (B’/L’) sin Ø
sq= 1+(1.5/1.62) sin36=1.54
sg = 1 - 0.4 (B’/L’)
=1-0.4 (1.5/1.62)= 0.62> 0.6
determine d factor
dc= 1+0.4k
k= D/B for D/B≤1
dc= 1+0.4 (1.8/1.8) = 1.4
dq= 1+2tan Ø(1-sinØ)2 k
dq=1+2tan36(1- sin 36)2 1
= 1+0.247= 1.247
d=1 for all Ø
qult=9(50.55)(1.69)(1.4)+1.8(15.6)(37.7)(1.54)(1.247)
+0.5(15.6)(1.5)(40)(0.62)(1)
1076+2033+290=3399kPa
Allowable BC qall= 3399/3=1133kPa

## Slide 18
2- Meyerhof B.C equation
qult= cNc sc dc+ q Nq sq dq+ 0.5  B N s d
For Ø = 36 from table3-3 Nc=50.55 Nq=37.8 N=44.4
sc= 1+ 0.2Kp(B/L)
Kp=tan2(45+ Ø/2)= tan2(45+18)=3.84
sc= 1+0.2(3.84)(1.8/1.8)=1.77
sq= s= 1+ 0.1Kp(B/L)
=1+0.1(3.84)(1.8/1.8)=1.39
d factor
dc = 1+ 0.2 Kp1/2 (D/B)
= 1+ 0.2 (3.84)1/2 (1.8/1.8)= 1.39
dq= d = 1+ 0.1 Kp1/2 (D/B)
=1+0.1(3.84)1/2(1.8/1.8)= 1.2
qult= 9(50.55)(1.77)(1.39)
+1.8(15.6)(37.8)(1.39)(1.2)
+0.5(15.6)(1.8)(44.4)(1.39)(1.2)
=1119.3+1770+1039=3929kPa
Allowable BC qall= 3929/3=1309kPa
ReB=1-(eB/B)1/2=1-(0.15/1.8)1/2=0.71
ReL=1-(eL/L)1/2= 1- (0.09/1.8)1/2=0.77
qall= qall. ReB. ReL= 1309(0.71)(0.77)= 715.6kPa

## Slide 19
Using the Inclination Factors
In the general case of inclined loading there is a horizontal component parallel to each base dimension defined as
Hi = HB parallel to the B dimension
For HB = 0 ; ic,B , iq,B , ig,B are all 1.0
Hi = HL parallel to the L dimension
For HL = 0 ; ic, L , iq, L , ig, L are all 1.0
These Hi values are used to compute inclination factors for the Hansen equation as follows.
dq,B= 1+2tan Ø(1-sinØ)2 D/B dq,L= 1+2tan Ø(1-sinØ)2D/L
dc,B= 1+0.4(D/B) dc,L= 1+0.4(D/L)
dc,B= 1+0.4tan-1(D/B) dc,L= 1+0.4tan-1(D/L)
sq,B = 1 + (Bʹ iq,B/L ʹ) sin Ø sq,L = 1 + (Lʹ iq,L/B ʹ) sin Ø
sg ,B= 1 - 0.4 (Bʹ ig,B/Lʹ ig,L) sg ,L= 1 - 0.4 (Lʹ ig,L/Bʹ ig,B)
sg,I ≥ 0.6 (if less than 0.6 use 0.6)
sc,B= 1+(Nq/Nc). (Bʹ ic,B/Lʹ) sc,L= 1+(Nq/Nc). (Bʹ ic,L/Bʹ)
ic,B= iq,B-{(1-iq,B)/(Nq-1)} ic,L= iq,L-{(1-iq,L)/(Nq-1)}
iq,B= {1- (0.5HB)/( V + Af Ca cot Ø)}α1 iq,L= {1- (0.5HL)/( V + Af Ca cot Ø)}α1
ig,B= {1- (0.7HB)/( V + Af Ca cot Ø)}α2 ig,L= {1- (0.7HL)/( V + Af Ca cot Ø)}α2
These are used in the following modifications of the "edited" Hansen bearing capacity equation
qult,B= cNc sc,B dc,B ic,B gc,B bc,B + q Nq sq,B dq,B iq,B gq,B bq,B + 0.5  B N s,B d,B i,B g,B b,B
qult,L= cNc sc,L dc,L ic,L gc,L bc,L + q Nq sq,L dq,L iq,L gq,L bq,L + 0.5  L N s,L d,L i,L g,L b,L

## Slide 20
Example 5
You are given the data shown on the sketch of a load test
HL,ult = 382 kN, Vult = 1060 kN
Required: Find the ultimate bearing capacity by the Hansen method.
Øps = 1.50 Øtri - 17° = 1.5(43) - 17 = 47.5°
Use Øps = 47°.
Nq = 187 Ng = 299
Nc=(Nq-1)cot Ø
=(187-1)cot47=174
2tan Ø(1-sinØ)2 =0.155 Nq/Nc=187/174=1.07
All bi = gi = 1.0 , since both the base and ground are horizontal.
dq,B= 1+2tan Ø(1-sinØ)2 D/B
1 + 0.155(0.5/0.5) = 1.16
dq,L= 1+2tan Ø(1-sinØ)2D/L
= 1 + 0.155(0.5/2.0) = 1.04
dg,B = dg,L = 1
iq,B= {1- (0.5HB)/( V + Af Ca cot Ø)}α1=1
ig,B= {1- (0.7HB)/( V + Af Ca cot Ø)}α2= 1
iq,L= {1- (0.5HL)/( V + Af Ca cot Ø)}α1
iq,L= {1- (0.5*382)/( 1060 + 0)}2.5=0.608

## Slide 21
ig,L= {1- (0.7HL)/( V + Af Ca cot Ø)}α2
ig,L= {1- (0.7*382)/( 1060 + 0)}2.5=0.361
sq,B = 1 + (B’ iq,B/L ’) sin Ø
sq,B = 1 + (0.5*1/2) sin 47=1.18
sq,L = 1 + (L’ iq,L/B ’) sin Ø
sq,L = 1 + (2*0.608/0.5) sin 47=2.78
sg ,B= 1 - 0.4 (B’ ig,B/L’ ig,L)
=1 - 0.4[(0.5 x l)/(2 x 0.361)] = 0.723 > 0.6
sg ,L= 1 - 0.4 (L’ ig,L/B’ ig,B)
= 1 - 0.4[(2 X 0.361)/(0.5 X I)] = 0.422 < 0.6 (use 0.60)
qult= cNc sc dc ic gc bc+ q Nq sq dq iq gq bq + 0.5  B N s d i g b
qult,B=q Nq sq,B dq,B iq,B + 0.5  B N s,B d,B i,B
= 0.5(9.43)(187)(1.18)(1.16)(l) + 0.5(9.43)(0.5)(299)(0.732)(l)(l)
= 1206.9 + 511.3 = 1718.2 1700kPa
qult,L=q Nq sq,L dq,L iq,L + 0.5  B N s,L d,L i,L
= 0.5(9.43)(187)(2.78)(1.04)(0.608) + 0.5(9.43)(2.0)(299)(0.60)(1.0)(0.361)
= 1549.9 + 612.76 = 2162.7 215OkPa
Use the smaller computed value, we find the Hansen method seems to give qult = 1700 kPa » 106OkPa of load test.