## Slide 1
Determination of liquid mixture composition by refractive index
Refractive index (R.I.) of a material: is the ratio of the velocity of light in vacuum to the velocity of light in the material
the R.I. can be defined as the ratio of the sin of the angle øv, which a ray of light makes with a normal to the surface in vacuum, to the sin of the angle øm in the material
Composition: in a mixture of A&B a composition is defined as the quantity of each of A&B in that mixture.

## Slide 2
Fig(1) shows according
to a plane surface of
the medium
exposed to
vacuum
øv
Øm
Medium
Vacuum (or air)
Fig.1

## Slide 3
As angle øv increase, the angle øm increase, and reach its maximum value øm when the angle øv becomes equal to a right angle, when the incident light is horizontal, since Sin90º=1
If øv >90º the ray of light is totally internal.
Øm
Fig.2
øv
d
d

## Slide 4
Velocity of light is less in dielectric material than it is in vacuum, due to interaction of the electrons of the polarizable molecules of the medium with the oscillating electric field of the radiation.
R.I. is a function of:
  Wave length (λ): yellow sodium D line (λ =5890-5896 Aº).
  Temperature (T =20 or 25)ºC.
  Nature of the substance.
  Impurity .

## Slide 5
Most refractometers operate on the concept of critical angle øcrit.: this is the angle øm for which øv (or øair)is exactly 90º
There are 2 types of critical angle refractometers:
  Abbe refractometer: its advantage that is require about 0.05 ml of liquid.
  Pulfric refractometer: require about 1ml of liquid.

## Slide 6: Procedure:
V (C6H6) (ml) | V(CCl4) (ml) | R.I. | wtC6H6=d*v (gm) | wtCCl4=d*v (gm) | n C6H6 mole | n CCl4 mole | nt | X C6H6 | X CCl4
0.1 | 0.9 |  |  |  |  |  |  |  | 
0.3 | 0.7 |  |  |  |  |  |  |  | 
0.5 | 0.5 |  |  |  |  |  |  |  | 
0.7 | 0.3 |  |  |  |  |  |  |  | 
Add 0.1ml of C6H6 and 0.9ml of CCl4 in test tube.
Add (2-3) drops of the solution in test tube to the refractometer.
Then measure the R.I when you see half dark and half light.
Draw the calibration curve.

## Slide 7
  This curve is( calibration curve) used to determine the composition the unknowns.
R.I.
0 XA or XB 1