## Slide 1
University of Salahaddin
College of science
Department of physics
Nuclear Lab.
Second Course
2023-2024

## Slide 2: Radiation
Radiation is an energy in the form of electro-magnetic waves or particulate matter, traveling in the air.
The spectrum of electromagnetic radiation.
λ (m)
Non-ionizing radiation
Ionizing radiation

## Slide 3: Radiation
Ionizing Radiation
Higher energy electromagnetic waves (gamma and X-ray) or Light and heavy particles (beta and alpha).
High enough energy to eject electron from an atom.
Non-ionizing Radiation
Lower energy electromagnetic waves.
Not enough energy to eject electron from an atom, but can excite the electron.
Radiation is classified as:

## Slide 4
Ionizing
Excitation
High
energy
low energy
Interaction of Radiation with Matter

## Slide 5: Definition of Nuclear Radiation
Nuclear radiation is the energy emitted by an unstable nucleus to became more stable.
Fig. Unstable nucleus emits radiation
Unstable nucleus
Radiation
Particle
Energy

## Slide 6
Alpha particles
Beta-minus particle
Beta-plus particle
Gamma rays
Beta particles
Types of Nuclear Radiation
Nuclear Radiation

## Slide 7: Penetrating power and Absorption of Nuclear Radiation
Proton
Neutron
Electron
paper
aluminum
lead
Alpha particles
Beta particles
Gamma rays
Animation (1)

## Slide 8: Penetrating power and Absorption of Nuclear Radiation
Proton
Neutron
Electron
paper
aluminum
lead
Alpha particles
Beta particles
Gamma rays
Animation (1):
Penetration power and absorption of alpha, beta, and gamma rays.

## Slide 9
S
N
Magnetic field
(a)
(b)
Animation (2). Shows how the different types of radiation are affected by:
(a) Magnetic field. (b) Electric field.
Electric field
Effect of electric and magnetic fields on the nuclear radiation.
Notes: Effect of a magnetic an electric fields on alpha ,beta and gamma radiation.
Behavior of alpha ,beta and gamma rays in magnetic and electric field
The radiations emitted by the uranium mineral could be resolved into three types by the application of electrical field.
(a) The rays which deflected slightly towards –ve electrode were named as alpha (a) rays.
(b) The rays which deflected towards +ve electrode were named as beta (~) rays.
(c) The rays which remained undeflected were named as gamma (y) rays.

## Slide 10
Summary
Types of nuclear radiation | Alpha(α) | Beta(β) | Gamma(ɣ)
Structure |  |  | 
Charge | +2 |  | 0
Mass | Heavy | Light | Rest mass zero
Ionizing | strong | weak | Very weak
Effects of fields | deflected by magnetic and electric fields | deflected by magnetic and electric fields | not deflected by magnetic or electric fields
Penetration effect | Stopped by a piece of paper | Stopped by a few millimeters of aluminum | Stopped by a several centimeters of lead
2 Proton
2Neutron
EM waves
+
+
+
-
Electron
Positron
-1
+1
or
or

## Slide 11: Geiger Muller Detectors
wall
fill gas
R
Output
A
or
Anode (+)
Cathode (-)
End window
Or wall

## Slide 12: Scintillation Detectors

## Slide 13: General Radiation Safety
Reduce TIME of your exposure.
Increase DISTANCE from the source.
Make use of available SHIELDING.

## Slide 14
Exp. (1)
Verification of Inverse Square Law for -Ray
Purpose
The student will verify the inverse square relationship between the distance and intensity of radiation.
This intensity is given by
Where
N is the total number of photos /s from the source
A is the total area of the sphere in cm2.
Equation (3) is required form of the inverse square law
Chart: 1/d^2 cm-2
| 0.01 | 8.2644628099173556E-3 | 6.9444444444444441E-3 | 5.9171597633136093E-3 | 5.1020408163265302E-3 | 4.4444444444444444E-3 | 3.90625E-3 | 3.4602076124567475E-3 | 3.0864197530864196E-3 | 2.7700831024930748E-3 | 2.5000000000000001E-3
 | 3651 | 3119.5 | 2694.5 | 2353 | 2009.5 | 1811 | 1570 | 1385 | 1215 | 1100.5 | 1006.5

## Slide 15
Exp. (2)
Absorption coefficient for  - rays
Purpose
The purpose of the experiment is to measure experimentally the linear and mass absorption coefficient in lead and copper for 662 KeV gamma rays.
Where
I: intensity after the absorber.
I0: intensity before the absorber.
: linear mass absorption coefficient in cm-1.
x: is the thickness in cm

## Slide 16
Exp. (3)
Determining energy and range of beta particles in aluminum (13Al)
Purpose
To investigate the absorption of beta particles and determine the range and maximum energy of beta particles.
The range, R, will then be substituted into the empirical formula
Where
R is the of beta particle in material, expressed in (g/cm2). Em is the maximum energy of the beta particle emitted, expressed in (KeV).

## Slide 17
Exp. (4)
Activity measurement of Gamma – Source (relative method)
Purpose
The purpose of this experiment is to outline one procedure by which the activity of a source can be determined, called the relative method.
Chart: BLV/VOLT
| 0 | 0.3000000000000001 | 0.6000000000000002 | 0.9 | 1.2 | 1.5 | 1.8 | 2.1 | 2.4 | 2.7 | 3 | 3.3 | 3.6 | 3.9 | 4.2 | 4.5 | 4.8 | 5.0999999999999996 | 5.4 | 5.7 | 6 | 6.3 | 6.6
 | 7002 | 5855 | 3086 | 2687 | 2680 | 2662 | 2654 | 2867 | 3029 | 3718 | 4496 | 4437 | 3572 | 1958 | 819 | 360 | 4511 | 14467 | 15303 | 13487 | 3172 | 36 | 3
The activity is defined as the number of disintegration per second in radioactive sample.

## Slide 18
Exp. (5)
Foundation of material height in closed containers.
Purpose
The purpose of the experiment is to determine the material height in a closed container.
Introduction
The level of material (foods, dyes, oils,……) in closed containers can be determined by the -ray absorption method.
The absorption of -ray in air is different from its absorption in the container walls and also through the wall + material inside.

## Slide 19
Exp. (6)
Operating Plateau for the Geiger Tube
Purpose
To determine the plateau and optimal operating voltage of a Geiger-Müller counter.
The equation for slope is
where
R1 and R2 are the activities for the beginning and end points, respectively.
V1 and V2 and the voltages for the beginning and end points, respectively.