## Slide 1: Practical analytical chemistry Lab 5 Standardization of NaOH 1st Stage - Earth Sciences and Petroleum Department PHD. Hijran S. jabbar MSc. Sara H. Assaf Email: sara.assaf@su.edu.krd 2022-2023
Kurdistan Region – Iraq
Ministry of Higher Education and Scientific Research
Salahaddin University-Erbil
College of Science
Department of Chemistry
1st Stage

## Slide 2
Experiment No. 2
Preparation and standardization of approximately 0.1M sodium hydroxide (NaOH) using standardized hydrochloric acid (HCl)

## Slide 3
Sodium hydroxide are always coated with thin layer of sodium carbonate as a result of reaction of hydroxide with atmospheric carbon dioxide (CO2).
Pure sodium hydroxide cannot be obtained; so that a standard solution of NaOH cannot be prepared by dissolving a known weight in a definite volume of water. Therefore sodium carbonate should remove from sodium hydroxide before preparation of the solution. Several methods are available for this purpose:-

## Slide 4
1- Ba(OH)2 method:
A slight excess of barium hydroxide is added to the solution of NaOH to precipitate carbonate as BaCO3 (precipitation), then filtered the solution to remove the precipitate (Filtration).

## Slide 5
2-Anion exchange method
It involves passing NaOH solution through a column of a strongly basic anion exchanger which has higher affinity to carbonate anion CO3-2 than for hydroxide OH-. The carbonate is removed and replaced by OH- of the anion exchanger.

## Slide 6
Preparation of solutions
Prepare 250mL solution of an approximate 0.1M HCl
Prepare 250mL solution of an approximate 0.1M NaOH
Reaction:
NaOH + HCl NaCl + H2O

## Slide 7
Preparation of 250mL solution of approximate 0.1M NaOH
Dissolve 1.00 gm of NaOH in small amount of water then complete to 250 ml with distilled water to obtain 0.1M NaOH solution.
Wt.(g) = M x V(ml) x M.Wt./ 1000
Wt.(g) = 0.1 x 250 x 40 / 1000 = 1 g

## Slide 8
Procedure:

## Slide 9: Calculation: At the equivalence point: no. of mole HCl = no. of mole NaOH (M × V) HCl = (M × V) NaOH (0.1 × Vav) = (M × 10) M = (0.1 × Vav) / 10 = ( Z ) mol/L NaOH

## Slide 10
T
H
A
N
K
Y
O
U
Do you have any
question
or
comments?