## Slide 1: Essential Treatment Processes for Industrial Wastewaters and Reusing for Irrigation
Shawnm Mudhafar Saleh
Second International Conference of Engineering and Innovative Technology SU-ICEIT-2019

## Slide 2: Problem statement:
Untreated industrial wastewaters (WWs) such as food processing factories , dairy factory, Steel factory, beverage,.. ., etc. playing a significant role in environmental pollution.

## Slide 3: Objectives:
Characterization of dairy and Erbil Steel Factory WWs.
Adequate industrial wastewater Treatment processes.
Reuse industrial wastewater for irrigation.

## Slide 4: Site Description:
Yörüksüt Dairy Factory (YDF)
  Established in Erbil since 2013
  13 km far from Erbil city
  The geographical coordinate
    Latitude 36° 9' 46" N
    longitude 43° 51' 57" E
  357 meters above sea level
  Produces about 40-50 tons of yogurt and buttermilk per day.
Erbil Steel Company (ESC)
  located at the left side of Erbil-Guwer main road
  21.6 km far from Erbil City
  The geographical coordinate
    Latitude 36° 8' 20" N
    longitude 43° 47' 52" E
  produce 600 tons/day of steel.

## Slide 5: Site Description (Cont.): YDF & ESC

## Slide 6: Materials and methods (Cont.):
  pH(Mv)
  pH
  Oxidation-reduction potential (ORP) (mv)
  Dissolved oxygen (DO)(%)
  DO (mg/l)
  Electrical conductivity (EC) (μ mhoss/cm)
  EC (μ mhoss/cm2)
  Ω. Cm
  Total dissolved solids (TDS) (mg/l)
  Pressure (P) (PSU)
  P (mm Hg)
  Temperature (T) (°C)
  σt
  Nitrite (NO2)(mg/l)
  Chemical oxygen demand (COD) (mg/l)
  Color (Pt.Co)
  Ammonia (NH3-N) (mg/l)
  Nitrate (NO3) (mg/l)
  Total Acidity (mg/l)
  Total Alkalinity (mg/l)
  Chloride (Cl) (mg/l)
The samples tested for 21 water quality parameters include:
Wastewater from YDF and ESC were collected and immediately transported to the laboratory of
Sanitary And Environmental Engineering Laboratory, College Of Engineering, Salahaddin University, Erbil, Iraq, and stored in refrigerator at 4 °C.

## Slide 7: Characteristic of typical Industrial WW
Type of Wastewater | pH | TSS (mg/l) | BOD(mg/l) | COD(mg/l) | BOD/COD | TDS(mg/l)
Dairy Industry | 4 | 12150 | 4000 | 21100 | 0.19 | 19000
Yeast Industry | 5.3 | 540 | 2100 | 3400 | 0.62 | 35000
Fruits & Vegetable Canning | 5.5 | 2200 | 800 | 1400 | 0.57 | 1270
Textile Industry | 6.5 | 1800 | 840 | 1500 | 0.56 | 17000
Pulp & Paper Industry | 8 | 1640 | 360 | 2300 | 0.16 | 1980
Beverage Industry | 9 | 760 | 620 | 1150 | 0.54 | 1290
Tannery Industry | 10 | 2600 | 2370 | 4950 | 0.48 | 8500
Results and Discussion: 1) Characteristics of WWs

## Slide 8
No. | Tests | Dairy wastewater | Cooling Furnal Coils | Cooling Forms | Cooling Steel Bars
1 | pH (mv) | -140.7 | -184.6 | -224.7 | -164.7
2 | pH | 8.8 | 9.59 | 10.32 | 9.22
3 | ORP (mv) | -76.4 | -73.4 | -92.5 | -79.6
4 | DO (%) | 0.1 | 0.1 | 0.1 | 0.1
5 | DO (mg/L) | 0.01 | 0.01 | 0.01 | 0.01
6 | EC (μ mhoss/cm) | 659 | 3201 | 13.79 | 1834
7 | EC (μ mhoss/cma) | 453 | 2192 | 9072 | 1270
8 | Ω. Cm | 1515 | 313 | 73 | 546
9 | TDS (mg/l) | 330 | 1600 | 6887 | 916
10 | P (PSU) | 0.32 | 1.68 | 7.95 | 0.94
11 | P (mm Hg) | >20.4 | 720.5 | 720.5 | 720.5
12 | T (°C) | 8.75 | 8.41 | 7.09 | 8.87
13 | σt | 0.1 | 1.2 | 6.2 | 0.5
14 | NO2 mg/L | 81 | 1 | 18 | 10
15 | COD mg/L | 329 | 180 | 534 | 84
16 | Color Pt.co | 922 | 67 | 491 | 240
17 | NH3-N mg/L | 6 | 0 | 0.31 | 0
18 | NO3 mg/L | 23.8 | 4 | 3 | 1.4
19 | Total Acidity mg/L | 40 | 32 | 0 | 16
20 | Total Alkalinity mg/L | 244 | 240 | 676 | 156
21 | Chloride (Cl) mg/L | 27.99 | 699.78 | 2499.23 | 299.907
Characteristics of collected wastewater samples

## Slide 9
Different levels of treatment are required for wastewater treatment:
Preliminary treatment process
  Large solids and large materials in raw wastewater
Primary treatment process remove
  organic and inorganic solids
  25-50% BOD5
  50-70% SS
  55-65% grease
  Organic nitrogen
  Organic phosphorus
  metals
Secondary treatment process remove
  organic
  Suspended solids
  85% of BOD5 with primary treatment
  If BOD5/COD > 0.6 secondary treatment is required

## Slide 10
Tertiary or advanced treatment remove
  >99% of contaminants
    Organic matter
    SS
    Nutrient (phosphorus and nitrogen)
    Pathogens
    Heavy metals
    Toxic materials
Disinfection remove
  Pathogens (microbes, viruses, and protozoa)
  Can be done chemically by (chlorine, ozone, ultraviolet radiation, chlorine dioxide, and bromine)

## Slide 11
Treatment Level | Process | Indicators | Standard
Primary | Sedimentation | Particle size | <30mg/L
Secondary | Filtration, Biological Chemical | BOD | <30mg/L
 |  | TSS | <30mg/L
 |  | Fecal Coliform bacteria | 100cfu/100 ml. (primary contact)
 |  | Fecal Coliform bacteria | 200cfu/100 ml. (secondary contact)
 |  | E-coli bacteria | 126cfu/100mL
Tertiary | Biological, Chemical | Ammonia | Based on receiving water
 |  | Nitrate | Based on receiving water
 |  | Phosphorus | Based on receiving water
 |  | Pharmaceuticals | Based on receiving water
Wastewater treatment levels

## Slide 12: 3) Reusing WW for Irrigation
Industrial wastewater should be treated to a level that qualify for irrigation purpose.
Re-using Wastewater for Irrigation

## Slide 13
Potential Irrigation Problem | Units | Degree on restriction on use |  |  |  | 
 |  | None | Moderate | Sever |  | 
Salinity |  |  |  |  |  | 
ECw | dS/m | ≤0.7 | 0.7-3 | 3.0 |  | 
TDS | mg/l | 450 | 450-2000 | 2000 |  | 
Permeability (effects of infiltration rate of water into the soil. Evaluate using ECw and SAR together |  |  |  |  |  | 
 | SAR=0-3 | ECw≥0.7 | ECw 0.7-0.2 | ECw≤0.2 |  | 
 | SAR=3-6 | ECw≥1.2 | ECw 1.2-0.3 | ECw≥0.3 |  | 
 | SAR=6-12 | ECw≥1.9 | ECw 1.9-0.5 | ECw≥0.5 |  | 
 | SAR=12-20 | ECw≥2.9 | ECw 2.9-1.3 | ECw≥1.3 |  | 
 | SAR=20-40 | ECw≥5.0 | ECw 5.0-2.9 | ECw≥2.9 |  | 
Specific ion toxicity |  |  |  |  |  | 
Sodium (NA) |  |  |  |  |  | 
Surface irrigation | mg/l | ≤3 | 3-9 | ≥9 |  | 
Sprinkler irrigation | mg/l | ≤70 | >70 |  |  | 
Guidelines for irrigation water quality

## Slide 14
Chloride (Cl) |  |  |  | 
Surface irrigation | mg/l | ≤140 | 140-350 | ≥350
Sprinkler irrigation | mg/l | ≤100 | >100 | 
Boron (B) |  |  |  | 
Surface-sprinkler irrigating | mg/l | ≤0.7 | 0.7-3 | ≥3
Miscellaneous effects |  |  |  | 
Nitrogen | mg/l | ≤5 | 5-30 | ≥30
(Total N) |  |  |  | 
Bicarbonate | mg/l | ≤90 | 90-500 | ≥500
(overhead sprinkling only) |  |  |  | 
Residual chlorine | mg/l | ≤1 | 1-5 | ≥5
(overhead sprinkler only) |  |  |  | 
pH |  | Normal range 6.5-8.4 |  | 
Guidelines for irrigation water quality (Cont.)

## Slide 15: Conclusions:
Untreated wastewater samples from YDF and ESC were collected and analyzed for 21 water quality parameters. Some parameters such as COD, color, TSS etc. were surpassed the standards for disposal of wastewater.
Results revealed that commonly fresh industrial wastewater from YDF and ESC cannot be used for irrigation.
Biological and/or physical-chemical treatment
processes are recommended for the treatment of industrial
wastewater so as to be suitable for irrigation purpose.

## Slide 16: THANK YOU