Civil Engineering Department

College of Engineering

Salahaddin University -Erbil

Subject: Construction Engineering – Course Book

Lecturer's name: Assist.Prof.Dr.Sinan Abdulkhaleq Yaseen

Academic Year: 2020-2021

| 1. Course name | Construction Engineering-I |
| --- | --- |
| 2. Lecturer in charge | Sinan Abdulkhaleq Yaseen |
| 3. Department/ College | Civil/Engineering |
| 4. Contact | Sinan.yaseen@su.edu.krd |
| 5. Time (in hours) per week | 3 hours |
| 6. Office hours | 9:00 am-15:00pm |
| 7. Course code |  |
| 8. Teacher's academic profile | https://academics.su.edu.krd/sinan.yaseen |

To the students of second year stage:

I would like to extend a warm welcome to you all. This subject, “Construction Engineering” will cover an overview to the planning and construction of building in general such as residential structures, including wide information on building phases, elements and some construction material. Two hours of lecture per week and site visit to an under-construction building. Please see additional information that you may need to reference again during the semester.

Outcomes

After completing this subject, the student will be able to:

1.	Describe the nature and scope of the structures construction industry using lecture notes and references.

2.	Understand individual building components and the details necessitates understanding the guiding performance requirements, process of manufacture and assembly, formwork systems and systematic organization of various building assemblies.

3.	Follow of broad range of "good" solutions during construction process.

4.	Identify the opportunities for "invention".

5.	Learn behavior of some structure elements under loads.

6.	Learn mechanical properties of some structural materials.

7.	Learn general safety rules, tools and equipment safety rules.

8.	Write a project report for the construction phases of a project while visiting the site works.

9.	Learn how to work and communicate together with a partner.

10.	Learn how to draw plans on a CAD (Computer-Aided Design) system.

Grade Distribution

Activities, Assignments = 04%

Quizzes = 06 %

Mid-semester Exams = 30 %

Final Exam = 60 %

Total =100% Grades distribution is tentative and subject to change

Forms of teaching

Different forms of teaching will be used to reach the objects of the course. Notes to be written on the board especially drawings, head titles, definitions and summary of conclusions, classification of materials and any other illustration, there will be class room discussions and the lecture will give enough background to be more clear.

Power points presentation will be use when required; besides work sheets will be designed to let the chance for practicing. Students should read the lectures notes regularly and to participate the class room discussions.

General Policies

1.	Students are expected to be present for every class meeting. Any anticipated absences should be cleared with the instructor in advance, when possible, with a typed written memorandum stating the date, reason, and proof for absence or the absence will be considered unexcused.

2.	Students have to come to class on time. If you know that you’ll need to leave before the class is over, try to sit as close to the door as possible so as not to disrupt others. Similarly, if you arrive in class late, just slip in as quietly as possible and take the first available seat.

3.	Full attention in class is required.  Accordingly, activities such as reading newspapers, emails, online chats, and SMS, doing other classes assignments and sleeping is not allowed in class.

4.	When you have a question or comment, please raise your hand first as a courtesy to your classmates and the professor. Remember, your questions are NOT an imposition – they are welcome.

5.	Cell phones must be turned off or on silent mode before the start of class. If a call has to be answered, the student must leave the class without disruption.

6.	No copying of others work in homework or exams unless group work is stated clearly by the instructor in this particular activity.

Exam Policies

•	Anticipated exam time frame is specified below. If any of these dates represent a conflict, please notify the instructor for possible changes of exam dates.

•	Quizzes are usually unannounced.

•	Make-up tests and quizzes will be allowed for only exceptional circumstances and proven medical emergencies.

•	Intermediate exams are not comprehensive. However, the final exam is comprehensive with emphasis on the latest material covered.

Assignment Policies

•	Consultation with other students for solving assignments is acceptable. But each student must report his/her work independently. All identical assignments may receive a score of zero on that assignment.

•	Assignments are due by class time one week from the date they are assigned.

•	Late assignments will receive a point deduction at the rate of 5% per day. No assignment will be accepted after graded assignments are returned except for proven medical emergencies.

•	Most exam problems will be similar to assignment problems. Therefore, solving assignments is a key to being successful on the exams.

Students with Disabilities

• Any student with a disability or other special needs and who needs special accommodations for this course are invited to share these concerns or requests with the instructor as soon as possible.

Introduction

Building construction is a complex, significant, and rewarding process. It begins with an idea and culminates in a structure that may serve its occupants for several decades, even centuries. Buildings are assembled outdoors on all types of sites and are subject to all kinds of weather. Building construction deals with the procedure of constructing buildings and the materials used for the building. The tools and equipment used for each work and the way of implementing the works.

Project Delivery Phases

The process by which a building project is delivered to its owner may be divided into the following five phases, referred to as the project delivery phases. Although there is usually some overlap between adjacent phases, they generally follow the order listed below:

·	Pre-design phase

·	Design phase

·	Pre-construction phase

·	Construction phase

·	Construction phase

·	Post-construction phase

Elements of a building

The following are the basic elements of a building:

1	Foundation

2	Plinth

3	Walls and columns

4	Sills, lintels

5	Doors and windows

6	Floors

7	Roofs

8	Steps, stairs and lifts

9	Finishing work

10	Building services.

The functions of these elements and the main requirement of them will be presented during the lectures of this subject.

Site evaluation

An important part of the pre-design phase of a building is site evaluation. This is a multifaceted evaluation. Some facets impact the construction materials and methods employed for the building significantly, while others play only a minor role.

Excavation

Excavation is the first step of construction. It refers to the process of removing soil or rock from its original location, typically in preparation for constructing foundations, basements, and underground utility lines and for grading of the ground surface.

Machines

Giving details on the using machines in construction

bulldozers, scrapers, graders, tractor shovels, excavating machines, cranes.

Foundation System

Foundation system refers to the structure that lies below the substructure. The selection of a particular type of foundation is often based on a number of factors, such as: adequate depth, bearing capacity failure, quality, adequate strength, adverse soil changes, and seismic forces.

Walls

Walls are built to partition living area into different parts. They impart privacy and protection against temperature, rain and theft. Walls may be classified as:

1	Load bearing walls

2	Partition walls

Bricks

These are walling units within a length of 230 mm, a width of 110 mm and a height of 70 mm. The usual size of bricks in common use is length 215 mm, width 102_5 mm and height 65 mm and like blocks they must be laid in a definite pattern or bond if they are to form a structural wall.

Types of Bonding

English bond, flemish bond, stack bonding.

Stone Masonry

Stone masonry has been favorites of builders and homeowners for hundreds of years. Masonry symbolizes strength, durability, and prestige and at the same time adds warmth, color, and scale to a home. Masonry is most visible in building walls, but is also used in foundations, fireplaces, garden walls, retaining walls, floors, sidewalks, patios, and driveways.

Concrete Blocks

These are used extensively for both load bearing and non-load bearing walls, externally and internally. A concrete block wall can be laid in less time and may cost up to half as much as a similar brick wall. Lightweight aggregate concrete blocks have good insulating properties against transfer of heat and have been much used for the inner leaf of cavity walls with either a brick outer leaf or a concrete block outer leaf.

Arch Construction: by the arrangement of the bricks or stones in an arch over an opening it will be self-supporting once the jointing material has set and gained adequate strength.

Openings: these consist of a head, jambs and sill and the different methods and treatments which can be used in their formation is very wide but they are all based on the same concepts.

Roof (Slabs)

Roof is the upper most portion of the building which protects the building from rain, wind and sun. Various types of roofs used may be divided broadly into three types:

1.	Flat roofs

2.	Pitched roofs

3.	Shells and folded plates. Flat roofs are used in plains where rainfall is less and climate is moderate. Pitched roofs are preferred wherever rainfall is more. Shells and folded plate roofs are used to cover large column free areas required for auditoriums.

Formworks

Concrete when first mixed is a fluid and therefore to form any concrete member the wet concrete must be placed in a suitable mould to retain its shape, size and position as it sets.

Doors

Doors are required to allow access to a building or compartments within a building. External doors must exclude the influence of the external climate – wind, rain, heat and cold – and for that reason many external doors today incorporate a certain level of insulation. Internal doors provide privacy and perhaps security within compartments. They are frequently required to provide resistance to fire.

Windows

A window must be aesthetically acceptable in the context of building design and surrounding environment, Windows should be selected or designed to resist wind loadings, be easy to clean and provide for safety and security. They should be sited to provide visual contact with the outside.

Finishing Works

Plaster: this is a wet mixed material applied to internal walls as a finish to fill in any irregularities in the wall surface and to provide a smooth continuous surface suitable for direct decoration.

Internal Wall Finishes: these can be classified as wet or dry. The traditional wet finish is plaster which is mixed and applied to the wall in layers to achieve a smooth and durable finish suitable for decorative treatments such as paint and wallpaper.

Fixing Wall Tiles: two methods are in general use:

1.	Thin bedding.

2.	Thick Bedding.

Grouting: when the wall tiles have set, the joints can be grouted by rubbing into the joints a grout paste either using a sponge or brush. Most grouting materials are based on cement with inert fillers and are used neat.

Floor Finishes: these are usually applied to a structural base but may form part of the floor structure as in the case of floor boards.

Surface Finishing: the surface of the concrete may be finished by power floating or trowelling which is carried out whilst the concrete is still plastic but with sufficient resistance to the weight of machine and operator whose footprint should not leave a depression of more than 3mm. Power grinding of the surface is an alternative method which is carried out within a few days of the concrete hardening.

Course program: This distribution is tentative and subject to change

| Month | Week No. | Introduction, Ref. Course program |
| --- | --- | --- |
| October | Week 1 Week 2 Week 3 Week 4 | Objectives, General introduction, Types of Constructions Building Construction Phases Site evaluation, Earth works Machines used for site preparation, excavation and backfilling. Quiz 1. H.W.1 Elements of a building Foundation System Types of foundation |
| November | Week 5 Week 6 Week 7 Week 8 | Pile foundation. Action of building under loads Site work Machines and equipment’s; Quiz 1. H.W.2 Walls System, Masonry brick walls Concrete block walls Stone |
| December | Week 9 Week 10 Week 11 Week 12 | walls Openings and arches. Formwork system Types of forms, Foundation formworks, Beam formworks Column formworks, slab formworks Formwork design; Quiz 3. H.W.3 Doors and windows Holiday Types and materials |
| January | Week 13 Week 14 Week 15 | Finishing works Plastering and paintings Wall cladding and tiling Roofing system. Finishing works Plastering and paintings Wall cladding and tiling Roofing system. Roofs (Slabs) Types of slab, One-way slab Two-way slab, Ribbed slabs Flat plate, Flat slab |

| Month | Week No. | Introduction, Ref. Course program |
| --- | --- | --- |
| October | Week 1 Week 2 Week 3 Week 4 | Objectives, General introduction, Types of Constructions Building Construction Phases Site evaluation, Earth works Machines used for site preparation, excavation and backfilling. Quiz 1. H.W.1 Elements of a building Foundation System Types of foundation |
| November | Week 5 Week 6 Week 7 Week 8 | Pile foundation. Action of building under loads Site work Machines and equipment’s; Quiz 1. H.W.2 Walls System, Masonry brick walls Concrete block walls Stone |
| December | Week 9 Week 10 Week 11 Week 12 | walls Openings and arches. Formwork system Types of forms, Foundation formworks, Beam formworks Column formworks, slab formworks Formwork design; Quiz 3. H.W.3 Doors and windows Holiday Types and materials |
| January | Week 13 Week 14 Week 15 | Finishing works Plastering and paintings Wall cladding and tiling Roofing system. Finishing works Plastering and paintings Wall cladding and tiling Roofing system. Roofs (Slabs) Types of slab, One-way slab Two-way slab, Ribbed slabs Flat plate, Flat slab |

References:

1	M. Mehta, W. Scarborough “BUILDING CONSTRUCTION, Principles, Materials, and Systems”, 2009.

2	R. Chudly, R. Greeno ” Building Construction Hand Book”, 2006.

3	R. Barry “The Construction of Buildings “7th edition, 1999.

4	Francis D. K. Ching , “Building Construction Illustrated “ fourth edition 2008.

5	Jonathan T. Ricketts, Frederick S. Merritt “Building Design and Construction Handbook” Sixth edition, 2000.

6	Sidney M. Levy” Construction Building Envelope and Interior Finishes Databook”, 2000.