## Slide 1
Practical Analytical chemistry
1st Stage
Environmental Department
Dr. Hazha Omer Othman
MSc. Suzan Salahaddin Taha

## Slide 2
Preparation and Standardization of Approximate 0.1N Acetic Acid (CH3COOH) by Standardized NaOH

## Slide 3
Acetic acid (CH3COOH) is an ethanoic acid (Ka= 1.8 × 10-5), its weak acid and partially dissociated in an aqueous solution.

## Slide 4
Glacial acetic acid is a pure and water-free acetic acid. It is a colorless liquid that absorbs water from the environment (hygroscopic), freeze at 16.5 ◦C and change to a colorless crystalline solid.
Acetic acid can be detected by its characteristic smell which has a distinctive (clear) pungent (hot) odor.

## Slide 5
is corrosive and therefore must be handled with appropriate care, since it can cause skin burns and permanent eye damage. These burns may not appear until hours after exposure.

## Slide 6
).
The solution at equivalence point not neutral, but slightly alkaline, the calculated pH at equivalence point is 8.72.
In this experiment, (methyl orange) or (methyl red) cannot be used because they change their color at a much lower pH (acidic medium), i.e. the color is changed before the equivalence point. Therefore, phenolphthalein (ph.ph) is used as indicator because its color changes in the alkaline region at a pH range of (8-9.6

## Slide 7
Chemical reaction of acetic acid standardization CH3COOH + NaOH → CH3COONa + H2O
CH3COONa + H2O → CH3COOH + NaOH

## Slide 8
Preparation of solutions:
Prepare 0.1N, 250mL NaOH
Prepare 0.1N, 250mL CH3COOH
Standardization of CH3COOH:
Vaverage= (V1 + V2) / 2
(N × V)NaOH = (N × V)CH3COOH
(0.1 × Vaverage)NaOH = (N × 10)CH3COOH